## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 03
01/29/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Cartoon of the day
[Peter Steiner]

## Slide 3
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 4: Before we get started…
Last time
  About how our code gets executed on the CPU; sequential execution
  Concepts touched on: instruction, assembly code, registers, CISC vs RISC, CPU organization (CU/ALU)
Today
  Registers
  ILP, focus on pipelining
  TLP, and HTT discussion
  Execution times
Other tidbits:
  Additional Reading: check the on-line syllabus
  First assignment went out
    Due on Th 02/04, at 9 pm
    Please register for an Euler account (see details in email of last night)

## Slide 5: Registers

## Slide 6: Revisiting an older slide, to get us going
lw $t0, 12($s2) # reg $t0 gets value stored 12 bytes from address in $s2
add $t0, $s4, $t0 # reg $t0 gets the sum of values stored in reg $s4 and reg $t0
sw $t0, 16($s2) # store what’s in $t0 at mem location 16 bytes from address in $s2
a[4] = delta + a[3]; //line of C code
  MIPS assembly code generated by the compiler (three instructions):
10001110010010000000000000001100
00000010100010000100000000100000
10101110010010000000000000010000
  Set of three corresponding MIPS instructions produced by the compiler:
  Line of C code:
Notes: Typically, a line of code maps into more (some time many) instructions.
Once the instructions are encoded into machine code, they are indistinguishable from data (it’s only location in memory that can differentiate between data and instructions)

## Slide 7: Registers, backdrop (1/2)
Review slide
  Instruction cycle: fetch-decode-execute (FDX)
  CU – responsible for controlling the process that will deliver the request baked into the instruction
  ALU – does the busy work to fulfill the request put forward by the instruction
  The instruction that is being executed needs to be stored somewhere
  Fulfilling the requests baked into an instruction usually involves input values and generates output values
    This data needs to be stored somewhere
Notes: “Stored somewhere”  in registers

## Slide 8: Registers, backdrop (2/2)
Registers, quick facts:
  A register is a hardware asset whose role is that of information storing (information: data value or instruction)
  A register is the storage type with shortest latency – it’s closest to the CU & ALU
    Latency – can be of the order of hundreds of picoseconds
The number and size of registers used are specific to an ISA
  The microarchitecture has to implement support per ISA’s specifications
  Example: Back in the day, for the MIPS ISA, there were 32 registers of 32 bits (no more, no less)
Notes: Typically, an n-bit register might require 4n … 8n transistors
Note: MIPS64 also uses 32 registers
Don’t expect to see too many registers: precious commodities which are located on prime real-estate

## Slide 9: Register Types (1/4)
Discussion herein covers only several register types typically encountered in a CPU (abbreviation in parenthesis)
  List not comprehensive, showing only the more important ones
Instruction Register (IR) – holds the instruction that is executed
  Sometimes known as “current instruction register” CIR
Program Counter (PC) – holds address of the instruction executed next
  NOTE: unlike IR, PC contains *address* of the instruction, not actual instruction
  Sometimes called IAR: Instruction Address Register
Notes: An utility that monitors the program counter can tell you what the hot spots of your executable are
PC is used by profilers to see which instructions are hot-spots

## Slide 10: Register Types (2/4)
Memory Data Register (MDR) – holds data read in from memory or, alternatively, produced by the ALU and waiting to be stored in memory
Memory Address Register (MAR) – holds address of RAM memory location where input/output data is supposed to be read in/written out
  NOTE: unlike MDR, MAR contains *address* of a mem location, not actual data
Return Address (RA) – the address where upon finishing a sequence of instructions, the execution should jump and commence with the execution of subsequent instruction
Notes: Other typical registers:
AC (accumulator): typically resides in the ALU

## Slide 11: Register Types (3/4)
Registers on previous two slides are a staple in most ISA
There are several other registers common to many chip designs
  These are encountered in different numbers (also depending on ISA)
Since they come in larger numbers they don’t have an acronym
  Registers for Subroutine Arguments (4) – a0 through a3
  Registers for Temporary Variables (10) – t0 through t9
  Registers for Saved Temporary Variables (8) – s0 through s7
    Saved between function calls
Notes: Side-note: here’s where the “common wisdom” of having fewer subroutine arguments comes from: there are only 4 registers to store them. When more, additional manipulations.

## Slide 12: Register Types (4/4)
Several other registers are involved in handling function calls
Summarized below, their meaning only apparent in conjunction with the organization of the virtual memory
  Stack Pointer (sp) – a register that holds an address that points to the top of the stack
  Global Pointer (gp) – register that holds on to a global pointer that points into the middle of a 64KB block of memory in the heap that holds constants and global variables (these objects can be quickly accessed with a single load or store instruction)
  Frame Pointer (fp) - a register that holds an address that points to the beginning of the procedure frame (for instance, the previous sp before this function changed its value)
Notes: Virtual memory – at the end of this segment

## Slide 13: Register, Departing Thoughts
Registers: we love them, we can’t have enough of them – they’re that good
If they are so good, why can’t we have more?
  Increasing their number is not straightforward
    Need to change the design of the chip (the microarchitecture)
    Need to change the very nature of an instruction (and as such, ISA gets touched in the process)
Examples:
  In 32-bit MIPS ISA, there are 32 registers
  [Details in two weeks] GP100 GPU (Pascal), register file size: 14,336 MB (~3.5 million registers)
    Seems impressive but it’s actually what you expect: let’s assume each CUDA thread has 32 registers set aside for it
      56 SMs * 2048 threads/SM * 32 registers/thread = 3.6 million registers needed (almost exactly what the hardware made available…)
Notes: We will see why so many registers on a GPU (don’t read too much into it right now)
Pascal: up to 2048 resident threads/SM  they all need registers
There’s a maximum of 255 registers/thread limit

## Slide 14: Quiz type question…
Why is it that adding one more register might lead to ISA changes?

## Slide 15: Registers, take home message
When processing one instruction, the chip needs all instruction-related operands in registers
Fallout, from above statement
  You might have GBs of data to process. To be processed, this data will have to find its way in registers
    We’ll talk about this data journey into registers later
    Reflect on this: all those many GBs of data will have to land at some point in some of the 32 registers at hand

## Slide 16: Pipelining
  “Nothing is particularly hard if you divide it into small jobs.”
  --Henry Ford, founder of Ford Motor Company [1863 –1947]

## Slide 17: Why pipelining was embraced: Too many cooks spoil the broth
[https://t.co/kYI3Mz1iKF]

## Slide 18
Workers on the first moving assembly line put together magnetos and flywheels for 1913 Ford autos. Highland Park, Michigan
http://www.gpschools.org/ci/depts/eng/k5/third/fordpic.htm [public domain]

## Slide 19
Historical change of the manufacturing line. Manual assembly line (left); Hyundai assembly line in Chennai, India (right)
Steve Jurvetson and Mike Bird [Creative Commons Attribution-Share Alike 4.0 International]
https://www.rediff.com/business/report/hyundai-uses-580-robots-in-chennai-plant-maruti-5000/20180530.htm

## Slide 20: Pipelining, or the Assembly Line Concept
Henry Ford: capitalized on, and improved the assembly line idea on an industrial scale and in the process shaped the automotive industry (Ford Model T)
Vehicle assembly line: a good example of a pipelined process
  The output of one stage (station) becomes the input for the downstream stage
  Once assembly line primed, a vehicle gets finished/manufactured during each clock cycle

## Slide 21: Dwelling on the concept of “clock cycle”
Ford plant, and an assembly line therein
  “clock cycle”: the time it takes from the moment a station gets its input to the moment its output leaves the station
The processor
  “clock cycle”: the amount of time between two ticks of the internal clock of the microprocessor (chip)
  Microprocessor clock speed typically measured in Hertz (pulses per second): number of pulses per second
How many pulses these days? What frequency?

## Slide 22: 50 years of microprocessor trends: clock ticks at 4 GHz (give or take)
[https://www.karlrupp.net/2015/06/40-years-of-microprocessor-trend-data/]
Look here
Notes: How the clock ticks: at 4 GHz, it’s been like that for a while…

## Slide 23: FDX cycle: sounds like 3 stages, seems to have 4, ends up being 5 or more
FDX cycle: Fetch, Decode, Execute - carried out for each machine instruction, sounds like 3 stages
  Sometimes called FDXW (W: “Write”) – so it’s more like four stages
Upon a closer look at what gets fetched (instructions and data) and then what happens upon execution leads to a generic five-stage process associated with an instruction
“generic” above means that, in a first order approximation, these five stages can represent any instruction, although some instructions might not have all five stages:
  Stage 1: Fetch an instruction
  Stage 2: Decode the instruction
  Stage 3: Data access
  Stage 4: Execute the operation (e.g., might be a request to calculate an address)
  Stage 5: Write-back into register file
NOTE: “FDX cycle” is a name, doesn’t have to do with “cycle time”, which is the time between two clock ticks
  Think about it like this: the “FDX cycle” is done for each instruction, and for each instruction it takes several clock cycles (ticks of the clock)
[Patterson, 4th edition]→
Notes: Modern CPU pipelines are 14-19 deep

## Slide 24: Haswell Microarchitecture: help to contextualize the FDX cycle [30,000 Feet]
Microarchitecture components:
  Instruction pre-fetch support (purple)
  Instruction decoding support (orange)
    CISC into uops
      Can be regarded as CISC to RISC step
  Instruction Scheduling support (yellowish)
  Instruction execution
    Arithmetic (blueish)
    Memory related (green)
[http://www.realworldtech.com]
Notes: LEA: Load effective address
The address generation unit (AGU), sometimes also called address computation unit (ACU), is an execution unit inside central processing units (CPUs) that calculates addresses used by the CPU to access main memory.

## Slide 25
Rules of thumb: costs to eXecute an operation > 1 clock cycle [refers to older MIPS ISA; cost of X in FDX]
Four clock cycles for SW
Five clock cycles for LW
Four clock cycles for add
Etc.
25
Notes: The numbers for the X86 family of chips is usually different

## Slide 26: Pipelining, the basics
Assume a five-stage pipeline (btw, it gets to be somewhere between 10-20 stages deep)
Pipelining, cornerstone idea: the following tasks can be worked upon simultaneously when processing five instructions:
  Instruction 1 is in the 5th stage of the FDX cycle
  Instruction 2 is in the 4th stage of the FDX cycle
  Instruction 3 is in the 3rd stage of the FDX cycle
  Instruction 4 is in the 2nd stage of the FDX cycle
  Instruction 5 is in the 1st stage of the FDX cycle
Notes: Balance issue:
For the simple 5-stage RISC pipeline discussed here, this is mostly true:
  register read/write ~100 ns
  fetch/ALU/data read ~200 ns
Modern processor: deep pipelines, because instructions are further broken down to be comparable in time

## Slide 27: Example: Streaming for execution 3 SW instructions
sw $t0, 0($s2) //store what is in register $t0 at mem location 0 bytes from address in register $s2
sw $t1, 32($s2) //store what is in register $t1 at mem location 32 bytes from address in register $s2
sw $t2, 64($s2) //store what is in register $t0 at mem location 64 bytes from address in register $s2
Case 1: No pipelining – 2100 picoseconds [ps]
Notes: sw: in MIPS means ‘store word’
ALU used to add offset
sw: no data access needed (missing stage 3)
sw $t0, 32($s2) # store what’s in $t0 at mem location bytes from address in $s2

## Slide 28: Example: Streaming for execution 3 SW instructions
sw $t0, 0($s2)
sw $t1, 32($s2)
sw $t2, 64($s2)
Case 2: With pipelining – 1200 picoseconds [ps] (5 GHz clock cycle)
Notes: Pipelining in use since the 1990s

## Slide 29: Pipelining: on its “balanced” attribute
An ideal situation is when each of pipeline stage takes the same amount of time for completion
  The pipeline is then balanced
If pipeline not balanced, there will be stations that wait for the laggard station at every single cycle
Common sense: If there is a station that takes a significantly longer time since it does significantly more than other stations, it should be broken into two and the length of the pipeline increases by one station
  Leads to deeper pipelines
  Typical pipeline depth today: 12-15 stages

## Slide 30: Pipelining Benefits: speed up & no code rewrite
Benefit 1: faster execution, owing to simultaneously working on multiple instructions
  Assume that you have
    A very large number of instructions
    Balanced stages
    A pipeline that is larger than or equal to the number “” of stages associated with the typical ISA instruction
  If 1 through 3 above hold, in a first order approximation, speed-up you get out of pipelining is approximately “”
Benefit 2: no effort required on the user’s part, no code rewrite needed to reap benefits
  This kind of parallel processing of stages is transparent to the user
  Unlike GPU or multicore parallel computing, you don’t have to do anything to benefit from it
Notes: Ideally: at each cycle you complete one instruction
This ignores the need to “prime” the pipeline and to pipeline shutdown.
This ignores hazards (see next)
NOTE: this is not parallel programing, but rather parallel execution (it’s out of the programmer’s hands)

## Slide 31: Pipelining, Good to Remember
The amount of time required to complete one stage of the pipeline: one clock cycle
Pipelined processor: one instruction finished in each clock cycle
Non-pipelined processor: no overlap when executing instructions
Important Remark:
  Pipelining does not decrease the time to complete one instruction but rather it increases the throughput of the processor by overlapping different stages of processing of different instructions
Notes: NOTE: an individual instruction may take longer to complete (because some stages are delayed to fit the common tick)
The issue here is so-called INSTRUCTION HETEROGENEITY
Ford solved this problem by limiting the number of options:
“Any customer can have a car painted any color that he wants so long as it is black.”
But the benefit is THROUGHPUT

## Slide 32: Pipelining Hazards
Q: if deep pipelines are good, why not make them deeper?
A: deep pipelines plagued by pipelining hazards
  Structural hazards
  Data hazards
  Control hazards
[Patterson, 4th edition]→

## Slide 33: Pipeline Structural Hazards: The problem at hand
A real world assembly line assembles the same product for a period of time
Typically, it can be quickly reconfigured to assemble a different product
The chip processes a broad spectrum of instructions that come one after another
  Example: A J-type instruction coming after a R-type instruction, which comes after three I-Type instructions
  If they were the same instructions (vehicles), designing a pipeline (assembly line) is straightforward
A structural hazard: the possibility of having a combination of instructions in the pipeline contending for the same hardware asset
  Not encountered when you assembly the same car model (things are “deterministic” in this case)
[Alden Jewell: https://www.flickr.com/photos/autohistorian/32637661426]
21,529,464 VW Beetle vehicles produced (1938 until 2003)
Notes: CONTENTION for hardware

## Slide 34
This can lead to a structural hazard – one will want to use to nail nails; somebody else might contend it for removing nails in a different job (“instruction”)
Claw Hammer

## Slide 35: Pipeline Structural Hazards: Fixing the problem
Example, how things can go south
  15-stage pipeline: instruction in stage 5 and instruction in stage 9 both need to use the same special register to store a temp variable
  Solution 1: perhaps a register can be commandeered somehow, for temporary use
  Solution 2: serialize the access, basically introduce a bubble in the pipeline so that there is no contention
    “bubble in the pipeline” – think of it as a skipped issue slot (the scheduler doesn’t issue anything)
  Solution 3: Out of order execution (OOOE) done statically (at compile time) or perhaps dynamically (at run time)

## Slide 36: Pipeline Structural Hazards: Fixing the problem - comments
Comment, Solution 1:
  Fortuitous, a matter of serendipity
  Increase number of registers?
    Brute force solution; expensive and consequential (requires a chip design change, perhaps even ISA)
    Note that “needing one extra register” is just one possible scenarios; there are might be other contention scenarios lurking
Comment, Solution 2:
  Introducing bubbles into the pipeline at run time slows down the execution
Comment, Solution 3 (OOOE):
  This is a good compromise: it’s general and when you can re-order instructions there is no slowdown

## Slide 37: Pipeline Data Hazards (1/2) [very common]
Example, to get the discussion going – Consider assembly below, with a five-stage pipeline chip:
add $t0, $t2, $t4 // $t0 = $t2 + $t4
addi $t3, $t0, 16 // $t3 = $t0 + 16 “add immediate instruction”
The first instruction is eXecuted in five clock cycles
Its output (value stored in register $t0) is needed in the very next instruction
Data hazard: unavailability of $t0 to the second instruction, which references this register
Resolution (less than ideal)
  Put bubbles in the pipeline to wait for the first instruction to fully complete
Notes: Data DEPENDENCIES
2nd stage of instruction 2 depends on data available only after 5th stage of instruction 1
Sub-optimal solution: introduce “bubbles” in the pipeline

## Slide 38: Pipeline Data Hazards (2/2)
add $t0, $t2, $t4 # $t0 = $t2 + $t4
addi $t3, $t0, 16 # $t3 = $t0 + 16 (“add immediate”)
Alternative [the good] Resolution: use “forwarding” or “bypassing”
Key observation: the value that will eventually be placed in $t0 is available after stage 3 of the pipeline (where the ALU actually computes this value)
    Analogy: we finished eating well before the dinner table is clean, the plates are in the dishwasher, and the floor is swept
Provide the means for that value in the ALU to be made available to other stages of the pipeline right away
  Avoids bubbling - don’t have to wait several cycles before the value made its way into $t0
  This process is called “intermediate result forwarding”
Supporting forwarding does not guarantee resolution of all scenarios
  Occasionally the pipeline ends up with bubbles for a couple of cycles
OOOE helps (insert unrelated instruction, wedged between two instructions that depend on each other)
Notes: Analogy: we finished eating well before the dinner table is clean, the plates are in the dishwasher, and the floor is swept

## Slide 39: Pipeline Control Hazards (1/2)
What happens when there is an “if” statement in a piece of C code?
  Example: if (sin(x)/x>0.5) …
A corresponding machine instruction decides the program flow
  Specifically, should the “if” branch be taken or not?
Processing this very instruction to figure out next instruction (branch or no-branch) will take a number of cycles
Should we bubble the pipeline while this instruction is fully processed and branching decision becomes clear?
  If yes: strategy always works, but slows down execution
  If no: rely on branch prediction and proceed fast but cautiously
Notes: BRANCHING
What is the instruction that should be inserted in the pipeline right after the one that actually decides the branch?

## Slide 40: Pipeline Control Hazards (2/2): Branch Prediction
Static Branch Prediction (1st strategy out of two):
  Always predict that the branch will not be taken and schedule accordingly
    That is, always schedule the “then” branch, never the “else” branch
  There are other heuristics for proceeding: for instance, for a do-while construct it makes sense to always be jumping back at the beginning of the loop
    Similar heuristics can be produced in other scenarios (a “for” loop, for instance)
Dynamic Branch Prediction (2nd strategy out of two):
  At a branching point, the branch/no-branch decision can change during the life of a program based on recent history
  In some cases branch prediction accuracy hits 90%
Note: when your prediction is wrong you have to discard the [micro]instruction[s] executed speculatively and take the correct execution path
Notes: Dynamic branch prediction: requires more hardware to implement the logic (keep track of previous paths)

## Slide 41: [New topic]Pipelining vs. Multiple-Issue (1/2)
Multiple-issue: what is that?
  In sequential computing, a multiple-issue processor core has the hardware chops to issue more than one instruction per cycle
Pipelining different than “Multiple-Issue,” which is another way of speeding up execution
Example: the C code below leads to a set of instructions that can be launched for execution at the same time
  IMPORTANT: No cross-dependency in updating a and c
int a, b;
float c, d;
//some code setting up a, b, c, d
a += b;
c += d;
Notes: Depart from the “assembly line” analogy. Here, think of a car manufacturing plant where more car models are produced simultaneously, by sharing common available resources (stations).
It’s actually good here to have very different “car models”: it’s less likely to have competition for same resources (stations).

## Slide 42: Pipelining vs. Multiple-Issue (2/2)
On average, more than one instruction is processed by the same core in the same clock cycle
Multiple-Issue can be done statically or dynamically
  Static multiple-issue:
    Predefined, doesn’t change at run time
    Who uses it: Intel, in AVX512 (but not only)
  Dynamic multiple-issue:
    Determined at run time, the chip has dedicated hardware resources that can identify and execute additional work
    Who uses it: Intel, AMD, IBM, NVIDIA, etc.
Notes: Dynamic multiple-issue makes use of a buffer for instructions to be able to look ahead.
We already alluded to other ILP techniques:
out of order execution
speculative execution and branch prediction
also, register renaming, etc.

## Slide 43: Pipelining vs. Multiple Issue
[Modern Operating System, Tanenbaum-Bos]→
(a) Three-stage pipeline
(b) Multiple issue processor

## Slide 44: Attributes of Dynamic Multiple-Issue
The data dependencies between instruction being processed takes place at run time
Checking for dependencies is complex, requires high cost in time and energy
Checks in place to make sure result is ok
  “ok”: no difference if the instructions are executed “multiple-issue” or “single issue”
NOTE: a chip that can do multiple-issue is also called a superscalar architecture
Notes: CU acts as supervisor to see what instructions can be issued and dispatched simultaneously

## Slide 45: The “Instruction-Level Parallelism” (ILP) concept
Pipelining, OOOE, and multiple-issue are presentations of what’s called Instruction-Level Parallelism (ILP)
ILP pursues various strategies to execute simultaneously multiple instructions
Important: these instructions belong to the same program or process; i.e., belong to *one* thread
  “process” – how the operating systems calls your program
Notes: Dynamic multiple-issue makes use of a buffer for instructions to be able to look ahead.
We already alluded to other ILP techniques:
out of order execution
speculative execution and branch prediction
also, register renaming, etc.

## Slide 46: ILP: various angles of attack (quick summary of ILP’s bag of tricks)
Instruction pipelining: execution of multiple instructions can be partially overlapped; each instructions divided into sub-steps (termed: micro-operations)
Superscalar execution: multiple execution units are used to execute multiple instructions in parallel
Out-of-order execution: instructions execute in any order but without violating data dependencies
Register renaming: a technique used to avoid data hazards and thus lead to unnecessary serialization of program instructions caused by the reuse of registers
Speculative execution: allows the execution of complete instructions or parts of instructions before being sure whether this execution is required
Branch prediction: used to avoid delays (termed: stalls in execution). Used in combination with speculative execution.
Notes: Various techniques. Most rely on available extra capacity (hardware/transistors).
For ILP to make a dent, you need large blocks of instructions that can be [attempted to be] run in parallel
Duplicate hardware speculatively executes future instructions before the results of current instructions are known, while providing hardware safeguards to prevent the errors that might be caused by out of order execution
Branches must be “guessed” to decide what instructions to execute simultaneously
  If you guessed wrong, you throw away that part of the result
Data dependencies may prevent successive instructions from executing in parallel, even if there are no branches

## Slide 47: Thread Level Parallelism (TLP) [happens on a single core]
ILP not the only “parallel” show in town
Another one: chip executes simultaneously instructions from different processes or different threads
  Called Thread-Level Parallelism (TLP)
Important to keep in mind: we are talking about parallelism on one hardware core, not multicore

## Slide 48: ILP vs. TLP: how are they different
Recall concept of “Program Counter” (PC): a register that holds address of next instruction
If all instructions executed by the chip in parallel are associated with one PC, we have ILP
TLP: the stream of instructions simultaneously processed by the chip associated with more than one PC

## Slide 49: Process vs. thread – getting a bit into the weeds [1/2]
TLP: chip executes simultaneously instructions from different processes or different threads
There is a subtle difference between processes & threads:
  TLP is what happens when two processes such as Matlab and Microsoft Word run on the chip
    Because two different processes, there are two different PCs
  TLP: two (or even more) OpenMP or POSIX threads simultaneously run on the chip
    Because two different threads, there are two different PCs

## Slide 50: Process vs. thread – getting a bit into the weeds [2/2]
How similar: Both processes and threads are independent sequences of execution
How different:
  Threads (of the same process) run in a shared memory space
    This is how shared-memory parallel computing takes place. Like OpenMP
  Processes run in separate memory spaces
    This is how distributed-memory parallel computing takes place. Like MPI*
What is a memory space?
  To be continued, in one week (after discussing the concept of Virtual Memory)

## Slide 51: Why did folks come up with this TLP idea?
Over time, transistor budget ballooned
  Owing to Moore’s Law
As such, many Functional Units available
TLP allows us to put them to good use

## Slide 52: An example of TLP: Intel’s HTT feature
Typical Intel core supports the “Hyper-Threading Technology” (HTT)
HTT: two threads/processes, each seeing its own stream of machine instructions, active at any given time
  “active”: also called “in flight”
The scheduler tries to issue instructions from both processes, at the same time
The beefing up of the CU/ALU hardware required to support HTT is actually pretty minor
  Extra hardware required to save execution state of a thread when idle and not running (for lack of data or available functional units)
[Intel]
Notes: Intel HT Technology improves performance through increased instruction level parallelism by having two threads with independent instruction streams, eliminating data dependencies between threads and increasing utilization of the available execution units. This effect typically increases the number of instructions executed in a given amount of time within a core, as shown in Figure 3. The impact of this greater efficiency is experienced by users as higher throughput (since more work gets completed per clock cycle) and higher performance per watt (since fewer idle execution units consume power without contributing to performance). In addition, when one thread has a cache miss, branch mispredict, or any other pipeline stall, the other thread continues processing instructions at nearly the same rate as a single thread running on the core. Intel HT Technology augments other advanced architectural features, higher clock speeds, and additional cores with a capability that is relatively inexpensive in terms of space on the silicon and production cost.

## Slide 53: Intel’s HTT Feature
In general, TLP requires the participation of the Operating System (OS)
  The OS sees one physical chip as two virtual chips; OS “talks” to both of them
Is HTT helpful?
  Yes: when running two modestly demanding processes
    Example: Running MS-Word and Spotify at the same time
      Execution threads are independent, when one execution thread stalls the other can be picked up and its PC advanced
  No: high performance computing, when one stream of instruction saturates the memory bandwidth
    Nothing left for anybody else to step in and nibble on excess-hardware leftover
NOTE: as of recently, the trend has been for TLP to be scaled back owing to security issues
Notes: Intel HT Technology improves performance through increased instruction level parallelism by having two threads with independent instruction streams, eliminating data dependencies between threads and increasing utilization of the available execution units. This effect typically increases the number of instructions executed in a given amount of time within a core, as shown in Figure 3. The impact of this greater efficiency is experienced by users as higher throughput (since more work gets completed per clock cycle) and higher performance per watt (since fewer idle execution units consume power without contributing to performance). In addition, when one thread has a cache miss, branch mispredict, or any other pipeline stall, the other thread continues processing instructions at nearly the same rate as a single thread running on the core. Intel HT Technology augments other advanced architectural features, higher clock speeds, and additional cores with a capability that is relatively inexpensive in terms of space on the silicon and production cost.

## Slide 54: HTT, Intel’s perspective
Highlights:
  The processor core maintains two architectural states, each of which can support its own execution thread
  Many of the internal microarchitectural hardware resources are shared between the two threads
[Intel]
Notes: DAN - Lots of good stuff here: https://software.intel.com/en-us/articles/performance-insights-to-intel-hyper-threading-technology (article by Antonio Valles (Intel))

## Slide 55: HTT: The Bottom Line
Essentially, one physical core shows up as two virtual cores
Why is it good?
  More execution units within the ALU are used at any given time
    Higher utilization rate of the hardware assets
  When one execution thread stalls (has a cache miss, branch mispredict, pipeline bubble, etc.), the other execution thread continues processing instructions at nearly the same rate as a single thread running on the core
[Intel]
Functional Unit A
Functional Unit B
Functional Unit C
Functional Unit D
Functional Unit A
Functional Unit B
Functional Unit C
Functional Unit D
Notes: DAN - Lots of good stuff here: https://software.intel.com/en-us/articles/performance-insights-to-intel-hyper-threading-technology

## Slide 56: TLP: further discussion
Multi-threading, a possible taxonomy (Hennessey & Paterson)
  Coarse grain multi-threading
  Fine grain multi-threading
  Simultaneous multi-threading
This taxonomy: It all goes back to what goes through this pipe at each clock cycle
The “brain”
The “executioner”

## Slide 57: Coarse multi-threading
The Instruction Control issues instructions from one thread for many cycles
  Bursts of tens or hundreds of instructions
Instruction Control switches to issuing from another thread only when the first thread runs into a long-latency operation
  Examples: cache miss, interrupt, etc.
  “long-latency”: Hundreds of cycles or so
!!!!!

## Slide 58: Fine multi-threading
Instruction Control can issue instructions from a different thread each cycle
  “Barrel-gun style” processing: thread from where next instruction is picked for execution can change at every cycle
  GPU computing similar to this
More nimble/sophisticated compared to coarse multi-threading
!!!!!

## Slide 59: Simultaneous multi-threading
Simultaneous multi-threading is like fine multi-threading with one caveat:
  Instruction Control can issue instructions from different threads in the same cycle
NOTE:
  Intel’s HTT is a “simultaneous multi-threading” technology
!!!!!

## Slide 60: Superscalar processor or TLP processor. Wrapping it up
Superscalar vs. TLP
  Superscalar: instructions associated with one PC
  TLP: instructions associated with two PCs
Superscalar: one PC on the chip
  HW has the means to execute more than one instruction per cycle
  Superscalar: it’s more than a “scalar”; i.e., one thread
TLP: Processor handles instructions from different threads/processes
NOTE: we are not talking about multiple-cores; we are still talking about one CPU core here

## Slide 61: Quiz: TLP flavors
Left-side pic: coarse TLP, fine TLP, or SMT?
  Not clear from the pic if it’s TLP coarse, TLP fine, or even non TLP (might be the operating system engaging in time slicing)
  To understand if it’s TLP or not one needs to know whether the processor is capable of maintaining more than one architectural state in flight
Right-side pic: coarse TLP, fine TLP, or SMT?
Functional Unit A
Functional Unit B
Functional Unit C
Functional Unit D
Functional Unit A
Functional Unit B
Functional Unit C
Functional Unit D