## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 04
02/01/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Cartoon of the day
[Mick Stevens]

## Slide 3: Quote of the day
“Success is the ability to go from failure to failure without loss of enthusiasm.” (Anonymous, but attributed to Lincoln, Churchill, etc. See here for more details.)

## Slide 4
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 5: Before we get started…
Last time
  Registers
  ILP (focus on pipelining)
  TLP, and HTT discussion
Today
  Execution times
  Memory related issues
  The memory hierarchy
  Caches
  NOTE: we’ll draw on a couple of C programs; please read ME459 C material if the programs look alien
Other tidbits:
  Assignment due on Th 02/04, at 9 pm
  Please be mindful of how to use Euler (see doc that emailed on Sat night)
  Please register for an Euler account (details provided in email of Th night)

## Slide 6: Measuring Speed of Execution

## Slide 7: Backdrop: CPU/OS juggle many programs at the same time
The hardware-software interplay:
CPU is hardware
The operating system (OS) is software

## Slide 8: Nomenclature (1/3)
Wall Clock Time
  Amount of time from the beginning of a program to the end of the program
  Includes; i.e., factors in, all the housekeeping (running other programs, OS tasks, etc.) that CPU does while running our program
  Perhaps most meaningful indicator of performance since this is what you see
CPU Execution Time
  Counts only the amount of time that is effectively dedicated to *your* program
  Many other programs running on your machine at the same time (time slicing)
  Requires a profiling tool to assess (like gprof, for instance)
On a dedicated machine; i.e., a quiet machine, Wall Clock Time and CPU Execution Time should be identical
[Patterson, 4th edition]→
Notes: In general: Program Execution Time is what you care about (end-to-end time to solution)

## Slide 9: Nomenclature (2/3)
Qualifying CPU Execution Time further:
  User time – the time spent processing instructions compiled out of code generated by the user or in libraries that are directly called by user code
  System time – time spent in support of the user’s program but in instructions that were not generated out of code written by the user
    OS support: open file for writing/reading, throw an exception, etc.
  The line between the user time and system time is somewhat blurred, sometimes hard to delineate and differentiate
  “system vs. user”: We bother to delineate since we can only cut into the “user time”; you can’t rewrite system code

## Slide 10: Nomenclature (3/3)
Clock cycle, cycle, tick – the length of the period for the processor clock
Clock cycle: sets the pace at which the execution proceeds
  In a pipeline process, in a perfect scenario, each clock cycle sees the completion of one instruction
  A constant value dictated by the frequency at which processor operates
  Examples:
    A 1 GHz processor has clock cycle of 1 nanosecond
    A 2 GHz processor has clock cycle of 0.5 nanoseconds (500 picoseconds)
    This machine I’m using right now: 3.8 GHz (AMD Ryzen 3900) – about 250 picosecond clock cycle

## Slide 11: The CPU Performance Equation
[Patterson, 4th edition]→
Three ingredients control the amount of time for execution of a program:
  Number of instructions that your program has (Instruction Count)
  Average number of “clock-cycles per instructions” (CPI)
  Clock Cycle Time
The CPU Performance Equation reads:
Alternatively, using the clock rate

## Slide 12: CPU Performance: How can we improve it?
To improve performance the product of three factors should be reduced
For a long time, we’ve piggy backed on “let’s increase the frequency”; i.e., reduce Clock Cycle Time
  We eventually hit a wall this way (the “Power Wall”)
As repeatedly demonstrated in practice, reducing the Instruction Count (IC) often times leads to an increase in CPI. And the other way around.
Notes: Power Wall relationship: power dissipation is proportional to frequency
RISC: large IC, small CPI
CISC: small IC, large CPI
Tweaking CPI – the goal of ILP (but that seems to have exhausted its capabilities: “ILP wall”)
Parallel computing: do more of this in parallel

## Slide 13: Side Trip: Revisiting, RISC or CISC?
Ongoing argument – whether RISC or CISC is the better ISA
The former is simple and therefore can be optimized easily. Yet it requires a large number of instructions to accomplish something in your C code
  High IC but low CPI
The latter is complex, but instructions are expressive. Leads to few but expensive instructions to accomplish something in your C code
  Low IC but high CPI
Specific example: ARM vs. x86

## Slide 14: SPEC CPU Benchmarks
Benchmarks help us understand what processor does well what
Idea: gather a collection of programs that use a good mix of instructions and flex the muscles of a chip
The “collection of programs”:
  Should be non-trivial and widely used
  Should be as objective as possible: not favor a chip manufacturer at the expense of another one
  Example: a compiler is used extensively, so it makes sense to have it included in the benchmark
Two common benchmarks:
  Tied to programs dominated by floating point operations: CFP2006
  Tied to programs dominated by integer arithmetic: CINT2006
Notes: SPEC: Standard Performance Evaluation Corporation (non-profit)
Different processors are better at different things.

## Slide 15: SPEC CPU Benchmark: Example, highlights AMD performance
CINT2006 Programs |  | AMD Opteron X4 – 2356 (Barcelona) |  |  | 
Description | Name | Instruction count [×109] | CPI | Clock Cycle Time [seconds ×10-9] | CPU Exec. Time [seconds]
Interpreted string processing | perl | 2118 | 0.75 | 0.4 | 637
Block-sorting compression | bzip2 | 2389 | 0.85 | 0.4 | 817
GNU C compiler | gcc | 1050 | 1.72 | 0.4 | 724
Combinational optimization | mcf | 336 | 10.00 | 0.4 | 1,345
Go game (AI) | go | 1658 | 1.09 | 0.4 | 721
Search gene sequence | hmmer | 2783 | 0.80 | 0.4 | 890
Chess game (AI) | sjeng | 2176 | 0.96 | 0.4 | 837
Quantum computer simulation | libquantum | 1623 | 1.61 | 0.4 | 1,047
Video compression | h264avc | 3102 | 0.80 | 0.4 | 993
Discrete event simulation library | omnitpp | 587 | 2.94 | 0.4 | 690
Games/path finding | aster | 1082 | 1.79 | 0.4 | 773
XML parsing | xatancbmk | 1058 | 2.70 | 0.4 | 1,143
[Patterson, 4th edition]→

## Slide 16: SPEC CPU Benchmark: Example, wrap up
  There are programs for which the CPI is less than 1.
    Suggests that multiple issue is at play
  Why are there programs with CPI of 10?
    The pipeline stalls a lot, most likely due to repeated cache misses and system memory transactions
[Patterson, 4th edition]→
Notes: Program with CPI=10 : combinatorics, likely many memory accesses “all over the place”. This segues in the next segment, where we will discuss memory-related issues.

## Slide 17: Important, common sense observation
You get the brownie points for writing code whose instructions fly through the chip
Nobody particularly impressed by instructions that take a long time to execute

## Slide 18: Big New Topic: Memory Aspects

## Slide 19: Transistors: why we love them & want as many as possible[old slide]
Focus first on how transistors are used to perform tasks (tied to CU and ALU use)
Later talk about how transistors are used to store data and instructions
Memory Data
Control Unit (CU)
Arithmetic Logic Unit (ALU)
data flow
instructions flow
internal consumption data
internal consumption (uops?)
Instructions
Data
Memory
Processor
(Chip)

## Slide 20: SRAM: significant consumer of transistors
SRAM – Static Random Access Memory
  Integrated circuit whose elements combine to make up memory arrays
  An “element”: a special circuit, called flip-flop
  One flip-flop requires four to six transistors
  Each of these elements stores one bit of information
  Very short access time: ns (order of magnitude(0): )
  Uniform access time of any element in the array (yet it’s different to write than to read)
  “Static” refers to the fact that once set, the element stores the value set as long as the element is powered
  Bulky, since a storing element is “fat”; problematic to store a lot per unit area (compared to DRAM)
  Expensive, since it requires four to six transistors and special layout and support requirements
[Patterson & H]→
Notes: SRAM is an integrated circuit whose elements combine to make up memory arrays.
In figure: the memory chip can store 4 million 32 bit data.
For 4 million addresses: 2^22, you need address lines.
Data in/out: 8 + 8
Additionally, need 3 control lines (Chip select, Write enable, Output enable)

## Slide 21: SRAM: It’s Expensive
Eats up relatively big chunk of the transistor budget
Back of the envelop calculation:
  Decent CPU processor: 4 billion transistors
  Assume 32 MB of L3 cache
    1 B = 8 bits
  Assume 4 transistors per bit
    Budget of transistors:
      25% of all transistors used for L3 cache :-(

## Slide 22: DRAM
DRAM type memory: the information stored as a charge in a capacitor
  No charge: 0 signal
  Some charge: 1 signal
The good: cheap, requires only one capacitor and one transistor
The bad: capacitors leak, so the charge or lack of charge should be reinforced every so often, dynamically
  D in DRAM comes for the “dynamically” attribute
Moral of the story: State of the capacitor should be refreshed every millisecond or so
  Refreshing requires a small delay in memory accesses
    Is this delay incurred often? (first order approximation answer)
      Given frequency at which memory is accessed, refreshing every millisecond means issues might appear once every million cycles
      Moral of the story: refresh is a rare event (in the life of the execution cycle)
[Patterson & H]→

## Slide 23: SRAM vs. DRAM: wrap-up
SRAM access time: of the order of nanoseconds or tens of nanoseconds
  Expensive but fast
  Transistor hog
  Needs no refresh
DRAM access time: of the order of hundreds of nanoseconds
  Less expensive but slow
  Higher capacity per unit area
  Needs refresh every 10-100 ms
  Sensitive to disturbances
Limit case: a 100X speedup if you can work off the SRAM
[Rauber&Runger]→
 | Transistors per bit | Access Time | Persistent? | Sensitive? | Price | Applications
SRAM | 6 | 1X | Yes | No | 100X | Cache memories
DRAM | 1 | 100X | No | Yes | 1X | Main Memory
Notes: [Rauber&Runger]→ Typical access times are 0.5–2.5 ns (ns = nanoseconds = 10−9 seconds) compared to 50–70 ns for DRAM (values from 2008 [84])
From Rochester (http://www.cs.rochester.edu/~sandhya/csc252/lectures/lecture-storage.pdf):
Key features
– RAM is packaged as a chip.
– Basic storage unit is a cell (one bit per cell).
– Multiple RAM chips form a memory.
• Static RAM (SRAM)
– Each cell stores bit with a six-transistor circuit.
– Retains value indefinitely, as long as it is kept powered.
– Relatively insensitive to disturbances such as electrical noise.
– Faster and more expensive than DRAM.
• Dynamic RAM (DRAM)
– Each cell stores bit with a capacitor and transistor.
– Value must be refreshed every 10-100 ms.
– Sensitive to disturbances.
– Slower and cheaper than SRAM.

## Slide 24: Feature Comparison Between Memory Types
 | SRAM | DRAM | Flash
Speed | Very fast | Fast | Very slow
Density | Low | High | Very high
Power | Low | High | Very low
Refresh | No | Yes | No
Retention | Volatile | Volatile | Non-volatile
Mechanism | Bi-stable Latch | Capacitor | Fowler-Nordheim tunneling
Notes: Flash memory: Toshiba (1980)
Uses “floating-gate transistors”

## Slide 25: New Topic: The Memory Hierarchy
Common Sense Observations
  Observation 1: over time, speed of data processing increased faster than speed at which we could bring over data to be processed
  Observation 2: the bigger the memory used to store data, the longer it takes to find/access an entry therein
    Compromise between size and speed of access

## Slide 26: Backdrop: Widening of the Processor-DRAM Speed Gap
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fourth edition
Notes: QUESTION: we talk about memory wall as an impediment to continuing increase in sequential computing performance and we said that the problem is that memory cannot keep up feeding the raw number crunching capability of the CPU.
But then, how can parallel computing be the answer? How could memory serve now multiple “consumers” and yet overall performance increase?
To explain this, we note that memory performance is related to two key concepts:
latency
bandwidth

## Slide 27: Consequences of common sense observations
Consequences of Observations 1 & 2: a hierarchy of memories has emerged
  It took some time to shape up, happened through a continuous improvement process
  Managing the hierarchy not trivial → a dedicated hardware asset called MMU (memory management unit) handling this task
    MMU’s purview: cache control, virtual memory management, memory protection, bus arbitration, etc.

## Slide 28: The memory hierarchy, how it shapes up
Since SRAM is expensive and bulkier, can’t have too much
  Plagued by space & cost constraints
Compromise:
  Have some SRAM on-chip, making up what is called the “cache”
  Have a lot of inexpensive DRAM off-chip, making up the “main memory”
    This is what people have in mind when they ask you “How much memory does your system have”?
In our code, we hope to have low “average memory access time” by hitting the cache repeatedly instead of taking costly trips to main memory
Notes: A single issue pipelined processor that operates at 2 GHz could in theory execute one instruction every 0.5 nanoseconds. SRAM has access times in that range; DRAM memory has access times about 50 times slower. In an ideal world, one would have all data available in SRAM so that the processor can work at capacity. Since SRAM is expensive and bulky only a small amount is available in the processor to store both data and instructions. This small amount of memory is called cache memory.

## Slide 29: There’s even a cache hierarchy…
Simplest memory hierarchy:
  Main Memory + One Cache (typically called L1 cache)
Today’s memory architectures typically have deeper hierarchy: L1+L2+L3
  L1 faster and smaller than L2
  L2 faster and smaller than L3
All caches are typically on the chip and are SRAM
Notes: L1 also uses “better components” than L2

## Slide 30: Typical Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g. file servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 31: Memory Hierarchy
Moving on to talk about caches
The collection of all registers is called “the register file”

## Slide 32: Cache Memories
Cache memories are small, fast, on-chip SRAM-based memories
  Purpose: to store close to the CU/ALU frequently accessed blocks of main (aka “system”) memory
Schematic of chip’s datapath (chip=datapath + CU), and where the cache fits in the big pic:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory
[Bryant and O‘Hallaron: CMU] →

## Slide 33: What it really looks like…
Source: Dell
Desktop PC
[Bryant and O‘Hallaron: CMU] →
Source: Dell
Motherboard
Source: Dell
Main memory (DRAM)
Source: PC Magazine
Source: techreport.com
CPU (Intel Core i7)
Gets dropped in here

## Slide 34: What it Really Looks Like [contd.]
[Bryant and O‘Hallaron: CMU] →
Bus interface
ALU
Register file
CPU chip (CU not shown below)
Cache
memory
Intel Sandy Bridge-E
Processor Die
[8 core-version]
L1: 32KB Instruction + 32KB Data
L2: 256KB
L3: 5–20MB
L3

## Slide 35: Caches: Come In Two Flavors
Data caches feed processor with data manipulated during execution
  If processor would rely on data provided by main memory the execution would be pitifully slow
    “Processor Clock” much faster than the “Memory Clock”
      Caches alleviate the memory pressure – processors are data hungry
Instruction caches: used to store instructions
  Simpler to deal with compared to the data caches
    By and large, instruction use is much more predictable than data use

## Slide 36: How Cache Comes into Play
All* read/write operations go through cache
Caches used to hold both data and instructions
  Data and instructions caches are in general different
    Intel: L1 DC (data cache) and L1 IC (instruction cache) have been distinct since approximately 1993
Main Memory
Cache
CPU Core
Bus

## Slide 37: Multiple Levels of Cache
Commodity chips today have 3 cache levels
  (some chips have a fourth cache level, see previous slide)
Main Memory
L3 Cache
Bus
L2 Cache
L1 D$
CPU Core
L1 I$

## Slide 38: Processor Clock vs. Memory Clock [important to understand]
Processor Clock: (look for the box )
  Dictates/defines the frequency at which Functional Units operate
Memory Clock:
  Dictates/defines the frequency used to move data into/out from main memory into cache
From RAM
To/From RAM

## Slide 39: Caches: How large? Also, how fast?
Ratio between cache size and main memory size
  Reasonable to expect something like 1:1000
    2013: 4 MB of L3 cache, versus 4 GB of main memory
    2017: 55 MB of L3 cache, versus 64 GB of main memory
Vintage: 2013 (related to Intel’s Haswell)
Latency in Clocks –Lower is Better
(log scale)
This chip has L4 cache, read more about it here
This is the overhead of a system memory access (about 100+ cycles)

## Slide 40: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 7
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way assoc.
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way assoc.
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way assoc.
  Access: 40-75 cycles
Cache line size: 64 bytes for all caches.
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 41
We talked about the hardware side of things, for caches
Let’s talk about the software side of things, to see how caches come into play

## Slide 42: Why Caches Work: the “Principle of Locality”
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  “Recently referenced items are likely to be referenced again in the near future”
Spatial locality:
  “Items with nearby addresses tend to come into use together”
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 43: Typical hit rates, actual numbers vary based on application
[https://www.extremetech.com/extreme/188776-how-l1-and-l2-cpu-caches-work-and-why-theyre-an-essential-part-of-modern-chips]
Instruction cache hit rate

## Slide 44: Spatial and Temporal Locality
Temporal Locality for memory access by a program
  Idea: If you access a variable at some time, then you’ll probably keep accessing the same variable for a while
    Example: a for loop with some variables inside the loop  you keep accessing those variables as long as you loop
Spatial Locality for memory access by a program
  A memory access pattern characterized by bursts of repeated requests for data that is physically located within the same memory region
  “Bursts” because these accesses should happen in a sufficiently short interval of time (lest the cache line gets evicted)

## Slide 45: Example, regarding concept of “locality”
Data references
  Array abc elements accessed in succession (stride-1 reference pattern) spatial locality
  Variable sum referenced at each iteration temporal locality
Instruction references
  Reference instructions in sequence spatial locality
  Cycle through loop repeatedly temporal locality
// some simple code snippet
sum = 0;
for (i = 0; i < n; i++)
sum += abc[i];
return sum;
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 46: Example: Adding the Entries in a 2D Matrix
Example used over several slides to show how “locality” and caches impact performance
Very related to your second assignment

## Slide 47: Example [motivation]: Adding the Entries in a 2D Matrix
Two equivalent ways to add the entries in a matrix
Row-wise:
Column-wise:
Example used over several slides to show how “locality” and caches impact performance
Second row
First row
First column
Second column
Third column
Fourth column

## Slide 48: Squashed format vs. 2D format
Storing a matrix: squashed format OR 2D format
Example:
Squashed format – using one long contiguous array of 6 entries. Like in your homework
The 2D format – using two arrays:
  Each has 4 entries
  Each of the two arrays stored somewhere in the memory (they might be far from each other)

## Slide 49: First way to represent 2D matrix: the “squashed,” 1D approach
One long array stores all entries in the matrix
  E.g., a 23 matrix will have an array of size 6
2D matrix stored in 1D array, row-wise fashion
  All the entries in the first row are stored first, followed by the entries in the second row, which are followed by the matrix in the third row, etc.
Note that we use malloc/new once
  We use delete once, when done with the array
Windows executable called “matrix1D.exe”
#include <cstdio>
struct squashedMatrix {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double *pMatVals;
};
int main() {
struct squashedMatrix mat1D;
mat1D.height = 1000; // perhaps you set this based on user input
mat1D.width = 2000; // perhaps you set this based on user input
mat1D.pMatVals = new double[mat1D.height * mat1D.width];
unsigned int i, j;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
mat1D.pMatVals[i * mat1D.width + j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0.;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
sum += mat1D.pMatVals[i * mat1D.width + j];
std::printf("The sum of the elements is: %f\n", sum);
// Done with the matrix; free the memory
delete[] mat1D.pMatVals;
return 0;
}

## Slide 50: A second way to represent the 2D matrix: the 2D approach
First, we allocate room to store a bunch of pointers to double
  There are “height” of these “double *” pointers
  These pointers stored in the array pRows
For each matrix row (and there are “height” of them), we allocate enough room to store “width” doubles
  These are the values that show up in a row of the matrix
Note that we use new/malloc multiple times
  We’ll have to use delete multiple times
Windows executable called “matrix2D.exe”
#include <cstdio>
struct Matrix2D {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double **pRows;
};
int main() {
struct Matrix2D mat2D;
mat2D.height = 1000; // perhaps you set this based on user input
mat2D.width = 2000; // perhaps you set this based on user input
mat2D.pRows = new double*[mat2D.height];
unsigned int i;
for (i = 0; i < mat2D.height; i++)
mat2D.pRows[i] = new double[mat2D.width];
// Get meaningful values in this matrix
unsigned int j;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
mat2D.pRows[i][j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
sum += mat2D.pRows[i][j];
std::printf("The sum of the elements is: %f\n", sum);
// Don't data anymore, free mem; note that free is used twice
for (i = 0; i < mat2D.height; i++)
delete[] mat2D.pRows[i];
delete[] mat2D.pRows;
return 0;
}

## Slide 51: The squashed approach, revisited: locality vs. non-locality
#include <chrono> // need this for cross-platform timers in C++
#include <cstdio>
#include <cstdlib>
struct squashedMatrix {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double *pMatVals;
};
int main(int argc, char *argv[]) {
if (argc != 2) {
std::printf("Pass 1 for row-wise, pass 2 for column-wise sum.\n");
return 1;
}
int option = std::atoi(argv[1]);
struct squashedMatrix mat1D;
mat1D.height = 2000; // perhaps you set this based on user input
mat1D.width = 2000; // perhaps you set this based on user input
mat1D.pMatVals = new double[mat1D.height * mat1D.width];
unsigned int i, j;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
mat1D.pMatVals[i * mat1D.width + j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0.;
auto start = std::chrono::high_resolution_clock::now(); // Get a timestamp
if (option == 1) {
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
sum += mat1D.pMatVals[i * mat1D.width + j];
} else if (option == 2) {
for (j = 0; j < mat1D.width; j++)
for (i = 0; i < mat1D.height; i++)
sum += mat1D.pMatVals[i * mat1D.width + j];
} else {
std::printf("Bad input option.\n");
return 1;
}
auto end = std::chrono::high_resolution_clock::now(); // Get a timestamp
auto elapsed = end – start; // Get difference between timestamps
std::printf("The sum of the elements is: %f\n", sum);
std::printf("Time spent in nanoseconds: %d\n",
std::chrono::duration_cast<std::chrono::nanoseconds>(elapsed).count()
);
// Done with the matrix; free the mem
delete[] mat1D.pMatVals;
return 0;
}

## Slide 52: Matrix, stored in squashed format
2

## Slide 53: Results, release build: 6 to 7 times faster if accessed w/ locality
TRUMAN Release> ./matrixRep1D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release> ./matrixRep1D.exe 1
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 3
TRUMAN Release> ./matrixRep1D.exe 2
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 23
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 54: The 2D approach, revisited: locality vs. non-locality
#include <chrono> // need this for cross-platform timers in C++
#include <cstdio>
#include <cstdlib>
struct Matrix2D {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double **pRows;
};
int main(int argc, char *argv[]) {
if (argc != 2) {
std::printf("Pass 1 for row-wise, pass 2 for column-wise sum.\n");
return 1;
}
int option = std::atoi(argv[1]);
struct Matrix2D mat2D;
mat2D.height = 2000; // perhaps you set this based on user input
mat2D.width = 2000; // perhaps you set this based on user input
mat2D.pRows = new double*[mat2D.height];
unsigned int i;
for (i = 0; i < mat2D.height; i++)
mat2D.pRows[i] = new double[mat2D.width];
// Get meaningful values in this matrix
unsigned int j;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
mat2D.pRows[i][j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0;
auto start = std::chrono::high_resolution_clock::now(); // Get a timestamp
if (option == 1) {
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
sum += mat2D.pRows[i][j];
} else if (option == 2) {
for (j = 0; j < mat2D.width; j++)
for (i = 0; i < mat2D.height; i++)
sum += mat2D.pRows[i][j];
} else {
std::printf("Bad input option.\n");
return 1;
}
auto end = std::chrono::high_resolution_clock::now(); // Get a timestamp
auto elapsed = end – start; // Get difference between timestamps
std::printf("The sum of the elements is: %f\n", sum);
std::printf("Time spent in nanoseconds: %d\n",
std::chrono::duration_cast<std::chrono::nanoseconds>(elapsed).count()
);
// Don't need data anymore, free mem; note that delete is needed twice
for (i = 0; i < mat2D.height; i++)
delete[] mat2D.pRows[i];
delete[] mat2D.pRows;
return 0;
}

## Slide 55: Matrix, stored in proper, 2D format

## Slide 56: Results, release build: 5 times faster if accessed w/ locality
TRUMAN Release> ./matrixRep2D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release> ./matrixRep2D.exe 1
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 4
TRUMAN Release> ./matrixRep2D.exe 2
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 20
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 57: The two scenarios, side by side: squashed and proper 2D
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
TRUMAN Release> ./matrixRep2D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release> ./matrixRep2D.exe 1
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 4
TRUMAN Release> ./matrixRep2D.exe 2
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 20
TRUMAN Release> ./matrixRep1D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release> ./matrixRep1D.exe 1
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 3
TRUMAN Release> ./matrixRep1D.exe 2
The sum of the elements is: 2772.088785
Time spent in nanoseconds: 23

## Slide 58: Final Exam type question: Qualitative Estimates of Locality
Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer
Question: Below, do we have good locality with respect to array a?
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
int sum_array_rows(int** a)
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 59: Final Exam type question: Qualitative Estimates of Locality
Question: Does this function have good locality with respect to array a?
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
int sum_array_cols(int** a)
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 60: Taking it to the next level: 3D Matrices – good locality
#include <iostream>
#include <chrono> // need this for timing
int main() {
const int M = 700;
double*** bPPP = new double**[M]; // use this to store 3d matrix
for (int i = 0; i < M; i++) {
bPPP[i] = new double*[M];
for (int j = 0; j < M; j++) {
bPPP[i][j] = new double[M];
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
auto start = std::chrono::high_resolution_clock::now();
// sum up all entries in 3D array
for (int i = 0; i < M; i++)
for (int j = 0; j < M; j++)
for (int k = 0; k < M; k++)
sum += bPPP[i][j][k];
auto end = std::chrono::high_resolution_clock::now();
auto elapsed = end – start;
auto as_micro = std::chrono::duration_cast<std::chrono::duration<double, std::micro>>(elapsed);
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << as_micro.count() << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
NOTE: We didn't delete[] our memory in this example, but you should always do it in your code.

## Slide 61: Taking it to the next level: 3D Matrices – bad locality
#include <iostream>
#include <chrono> // need this for timing
int main() {
const int M = 700;
double*** bPPP = new double**[M]; // use this to store 3d matrix
for (int i = 0; i < M; i++) {
bPPP[i] = new double*[M];
for (int j = 0; j < M; j++) {
bPPP[i][j] = new double[M];
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
auto start = std::chrono::high_resolution_clock::now();
// sum up all entries in 3D array
for (int k = 0; k < M; k++)
for (int j = 0; j < M; j++)
for (int i = 0; i < M; i++)
sum += bPPP[i][j][k];
auto end = std::chrono::high_resolution_clock::now();
auto elapsed = end – start;
auto as_micro = std::chrono::duration_cast<std::chrono::duration<double, std::micro>>(elapsed);
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << as_micro.count() << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
NOTE: We didn't delete[] our memory in this example, but you should always do it in your code.

## Slide 62: Running the code in Debug vs. Release mode: big difference?
#include <iostream>
#include <chrono> // need this for timing
int main() {
const int M = 700;
double*** bPPP = new double**[M]; // use this to store 3d matrix
for (int i = 0; i < M; i++) {
bPPP[i] = new double*[M];
for (int j = 0; j < M; j++) {
bPPP[i][j] = new double[M];
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
auto start = std::chrono::high_resolution_clock::now();
// sum up all entries in 3D array
for (int i = 0; i < M; i++)
for (int j = 0; j < M; j++)
for (int k = 0; k < M; k++)
sum += bPPP[i][j][k];
auto end = std::chrono::high_resolution_clock::now();
auto elapsed = end – start;
auto as_micro = std::chrono::duration_cast<std::chrono::duration<double, std::micro>>(elapsed);
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << as_micro.count() << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
“Debug” mode
“Release” mode

## Slide 63: Three observations related to our 2D and 3D examples
Observation 1: Final value for sum - stays the same (at least as far as we can tell)
  We’ll talk more about this when we do parallel computing w/ CUDA and then OpenMP
Observation 2: Difference between Debug vs Release builds
  3X to 4X speedup normal to see when going from debug to release (see also results on next slide)
Observation 3: Amount of time to get the result quite different
  Release mode build: the undesirable solution for 3D matrix is 30 times slower
    This is the case you see in practice – you build in release

## Slide 64: Observations on “Observation 1”
The fact that the results are the same is remarkable
Why remarkable?
  Finite precision arithmetic: addition loses its commutative and associative attributes
Because of finite precision
Because of finite precision

## Slide 65: Observations on “Observation 3” (most important)
First time in 759 discussing how to improve performance
  This type of gain; i.e., 30X speed up, not encountered every day…
Q: What mechanism comes into play to yield a 30X speed gain?
A: The cache
  L1 cache: 4 cycles
  System memory access: 120 cycles

## Slide 66: Indirection and how it’s hurting… An example. [one slide side trip]
Indirection: given an index i, you don’t need a[i]
  Rather, you need a[indir[i]] (this is one level of indirection; can go higher yet…)
What’s hurting here?
  First, when stride is large, you index into an array indir of non-negative integers but keep missing
    No locality…
  Second, you will subsequently jump in the array a all over the place
    Very likely you’ll just keep missing
Unfortunately, indirection in computing very common
void loop(int* a, unsigned int* indir, int N, int stride)
{
int sum = 0;
for (int i = 0; i < N; i+=stride)
sum += a[indir[i]];
}

## Slide 67: The Lesson Learned
Fact: Wide gap between using data and moving data
  Using data: you do sin of that data, log, pow, add, subtract, etc. (processing the data)
  Moving data: getting your data from the system memory (64 GB/128/etc. GB that you have on your system)
Fact: The cache used to close the big speed gap
Trait of well-written programs: they manage to leverage data/instruction locality
  Locality is what allows caches to come into play
  Locality necessary, but not sufficient (more later, “false sharing”)

## Slide 68
We’ve seen that caches can make a difference in speed of execution
Let’s see how they work, which will explain why they help

## Slide 69: [Back to caches: The inner workings of caches] General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
The Cache
The Main Memory
Main Memory: Larger, slower, cheaper memory
(shown here as partitioned into “blocks” that are
mapped into cache lines)
Data copied in block-sized transfer units. Each block (such as block 10, for instance) typically holds 64 bytes of data (called cache line).
Smaller, faster, more expensive
memory can store a subset of
the main memory blocks
4
4
4
10
10
10
Everything handled in hardware. Invisible to programmer
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 70: Cache Line (aka Cache Block)
When data is brought in cache because a piece of data is needed, the MMU brings more than just the needed piece of data
Why bring more data than what absolutely necessary?
  Because penalty is not high for bringing more: wide buses, little extra cost in bringing more data than exactly what needed
Corollary: you will reduce the number of trips to main memory if you use multiple times data from a cache line
“cache line”
  Many systems have cache line of 64 Bytes (8 doubles OR 16 floats OR 16 ints OR 64 chars, etc.)
  Cache line size is the same for L1, L2 and L3 caches

## Slide 71: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
Hit Rate: on average, how many out of 100 mem requests hit the cache?

## Slide 72: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where Block b goes
Replacement policy: determines which block gets evicted (victim)
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 73: Cache Miss Classification, by Request Type
One possible way to classify cache misses by the type of request leading to miss
Cache misses, by request type:
  Cache read miss from an instruction cache: generally causes the most delay, because the processor, or at least the thread of execution, has to wait (stall) until the instruction is fetched from main memory
  A cache read miss from a data cache: usually causes less delay (compared to instruction cache miss)
    OOOE: Instructions not dependent on the cache read (if any) can be issued and executed until the data is fetched from main memory and the stalled instructions can resume execution
    TLP: Another thread can be picked up for execution
  A cache write miss to a data cache: generally causes the least delay, because the write can be queued and there are few limitations on the execution of subsequent instructions. The processor can continue unless the queue is full and then it has to stall for the write buffer to partially drain

## Slide 74: Reasons for Cache Misses
Cold (compulsory) miss
  When happens: cache is empty (e.g., beginning of the program, time slicing while having multiple programs in flight)
Capacity miss
  When happens: Not enough space, working set is too large
    Example: the active part of main memory overwhelms in size what can be accommodated by the cache
      You are asking for more than what level can accommodate (fit)
Conflict miss
  When happens: Enough space, but you have bad luck (lots of “conflicts”, as dictated by placement/replacement policy in place)
  Fact: In the memory hierarchy, the cache blocks at level map into a small subset of block positions at level
    Example: block at level must be placed in block () at level
  Conflict misses occur when the level cache is large enough, but multiple data objects all map to the same block in the level cache.
    Example: Referencing in this order blocks 0, 8, 0, 8, 0, 8, ... would miss every time (since )

## Slide 75: Placement & Replacement Policies
The cache is small, while the memory that you try to cache in this cache is large
  The cache: prime real estate – when somebody comes in, somebody else has to be evicted
Caching: like bringing visitors from a large city to live in one apartment building next to some prime attraction
  “prime attraction”: the registers and the ALU/CU
placement policy: deciding at which “floor of the building” to host the new visitors (the new cache line)
If there are 2 or 4 or 8, etc. apartments (cache lines) at each floor level, which apartment do you choose?
  “replacement policy” – if you have Option A and Option B, which one should you choose: A or B?
    You’ll kick out tenants from apartment A, or tenants from apartment B?

## Slide 76: Placement & Replacement Policies [continued]
Policies that are common:
  “When you bring a line of cache…”
    You are free to place wherever (fully associative cache): Only 1 floor in the building (ranch-style apartment building), but lots of apartments
    Based on the address of the request you can put it in one of the 4 floors (many floors, and four apartments at each floor level)
      You can have, for instance, 2 apartments, or 8 apartments, or k places (for k-way associative cache)
    You can only put it in one place (direct mapped cache): skyscraper, but with one apartment per floor
  Note: you always have to place; sometimes you have to replace, too

## Slide 77: Placement & Replacement Policies [continued]
Direct mapping: cache is skinny skyscraper, with one apartment per floor
  Recall that apartment is large enough to accommodate 64 folks (Bytes)
Associative, K-way: a certain number of floors, each with K apartments
Fully associative cache: apartment level with ground level only

## Slide 78: Placement & Replacement Policies: further discussion
Fully associative (the ranch)
  Pros: you have full control which old cache line you want to kick out (lots of freedom for replacement policy)
  Cons:
    Higher overhead to find what you’re looking for (data can be anywhere in cache)
    Higher overhead to decide whom to evict (the “victim”)
Direct mapped (the tall skinny skyscraper)
  Pros: very fast to find if in cache or not
  Cons: sometimes, you’ll have to evict a line cache that sees a lot of use (no freedom at all in the placement policy)
K-way associative (Hilton Garden Inn)
  Decent compromise:
    It yields a reasonably decent replacement policy – you have K options to choose from
    At the same time, you don’t have to search too many apartments at a floor level
  NOTE: Intel and AMD chips - 2, 4, 8, 16-way associative
    Depends on cache level and which chip model

## Slide 79: [New Topic:] General Cache Organization [Symbols Used and Their Meaning]
B: Number of bytes in a cache line
  Typically, B is 64
E: The number of cache lines (“Elements”) that combine to make up a set
  Typically, E is 1, 2, 4, 8, or 16 (other values possible)
S: the number of “Sets” that make up the cache
: total cache size