## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 06
02/05/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Cartoon of the day

## Slide 3
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 4: Before we get started…
Last time
  Caches: how they work
  Example showing importance of cache locality
Today
  Caches, wrap up
  Virtual memory
Other tidbits:
  Assignment due on Th, 02/11, at 9 pm
  Do not run your code on the Euler headnode (use Slurm)
  Please read the ME459 “elements of C” material if malloc/new & pointers are not your friends

## Slide 5: Opportunity for independent study/research volunteering
If you are interested in computer graphics or computer vision and want to do an independent study or volunteer in a research lab, I’d like to work with you
Interested in working with one or two folks who know C or C++ and can help with simulating autonomous vehicles and robots
  A big plus if you are familiar with the Unity3D or Unreal gaming engines, or Carla/LGSVL sim environments
Topics of interest:
  Programmatic generation of virtual worlds: off-road scenarios, Mars/Moon, highways.
  Sensor simulation (camera simulation, lidar simulation, radar simulation, infrared sensing)
  Vehicle autonomy stacks for off-road mobility (like Autoware)
Why help is needed: NASA, US Army, and NSF projects that we want to expand and go beyond the call of duty
For more details, join me before office hours on Monday, February 8
  I’ll be in BBC at 7 PM to answer any questions and provide more context
Important: unfortunately, no funding support available. If we work together, it’ll be independent study or research volunteering

## Slide 6: The Caching Landscape in the Memory Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler/CU
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 7: Example [using CAE’s tux-103]
processor : 0
vendor_id : GenuineIntel
cpu family : 6
model : 60
model name : Intel(R) Core(TM) i5-4570 CPU @ 3.20GHz
stepping : 3
microcode : 0x20
cpu MHz : 3197.500
cache size : 6144 KB
physical id : 0
siblings : 4
core id : 0
cpu cores : 4
apicid : 0
fpu : yes
fpu_exception : yes
cache_alignment : 64
address sizes : 39 bits physical, 48 bits virtual
>> less /proc/cpuinfo
/sys/devices/system/cpu/cpu0/cache/index2/coherency_line_size:64
/sys/devices/system/cpu/cpu0/cache/index2/level:2
/sys/devices/system/cpu/cpu0/cache/index2/number_of_sets:512
/sys/devices/system/cpu/cpu0/cache/index2/size:256K
/sys/devices/system/cpu/cpu0/cache/index2/type: Unified
/sys/devices/system/cpu/cpu0/cache/index2/ways_of_associativity:8
Cache line size: 64 bytes → 2^6 Bytes
8-way associative → 2^3
L2 cache size: 256KB → 2^18 Bytes
Number of sets: 2^18/(2^6*2^3)=2^9=512
>> grep . /sys/devices/system/cpu/cpu0/cache/index*/*
BES=T
2^6 2^3 2^9=2^18=256KB

## Slide 8: Revisiting an old slide [hopefully it makes better sense now]
Registers
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Registers
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 20-30 cycles
Block size: 64 bytes for all caches.
[Bryant and O‘Hallaron: CMU] →

## Slide 9: We’ve done memory reads. What about writes?
Multiple copies of data exist stored in different places and at the same time:
  L1, L2, L3, Main Memory, Secondary Memory (Disk)
How should a write-hit be handled?
  Write-through (write immediately to main memory as well)
  Write-back (defer write to main memory until replacement of line)
    Need a dirty bit (indicate whether line different from memory or not)
How should a write-miss be handled?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow; i.e., if locality is good
  No-write-allocate (writes straight to memory, does not load into cache)
Typical combos met in practice:
  Write-back + Write-allocate ← more common
  Write-through + No-write-allocate

## Slide 10: Cache performance metrics [a nomenclature matter]
Miss Rate
  Defined as Miss Rate = 1 – Hit Rate (note that we defined the Hit Rate in the previous lecture)
  Represents the fraction of memory references that are not found in cache
  Typical numbers (in percentages):
    As low as 3-10% for L1
    Can be quite small (e.g., < 1%) for L2, depending on size, nature of problem you run, etc.
Hit Time
  Time to deliver a line in the cache into a register of the processor
    Includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    Typically 50-200 cycles for main memory (Trend: slightly increasing)
[Bryant and O‘Hallaron: CMU] →

## Slide 11: People Talk Miss Rate, Not Hit Rate
People talk about miss rate, and not hit rate
Weird math: Although 97 and 99 close, time-wise, 99% hit rate twice as costly as 97% hit rate
  Assumptions, for back of the envelope calculation: a) cache hit time of 1 cycle b) miss penalty of 100 cycles
  97% vs 99% hit rate: Access cost for 100 mem operations
  97% hit rate:
  99% hit rate:
You’d think that 97% is as good as 99%. It’s not…
  This is why “miss rate” is used instead of “hit rate”: 1% miss rate vs. 3% miss rate
[Bryant and O‘Hallaron: CMU] →

## Slide 12: Writing Cache Friendly Code: Rules of Thumb (more to come)
Basic facts:
  You have no *direct* control over what data gets cached
  However, you are not helpless: ensure your code is “local” (spatially and/or temporally)
when you write code, do not violate locality, if at all possible

## Slide 13: Other performance rule of thumb
Make the common case go fast
  Focus on the inner loops of the “heavy” functions
Try to have cache-friendly code in the inner loops
  Repeated references to same variables are good (temporal locality)
  “stride of one” reference patterns are good (spatial locality)
[Bryant and O‘Hallaron: CMU] →

## Slide 14: Approaching the task of programming
By and large, people write code by paying attention to
  Correctness
  Esthetics of the solution developed
    Objects, lists, patterns, inheritance, etc. – code is flexible and easy to maintain
  Portability
  Legacy
Data Analytics (Big Data): you should think about performance when writing/designing software
  Cache friendly code via “locality” is king
  When you write a line of code, always pause and ask yourself: where is this data that I’m referencing here comes from?
Departing thoughts:
  Does “performance” come before “esthetics”? Or “portability”?
  Good read: “The Mythical Man-Month,” by Frederick Phillips Brooks Jr.

## Slide 15: The “Memory Mountain” Experiment
Task at hand in this exercise: adding up numbers in an array (just like example of two lectures ago)
  The numbers must be brought over into the chip to be added
  Timing how long it takes to finish execution: a good proxy for speed of moving data
    Why?
      Because the math is trivial, eats up no time at all: sum = sum + a[i]
Moral of the story: the good cases are the ones with very high “effective bandwidth”
“effective bandwidth”: computed by dividing amount of data used during solving problem to the amount of time required to finish the execution
  Note: the data used is less than the data moved (you don’t use everything that you move)

## Slide 16: Memory Mountain Test Function
Call test() with many combinations of elems and stride.
For each elems and stride:
1. Call test() once to warm up the caches (important!!!)
2. Call test() again and measure the read throughput (MB/s)
NOTE: the “volatile” qualifier used to not optimize away the accumulator
void test(double* data, int elems, int stride) /* The test function */
{
int i;
double result = 0.0;
volatile double sink;
for (i = 0; i < elems; i += stride) {
result += data[i];
}
sink = result; /* So compiler doesn't optimize away the loop */
}
[http://www.cs.cmu.edu/afs/cs/academic/class/15213-f10/www/code/10-cache-memories/mountain/]→
void test(long *data, long elems, long stride)
{
volatile long accum = 0;
long i, sx2 = stride * 2, sx3 = stride * 3, sx4 = stride * 4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems;
long limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i + stride];
acc2 = acc2 + data[i + sx2];
acc3 = acc3 + data[i + sx3];
}
/* Finish any remaining elements */
for (; i < length; i += stride) {
acc0 = acc0 + data[i];
}
accum = ((acc0 + acc1) + (acc2 + acc3));
}
[http://www.cs.cmu.edu/afs/cs/academic/class/15213-f16/www/code/10-cache-memories/mountain/]→
2010 Vintage
2016 Vintage

## Slide 17: The Memory Mountain [2008]
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 5427 | 2757 | 1939 | 1455 | 1151 | 951 | 803 | 701 | 672 | 646 | 626 | 610
64m | 5496 | 2760 | 1936 | 1459 | 1149 | 949 | 803 | 703 | 666 | 644 | 621 | 610
32m | 5498 | 2758 | 1938 | 1454 | 1151 | 934 | 811 | 704 | 671 | 645 | 625 | 611
16m | 5506 | 2769 | 1941 | 1460 | 1153 | 953 | 811 | 705 | 672 | 646 | 626 | 614
8m | 5657 | 2977 | 2090 | 1586 | 1251 | 1035 | 882 | 766 | 777 | 836 | 1018 | 1365
4m | 10401 | 8422 | 7522 | 6468 | 5469 | 4809 | 4284 | 3894 | 3900 | 3899 | 3898 | 3897
2m | 10401 | 8418 | 7517 | 6468 | 5465 | 4804 | 4284 | 3898 | 3896 | 3897 | 3893 | 3897
1024k | 10479 | 8469 | 7578 | 6508 | 5510 | 4854 | 4326 | 3935 | 3939 | 3945 | 3951 | 3963
512k | 10486 | 8465 | 7578 | 6508 | 5514 | 4854 | 4330 | 3938 | 3945 | 3952 | 3956 | 3969
256k | 10479 | 8456 | 7578 | 6503 | 5510 | 4850 | 4322 | 3931 | 3935 | 3938 | 3944 | 3958
128k | 10473 | 8443 | 7552 | 6488 | 5496 | 4833 | 4307 | 3920 | 3912 | 3922 | 3923 | 3938
64k | 10460 | 8414 | 7537 | 6463 | 5474 | 4817 | 4295 | 3902 | 3897 | 3899 | 3893 | 3905
Core 2 Duo
2.4 GHz
32 KB L1 d-cache
6MB L2 cache
64 B block size
Ridges
of temporal locality
L1
Mem
L2

## Slide 18: The Memory Mountain [2014]
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 16636 | 8966 | 5846 | 4298 | 3403 | 2789 | 2348 | 2055 | 1904 | 1786 | 1693 | 1607
64m | 16925 | 9080 | 5860 | 4307 | 3408 | 2795 | 2352 | 2058 | 1912 | 1791 | 1695 | 1608
32m | 17168 | 9212 | 5897 | 4331 | 3431 | 2822 | 2375 | 2078 | 1924 | 1809 | 1713 | 1628
16m | 17405 | 9559 | 6027 | 4458 | 3520 | 2899 | 2465 | 2179 | 2049 | 1952 | 1883 | 1825
8m | 19339 | 11837 | 8045 | 6079 | 4927 | 4246 | 3745 | 3289 | 3131 | 3026 | 2899 | 2924
4m | 20728 | 16852 | 13212 | 10371 | 8542 | 7259 | 6345 | 5627 | 5396 | 5228 | 5090 | 4977
2m | 29025 | 19350 | 13735 | 10550 | 8610 | 7308 | 6361 | 5648 | 5417 | 5241 | 5094 | 4978
1024k | 29291 | 19543 | 13689 | 10508 | 8597 | 7281 | 6354 | 5628 | 5388 | 5218 | 5071 | 4956
512k | 29290 | 19411 | 13779 | 10594 | 8667 | 7390 | 6438 | 5684 | 5453 | 5325 | 5213 | 5128
256k | 29762 | 21456 | 16905 | 13504 | 11044 | 9359 | 8175 | 7240 | 7082 | 6889 | 6858 | 6835
128k | 30042 | 23953 | 22661 | 18952 | 15706 | 13602 | 11761 | 10409 | 10184 | 10137 | 10158 | 9875
64k | 29468 | 23044 | 21501 | 19208 | 15955 | 13551 | 11784 | 10516 | 10364 | 10320 | 10262 | 10132
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Core i5 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
[Bryant and O‘Hallaron: CMU] →

## Slide 19: Cache Capacity Effects from Memory Mountain
Chart: Working set size (bytes)
| 128m | 64m | 32m | 16m | 8m | 4m | 2m | 1024k | 512k | 256k | 128k | 64k | 32k | 16k
s8 | 2055 | 2058 | 2078 | 2179 | 3289 | 5627 | 5648 | 5628 | 5684 | 7240 | 10409 | 10516 | 26110 | 27746
Core i7 Haswell
3.1 GHz
32 KB L1 Data Cache
256 KB L2 Cache
8 MB L3 Cache
64 B block size
Slice through memory mountain with stride=8
L1
L2
L3
Main Memory
[Bryant and O‘Hallaron: CMU] →

## Slide 20: The “Memory Mountain” experiment: closing thoughts
Read throughput (read bandwidth)
  Number of bytes read from main memory per second (MB/s)
Memory mountain: Measures read-throughput as a function of spatial and temporal locality
  Bandwidth is always the same, but the effective bandwidth changes based on locality
[Bryant and O‘Hallaron: CMU] →

## Slide 21: Looking ahead
What we saw in the Memory Mountain experiment:
  Sometimes I get a cake, eat a slice and throw away the rest
We’ll touch on this “wasteful use of data” when we talk later about the “roofline model” for performance analysis
  We’ll look at the “roofline model” for GPU computing, but it applies to all other flavors of computing: sequential, multi-core, etc.

## Slide 22: Rearranging loops to improve spatial locality
Supplemental Reading

## Slide 23: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  Each row in contiguous memory locations
Stepping through columns in one row:
  Accesses successive elements
  If blockSize B [in bytes] > sizeof(aij) [in bytes], exploit spatial locality
    Miss Rate = sizeof(aij) / B
Stepping through rows in one column:
  Accesses distant elements
  When N is large, no spatial locality
    Miss rate = 1 (i.e. 100%)
for (i = 0; i < N; i++)
sum += a[0][i];
for (i = 0; i < N; i++)
sum += a[i][0];
[Bryant and O‘Hallaron: CMU] →

## Slide 24: Matrix Multiplication Example
Description:
  Multiply two N x N matrices
  Matrix elements are doubles (8 bytes)
  2N3 total FP operations
  N reads per matrix entry
  N values summed to get one entry
    But may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c
[http://www.cs.cmu.edu/afs/cs/academic/class/15213-f16/www/code/12-cache-memories/matmult]→

## Slide 25: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 64B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x
[Bryant and O‘Hallaron: CMU] →

## Slide 26: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.125 1.0 0.0
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 27: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.125 1.0 0.0
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 28: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.125 0.125
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 29: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.125 0.125
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 30: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 31: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
[Bryant and O‘Hallaron: CMU] →

## Slide 32: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.125
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.25
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
[Bryant and O‘Hallaron: CMU] →

## Slide 33: 2008-era Matrix Multiply Performance
Nanoseconds per floating-point operation. Measured on 2.4GHz Core 2 Duo
Chart: N
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650
ijk | 1.1 | 1.32 | 1.31 | 1.3 | 1.32 | 1.31 | 1.31 | 1.89 | 2.2 | 2.55 | 2.66 | 2.69 | 2.73
jik | 1.13 | 1.31 | 1.29 | 1.29 | 1.28 | 1.28 | 1.28 | 1.9 | 2.2 | 2.55 | 2.65 | 2.68 | 2.72
jki | 0.62 | 0.69 | 0.66 | 0.78 | 0.86 | 3.43 | 3.92 | 4.18 | 4.71 | 5.13 | 5.24 | 5.36 | 5.38
kji | 0.67 | 0.69 | 0.65 | 0.76 | 0.77 | 3.42 | 3.89 | 4.17 | 4.69 | 5.12 | 5.23 | 5.34 | 5.34
kij | 0.84 | 0.82 | 0.81 | 0.81 | 0.81 | 0.83 | 0.84 | 0.84 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83
ikj | 0.83 | 0.81 | 0.8 | 0.8 | 0.79 | 0.81 | 0.81 | 0.82 | 0.82 | 0.81 | 0.81 | 0.81 | 0.83
ijk / jik (1.125)
jki / kji (2.0)
kij / ikj (0.25)
[Bryant and O‘Hallaron: CMU] →

## Slide 34: 2014-era Matrix Multiply Performance
Nanoseconds per floating-point operation. Measured on 3.1 Ghz Haswell
Chart: N
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650
ijk | 0.39 | 0.4 | 0.42 | 0.47 | 0.44 | 0.45 | 0.45 | 0.49 | 0.46 | 0.47 | 0.47 | 0.5 | 0.47
jik | 0.4 | 0.4 | 0.42 | 0.43 | 0.43 | 0.44 | 0.45 | 0.46 | 0.45 | 0.45 | 0.45 | 0.45 | 0.45
jki | 0.38 | 0.35 | 0.35 | 0.43 | 0.44 | 0.96 | 1.21 | 1.25 | 1.23 | 1.23 | 1.23 | 1.24 | 1.23
kji | 0.37 | 0.36 | 0.33 | 0.46 | 0.42 | 0.97 | 1.22 | 1.26 | 1.24 | 1.25 | 1.24 | 1.25 | 1.24
kij | 0.35 | 0.31 | 0.3 | 0.31 | 0.3 | 0.3 | 0.29 | 0.29 | 0.29 | 0.29 | 0.29 | 0.29 | 0.29
ikj | 0.33 | 0.31 | 0.3 | 0.29 | 0.29 | 0.28 | 0.28 | 0.28 | 0.28 | 0.28 | 0.28 | 0.28 | 0.28
ijk / jik (1.125)
jki / kji (2.0)
kij / ikj (0.25)
[Bryant and O‘Hallaron: CMU] →

## Slide 35: New Topic: Virtual Memory

## Slide 36: Why talk about “Virtual Memory”?
Understand how memory transactions take place, and why some incur higher overhead
Add more credibility to some key points of this course, e.g.,
  Number crunching is inexpensive
  Moving information back and forth is expensive
    Both in terms of time & power

## Slide 37: Why talk about “Virtual Memory”?
  It will help us understand how unlucky a memory transaction can become
    E.g.: page faults, memory thrashing :-(
  It’ll make us appreciate caches even more
    They serve multiple purposes, e.g., help with: data storage, instruction storage, finding things in main memory (address translation)
  It helps us understand how unified memory works for GPU computing (discussed later, after GPU computing segment)
Notes: DN: nice summary of page faults vs thrashing is here - https://stackoverflow.com/questions/19031902/what-is-thrashing-why-does-it-occur

## Slide 38: Motivating Questions/Issues [1/3]
Question 1: How come you might have only 512MB of main memory on your laptop, yet you can new[] an array of 1 GB?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 39: Motivating Questions/Issues [2/3]
Question 2: How can 20+ processes seemingly run at the same time? How do they each know where they can read/write data from/to?
  Assume I have 1 GB of RAM, and programA allocates 2 GB of memory and programB allocates 2 GB of memory. How can they run at the same time?
  Does programA need to know what addresses in memory it can use for data so that it doesn’t step on the feet of programB (and perhaps programC, programD, etc.)?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 40: Motivating Questions/Issues [3/3]
Question 3: How can you compile a program on a Windows workstation with 16 GB of memory and run it later on a different laptop with 1 GB of memory; i.e., less memory?
  Are there any problems w/ addresses being referenced by the instructions?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 41: Preamble, Virtual Memory
When you compile a program there is no way to know where in the physical memory the code will get its data allocated
  There are other “tenants” that inhabit the physical memory & they are already there before you get there
Solution: the code compiled under assumption that resulting process has undisputed access to 4 GB of pristine memory (on 32 bit systems)
  The “pristine memory” is called the virtual memory space
Notes: hardware (MMU: memory management unit) converts virtual addresses into physical addresses
OS provides support for paging (conceptually using more memory than physically available)

## Slide 42: Virtual vs. Physical Memory
Virtual memory: a dally and quaint fictitious space of 232 addresses (on 32-bit architectures) in which a process sees its data being placed, the instructions stored, etc.
Physical memory: a busy place that hosts at the same time data and instructions associated with tens of applications running on the system
For the virtualphysical memory trick to work out it take the interplay between the compiler, the operating system (OS), and the execution model embraced by the processor

## Slide 43: Why do we like Virtual Memory?
The Virtual Memory paradigm allows:
  Running programs that require more memory than physically available
  Running multiple programs “simultaneously” (multi-tasking)
  Handling of memory fragmentation/segmentation insofar as the main memory is concerned
  Transparent and unitary handling of memory and secondary storage (hard disk / solid state disk)
What is the hardware component that manages the Virtual Memory show?
  The Memory Management Unit (MMU)
    MMU part of the chip these days (back in the day, it used to be an entity by itself, off chip)

## Slide 44: The Virtual Memory: its structure, and how it changes during execution [How perceived by compiler & runtime]
addresses (32 bit OS)
Notes: Ignore for the moment the messiness of the physical memory and concentrate on how the “pristine” layout of the virtual memory is seen by a process.
Each process partitions its virtual memory layout in several segments as shown here.

## Slide 45: Anatomy of the Stack
Function bar and associated stack frame
  Should the function bar be called, this is how the stack should be pushed
  A “pop” operation is the opposite, it shrinks the stack
This is where the top of the stack used to be before function bar was called
Notes: Reasons for the stack: you don’t know how many times a function is called. The function needs to place its data somewhere, right? It’s like a hidden malloc followed by a copying the arguments (a and b, above) in this memory, which will also be hit by t1, t2, etc.
The stack is a segment of fixed size that is managed in a LIFO manner (push and pop).
Order of variables in stack is decided by compiler. Typically arrays are stored contiguously.
Note: stack also stores value of return address (from subroutine). This is a back-door that can be used by malicious programs to hijack execution: bar() above could try to write to initials[1000] in the hope to overwrite a return address for a function higher up in the call stack.

## Slide 46: Virtual Memory: The Page Table
Virtual memory allows the processor to work in a virtual world in which each process, when run by the processor, seems to have exclusive access to a very large memory space (, addresses, that is)
This virtual world is connected back to, or mapped back into, the physical memory through a Page Table (PT)
  This is one level of indirection
Notes: Back to the MMU’s job: Translating between virtual addresses and physical addresses. This is done through a so-called Page Table
To see how the PT works, let’s first dissect a virtual memory address…

## Slide 47: Anatomy of a Virtual Memory Address
A virtual address split into two parts (another case of address splitting, like for caches, when we split 3 ways):
  The page number
  The offset
Example below assumes a 32-bit OS with virtual pages of bytes
[physical memory]
Notes: The virtual memory is split into pages.
The physical memory is split into frames.
This is for a 32-bit OS with virtual pages of 4096 bytes.
4096 = 2^12  need 12 bits to indicate the offset in the page.
(Note: unit of address resolution is 8 bits  a virtual page holds 4 KB)
The remaining 32-12 = 20 bits used to index into the Page Table to get the corresponding frame number (which is held in N bits)

## Slide 48: Anatomy of a Virtual Memory Address
A page of virtual memory corresponds to a frame of physical memory
The size of a page (or frame, for that matter) is typically 4096 bytes
  Compare to 64 bytes, the size of a memory block (cache line)
212=4096: 12 bits of the address are sufficient to relatively position each byte in a page
  Bits marked 0 through 11 on the previous slide

## Slide 49: The Translation Process
Example: imagine that your physical memory is 2 GB
The physical address has 31 bits: 231=2GB
Then the page table converts the bits 12 through 31 of the virtual address into bits 12 through 30 of the physical address
Notes: N depends on the amount of available RAM:
e.g. for 2GB of RAM, N=19. Because 2GB=2^31 bits and 31=12+19
since N max = 20  a 32-bit OS can reference 4GB of memory  a maximum of 1 million pages
each address requires 4bytes  the PT takes 4MB
each active application has its own PT  lots of memory just for the PTs

## Slide 50: Comments on the Page Table (PT): Preamble to TLB
Page table enables the translation of virtual addresses into physical addresses
Every single process executing on a processor and managed by the OS has its own page table
Page table is stored in main memory
  For a 32-bit operating system size of a page table can be up to 4 MB in size
    4 MB: 2^20 addresses, each requiring 4(?) bytes to encode
  Start address of the PT for a process is stored in a dedicated register (PTR)
    The job of the Operating System to take care of this
Notes: Recall:
N depends on the amount of available RAM:
e.g. for 2GB of RAM, N=19. Because 2GB=2^31 bits and 31=12+19
since N max = 20  a 32-bit OS can reference 4GB of memory  a maximum of 1 million pages
each address requires 4bytes  the PT takes 4MB
each active application has its own PT  lots of memory just for the PTs
NOTE: memory requirements for PT even slightly larger than that: there are additional bits associated with each entry, e.g.
valid bit indicating if the physical address is on secondary storage
use bit used in LRU eviction strategy

## Slide 51: The TLB [Translation Lookaside Buffer] [1/2]
If you go to Page Table in main memory for each address translation this would be very costly
  One trip to translate address, one trip to actually fetch the data
There is a “cache” for the address translation process: TLB
  Translation Lookaside Buffer: holds the translation of a small collection of virtual page numbers into frame IDs
Notes: On page fault, the OS does the following:
data requested is located in secondary storage
request made for an entire (“surrounding”) frame to be brought over in main memory
room is made for the new frame as a virtual page (this may require evicting an existing one; e.g. using a LRU strategy)
the new frame is loaded in the virtual page
the PT is updated to reflect the change
control returns to process which is instructed to retry the instruction that led to a page fault

## Slide 52: Illustration: The role of the TLB
A TLB is just another cache
  Implemented in hardware, on-chip
A TLB miss leads to substantial overhead in the translation of a virtual memory address
Notes: Without a TLB, the purpose of caches would be defeated: a trip to memory would be required just to interrogate the PT to figure out the actual physical address of the required information (instruction or data)
Typically, TLB has between 16 and 512 entries.
Its “cache line” is 2 PT rows.
Mapping is usually fully associative.
Hit time very short (1 cycle)
Miss penalty 10-100 cycles
Typical TLB miss rate: 0.01 – 0.1%

## Slide 53: The TLB [Translation Lookaside Buffer] [2/2]
The Good, the Bad and the Ugly [1966, Rated R, w/ Clint Eastwood, 97% Rotten Tomatoes]
  The Good: the TLB leads to a hit and allows for quick address translation
  The Bad: TLB doesn’t have the required information cached and a trip to main memory in order
  The Ugly: the value at address that was just translated is not in cache and trip to main memory in order
  The Really Ugly: the requested frame not in main memory and a trip to secondary memory in order
    Called “page fault,” you’re hitting significant latency at this point
    “memory thrashing”: repeatedly hitting page fault upon page fault, to the point where time wasted in handling page faults dominates all the rest
Purpose of this slide: understand what happens when you don’t hit caches and you need to figure out where your data is and then fetch it
Notes: On page fault, the OS does the following:
data requested is located in secondary storage
request made for an entire (“surrounding”) frame to be brought over in main memory
room is made for the new frame as a virtual page (this may require evicting an existing one; e.g. using a LRU strategy)
the new frame is loaded in the virtual page
the PT is updated to reflect the change
control returns to process which is instructed to retry the instruction that led to a page fault

## Slide 54: Quick side-trip, speed of memory
We saw 5X to 30X speedup if we hit the cache (good locality)
  Scenario: cache miss, you go to main memory
When handling large data sets, if they don’t fit in main memory and spill into secondary memory, lack of locality can lead to 1000X slowdowns
  Scenario: main memory page fault (even worse if you start getting into memory thrashing)

## Slide 55: Memory Access: The Big Picture, Includes Cache
A simplified version of how a memory request is serviced:
Notes: Note that the virtual memory mechanism allows looking at main memory as a “cache” for secondary storage.
Memory block  memory frame
Cache line (64 bytes)  virtual memory page (4096 bytes)
Cache miss  page fault
Note: page fault much more costly (secondary storage is even “farther” from RAM than RAM is to CPU)

## Slide 56: Quiz: on the likelihood of a “miss”
Say an integer operand from some address is needed to do some computation in the ALU.
When is it more likely to not hit the cache?
  When you are looking for the operand in the data cache
  When you are doing the page translation associated with the address of the integer
Notes: Looking for operand: you’re dealing w/ a cache line. For integers, there are 15 more integers next to you, in the same cache line
Looking for a page translation: there are 4096 bytes that share the same page, so there are 1023 other integers that will hit the same Page Table entry

## Slide 57: Quiz: Chop time for Cache read Virtual or Physical address?
To do, for instance, a cache read, you chop the address in three parts
Based on the picture at the right, what gets chopped in three parts: an address in virtual memory or in physical memory?

## Slide 58: Memory-related aspects: various other tidbits
Going on several tangents
  Virtual vs. Physical memories: how their size comes into play
  Pointers in gdb/Visual Studio: pointing into virtual or physical memory?
  Unit of address resolution
  Difference between thread and process (came up in the context of TLP)
  32 to 64 bit transition
  Frame size

## Slide 59: Virtual vs. Physical memories: how their size comes into play
Assumption: in this discussion we’re dealing with a 32 bit operating system
  Simpler to talk about it, fewer bits/smaller memories to keep track of. Nothing changes for 64 bit OSs
Case 1: The physical memory smaller than virtual memory
Case 2: The physical memory larger than virtual memory

## Slide 60: Case 1: Assume 2GB MB of RAM (my slim laptop)
2 GB of RAM: 2X more addresses in virtual memory than you have in physical memory
Depending how much memory your program uses, multiple virtual pages are going to be mapped into the same physical frame
Consequence: in reality, each entry in the Page Table always has [at least] one additional bit
  clean/dirty bit – indicates that translation to frame should not proceed immediately

## Slide 61: The Clean/Dirty Bit & the concept of Page Fault
Bit is “clean”: two conditions need to happen for the bit to be clean
  The frame that the page gets translated into has been loaded in main memory (think onset of execution)
  Since last translation, that very frame has not been associated with other virtual page
Bit is “dirty”:
  We called this before “page fault”, costly scenario to handle
  The OS will look for the needed frame on disk (secondary memory)
    The way you can think about it: the RAM (main mem) is the cache of the hard-disk (secondary mem)
      If bit in Page Table is dirty, the translation refers to address in secondary memory, not in main memory

## Slide 62: Case 2: Assume 16 GB of RAM (beefy workstation)
GB: this is good for your code, the likelihood of a memory frame getting evicted is smaller
PT should be “wide” enough (have enough bits) to recreate addresses to 16 GB of information
  You need 22 bits for pages of 4096 bytes:
    4096: 12 bits
    16 GB: need 34 bits to store addresses
    34-12=22 bits needed in each entry of the translation table
  NOTE: You have the same number of entries in the PT; they’re just wider compared to Case 1.
Note: clean/dirty bit also present if you have lots of physical memory since other programs run on the machine can render the bit “dirty”
  Imagine you run your code and Matlab comes in and starts working on 3.4 GB of memory
    Some of your frames will likely get evicted to disk
      Recall the concept of memory hierarchy, when things don’t fit, they’re send down the memory hierarchy

## Slide 63: [Short Topic] gdb/VS Pointers: Pointing In Virtual or Physical Memory?
Q: Is 0x000000DD582FFA18 an address in the virtual mem. or in the physical mem.?
A: This is a virtual memory address
  You see physical addresses if you are Linus Torvalds and work on kernel development
Quick note: addresses are provided in hex representation
Fewer digits to look at (would you prefer to look at 64 binary digits?)
Easy to figure out – each byte filled w/ binary digits translates into two digits out of the 16 hex digits used for the address
[https://inst.eecs.berkeley.edu/~cs61c/sp14/disc/12/dis12Sol.pdf]

## Slide 64: [Short Topic] The Unit of Address Resolution
How many bits are available for data storage at each address?
Example:
  We have 232 addresses that we can access
  If each address points to a location that stores 8 bits (one byte) then we have 4 GB of addressable memory
  However, if each address refers to a location that stores 2 bytes, we have 8 GB of addressable memory
Intel and AMD CPUs: the unit of address resolution is 1 byte (8 bits)
Consequence: the Intel 32 bit processors “see” a virtual memory space that can be 4 GB big and can reference each byte therein

## Slide 65: [New Short Topic] Difference between thread and process
A processor (core) can execute instructions from multiple threads at the same time
  This is a facet of TLP
  Example: OpenMP launches 2 threads to perform a for-loop in parallel
A processor (core) can execute instructions from multiple processes at the same time
  This is a facet of TLP
  Example: the OS runs both Outlook client and Chrome, and they’re simultaneously executed
What is the difference?
  The threads operate in the same virtual memory space; therefore, there is one Page Table
  The processes each has its own virtual memory space; therefore, there are two Page Tables

## Slide 66: In the weeds… A matter of semantics
The OS runs your program
  The program is run
The processor (core) executes [the instructions of] your program
  The instructions are executed

## Slide 67: [New Short Topic] The 32 to 64 bit migration (1/2)
If the architecture and OS have 32 bits to represent addresses, it means that 232 addresses can be referenced
The data sets that we’re working with today are really large
  Having only 232 addresses to work with hardly enough
  Example: I have 32 GB of RAM and need to work with 8 GB array. How do I reach the end of array? Addresses are not large enough…
This motivated push towards having addresses represented using 64 bits:
  Memory space that I can address balloons to 264 bytes

## Slide 68: The 32 to 64 Bit Migration (2/2)
Note that a 64 bit architecture typically calls for two things:
  From a hardware perspective: size of the registers, translation tables, tags in caches, etc. – they need to change
  From a software/OS perspective, the program “operates” in a huge virtual memory space
    The new number of addressable bytes: 18,446,744,073,709,551,615
    In reality, the virtual memory addresses are represented using only about 40 to 50 bits
Notes: But, a shift from 32-bit to 64-bit isn’t an automatic win
“Your pointers will get bigger; your alignment boundaries get bigger; your data is less dense; equivalent code is bigger. You will fit less useful information into one cache line, code and data, and you will therefore take more cache misses. Everything, but everything, will suffer. Your processor's cache did not get bigger. Even other programs on your system that have nothing to do with the code you’re running will suffer. And you didn’t need the extra memory anyway. So you got nothing. Yay for speed-brakes.”
Rico Mariani (Microsoft) on why Visual Studio is still a 32-bit application

## Slide 69: Example [using CAE’s tux-103]
processor : 0
vendor_id : GenuineIntel
cpu family : 6
model : 60
model name : Intel(R) Core(TM) i5-4570 CPU @ 3.20GHz
stepping : 3
microcode : 0x20
cpu MHz : 3197.500
cache size : 6144 KB
physical id : 0
siblings : 4
core id : 0
cpu cores : 4
apicid : 0
fpu : yes
fpu_exception : yes
cache_alignment : 64
address sizes : 39 bits physical, 48 bits virtual
>> less /proc/cpuinfo

## Slide 70: [New Short Topic] The size of the frame/page
Refresher: a memory page, or virtual page, is a fixed-length contiguous block of virtual memory, described by a single entry in the Page Table
The frame is the fysical (or physical) counterpart of a virtual page
Typically, size of page is 4 KB but can be of 1024 KB for certain applications
  Example: working with very large data sets (big data)

## Slide 71: The size of the frame/page
Large page size, pros
  Less TLB pressure
  Why?
    Fewer pages to blanket the virtual memory means fewer entries in the Page Table, which means
      Fewer values that compete for storage in the TLB cache. More TLB hits: faster program
      [not that big of a deal] The size of the Page Table is smaller – less memory needed to store it
Large page size, cons
  Might lead to wasteful use of physical memory
    Example: page size 1024 KB. If you need to allocate 1030 KB of memory, you use two pages/frames
      If your process doesn’t use rest of the second page, then there’ll be a sizeable hole in physical memory

## Slide 72: The size of page/frame
[https://en.wikipedia.org/wiki/Page_(computer_memory)]
Architecture | Smallest page size | Larger page sizes
x86-64 | 4 KiB | 2 MiB, 1 GiB
UltraSPARC Architecture 2007 | 8 KiB | 64 KiB, 512 KiB, 4 MiB, 32 MiB, 256 MiB, 2 GiB, 16 GiB
SPARC v8 with SPARC Reference MMU | 4 KiB | 256 KiB, 16 MiB
Power Architecture | 4 KiB | 64 KiB, 16 MiB, 16 GiB
IA-64 (Itanium) | 4 KiB | 8 KiB, 64 KiB, 256 KiB, 1 MiB, 4 MiB, 16 MiB, 256 MiB
ARMv7 | 4 KiB | 64 KiB, 1 MiB, 16 MiB
32-bit x86 | 4 KiB | 2 MiB, 4 MiB

## Slide 73: Departing thoughts, memory aspects
Memory transactions:
  Add overhead, at times rather large, owing to complex process of moving data
    From disk to main memory to cache to register
  Time and power costly
Keep in mind the memory hierarchy; understand the size of the memories on your machine
  The closer to the top of the hierarchy, the better off you are
If the speed of the code matters, pay attention to how you use memory

## Slide 74: Side-trip: Using C/C++ in this class
Using C/C++ in this class: good vehicle to explain how memory works
  Two aspects that bring C++ close to hardware: pointers & the new (memory allocation) operator
The overhead of memory transactions is there in any language (Fortran, Matlab, Python, etc.)
For your favorite language, learn how indexing into your arrays doesn’t violate locality

## Slide 75: Parallel computing: why, and why now?

## Slide 76: Acknowledgements
Sources for some of the material presented today
  Hennessy and Patterson (Computer Architecture, 5th edition)
  John Owens, UC-Davis
  Darío Suárez, Universidad de Zaragoza
  John Cavazos, University of Delaware
  Others, as indicated on various slides
  I apologize if I included a slide and didn’t give credit where was due
  Any mistakes in these slides belong to me, not the individuals above

## Slide 77: Argument made in this segment of the course
Sequential computing execution speed: only modest gains over the last decade
Parallel computing is where speed improvements have come from

## Slide 78: Main causes for sequential computing speed stalling
Memory Wall
Instruction Level Parallelism (ILP) Wall
Power Wall
Not necessarily walls, but increasingly steep hills to climb
Source: “The Many-Core Inflection Point for Mass Market Computer Systems”, by John L. Manferdelli, Microsoft Corporation
Notes: Predicted in 2000:

## Slide 79: Memory Wall
Memory Wall: What is it?
  The growing disparity of speed between CPU and memory outside the chip
Memory accesses have gradually become a mighty barrier to computer performance improvements
  The trend: ever growing caches to improve average memory reference time to fetch or write instructions or data
    Caches are a transistor black hole
    Also, as cache gets gradually larger, it also gets gradually slower
Memory Wall: due to latency and limited communication bandwidth beyond chip boundaries.

## Slide 80: Memory Latencies [typical server and mobile computers]
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Server
Mobile
CPU
Registers
Notes: Hammad: in the fifth edition of the book embedded/mobile have their own diagram

## Slide 81: Memory Speed: Widening of the Processor-DRAM Performance Gap
Plot:*log* scale, the increasing gap between CPU and memory
  The memory baseline: 64 KB DRAM in 1980
Memory speed increasing rate: 1.07/year
Processors improved
  1.25/year (1980-1986)
  1.52/year (1986-2004)
  1.20/year (2004-2010)
You have the chops to process data, but can’t bring data to processor fast enough

## Slide 82: Memory Latency vs. Memory Bandwidth
Latency [in our context]: how much time it takes a packet of data to get from one designated point to another
  Measured in seconds, also called “lag”
  The utility “ping” in Linux measures the latency of a network
  For memory transactions: send 32 bits to destination and back, measure how much time it takes gives you latency
Bandwidth: how much data can be transferred per second
  You can talk about bandwidth for memory but also for a network (Ethernet, Infiniband, modem, DSL, etc.)
Improving Latency and Bandwidth
  Mostly the job of folks in Electrical Engineering
  Once in a while, Materials Science colleagues deliver a breakthrough
  Promising technology: optic networks; layered memory on top of chip; etc.

## Slide 83: Memory Latency vs. Memory Bandwidth
Memory Access Latency more challenging to improve as opposed to improving Memory Bandwidth
Improving Bandwidth: add more “pipes”
  Requires more pins that come out of the chip for DRAM, for instance
  Adding more pins is not simple – very crowded real estate plus the technology is tricky
Improving Latency: no easy answer here
Analogy:
  If you carry commuters with a train, add more cars to a train to increase bandwidth
  Improving latency requires the construction of high speed trains (expensive/complex)

## Slide 84: Latency vs. Bandwidth: Recent Evolution of Speed Gains
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Notes: For the Microprocessor this is measured in MIPS (million instructions per second). Many reported IPS values have represented "peak" execution rates on artificial instruction sequences with few branches, whereas realistic workloads typically lead to significantly lower IPS values.

## Slide 85: Memory Wall, Conclusions [IMPORTANT SLIDE]
Take-home message: try to stay away from long and winding conversations with main memory
Memory-wise, you may or may not be at top speed for your memory
  Effective bandwidth==Nominal bandwidth: you move lots of data - ok, fact of life, some applications are just like that
  Effective bandwidth < Nominal bandwidth: you bring a block of data, use little of it, and ask for data from a different block
    Examples – sparse matrix operations, combinatorics, etc.
    Where we saw this: the memory mountain

## Slide 86: Memory Wall, Conclusions [IMPORTANT SLIDE]
This is an important picture to have in mind when writing software
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition

## Slide 87: The next wall: Instruction Level Parallelism (ILP)
Instruction pipelining: the execution of multiple instructions overlapped; each instructions is divided into series of sub-steps (termed: micro-operations)
Superscalar execution: multiple execution units are used to execute multiple instructions in parallel
Out-of-order execution: instructions execute in any order but without violating data dependencies
Register renaming: a technique used to avoid data hazards and thus lead to unnecessary serialization of program instructions
Speculative execution: allows the execution of complete instructions or parts of instructions before being sure whether this execution is required
Branch prediction: used to avoid delays (termed: stalls). Used in combination with speculative execution.

## Slide 88: Intel Haswell example: ILP elicits very complex microarchitecture
[http://www.realworldtech.com/haswell-cpu/ ]
Notes: Dan - AGU: Address generation unit

## Slide 89: Sample Pipeline Depths
Pipeline Depth | Processors
6 | UltraSPARC T1
7 | PowerPC G4e
8 | UltraSPARC T2/T3, Cortex-A9
10 | Athlon, Scorpion
11 | Krait
12 | Pentium Pro/II/III, Athlon 64/Phenom, Apple A6
13 | Denver
14 | UltraSPARC III/IV, Core 2, Apple A7/A8
14/19 | Core i*2/i*3 Sandy/Ivy Bridge, Core i*4/i*5 Haswell/Broadwell
15 | Cortex-A15/A57
16 | PowerPC G5, Core i*1 Nehalem
18 | Bulldozer/Piledriver, Steamroller
20 | Pentium 4
31 | Pentium 4E Prescott
[http://www.lighterra.com/papers/modernmicroprocessors/]→

## Slide 90: The ILP Wall
Dedicated hardware speculatively executes future instructions before the results of current instructions are known, while providing hardware safeguards to prevent the errors that might be caused by out of order execution
Branches must be “guessed” to decide what instructions to execute simultaneously
  If you guessed wrong, you throw away that part of the result
Data dependencies may prevent successive instructions from executing in parallel, even if there are no branches
Predicting the future comes at the cost of microarchitecture complexity and power cost

## Slide 91: The ugly head of speculative execution
Speculative execution difficult to implement safely
Has become infamous for a recently-revealed series of vulnerabilities
  Foreshadow (Intel, 2018)
  Meltdown (Intel, Apple)
  Spectre (Intel, Apple, ARM, AMD)
    Everything before 2019 that uses branch prediction
    Arbitrary locations in the allocated memory of a program can be read

## Slide 92: [The last wall] The Power Wall
Power dissipation related to the clock frequency and feature length
  Consequence (the wall): clock rates are limited to some threshold value
Significant increase in clock speed without heroic/expensive cooling not possible. Chips would simply melt
Between 1990 and 2010, clock speed increased by a factor of 4,000
  The ability of manufacturers to dissipate heat is limited though…
  Looking back at the last ten years the clock rates pretty much flat

## Slide 93: The Power Wall
Power, and not manufacturing, limits traditional general purpose microarchitecture improvements
  Point made already in 1999 by F. Pollack, Intel Fellow, see here .
  Kind of true, but sadly Intel not pushing the manufacturing frontier anymore. Taiwan & S. Korea do.
Leakage power dissipation gets worse as gates get smaller, because gate dielectric thicknesses decrease proportionately

## Slide 94: Dennard’s Scaling: Making Moore’s Law Useful
Dennard scaling: dictates how the voltage/current, frequency should change in response to smaller feature size
Voltage lower and lower, static power losses more prevalent
The bad news: direct tunneling gate leakage current (thin dielectric) transistors too close
Amount of power dissipated grows to high levels
  Thermal runaway
  Moving towards threshold at which computing not reliable
    What’s noise and what’s information?

## Slide 95: The “dark silicon”
Dark Silicon: transistors that manufacturers cannot afford to turn on
Too many transistors on a chip – cannot afford to power them lest the chip melts
Esmaeilzadeh, H.; Blem, E.; St.Amant, R.; Sankaralingam, K.; Burger, D., "Dark silicon and the end of multicore scaling," in Comp. Architecture (ISCA), 2011 38th Annual International Symp., pp.365-376, 2011

## Slide 96: One slide detour: “spending energy” rates
NVIDIA Tesla K80
  TDP: 300 Watts
Intel® Xeon® Processor E7-8890 v3
  TDP: 165 Watts
Human Brain
  20 Watts
  Represents 2% of our mass
  Burns 20% of all energy in the body at rest
  Our entire body, ball park: 100-120 Watts
Notes: [DN]
For a Opteron 6276, TDP is 115 W.
The Thermal Design Power (TDP) is the average maximum power a processor can dissipate while running commercially available software. TDP is primarily used as a guideline for manufacturers of thermal solutions (heatsinks/fans, etc) which tells them how much heat their solution should dissipate. TDP is not the maximum power the CPU may generate - there may be periods of time when the CPU dissipates more power than designed, in which case either the CPU temperature will rise closer to the maximum, or special CPU circuitry will activate and add idle cycles or reduce CPU frequency with the intent of reducing the amount of generated power.
TDP is usually 20% - 30% lower than the CPU maximum power dissipation.

## Slide 97: Shift in Perception
Increasing clock frequency is primary method of performance improvement
Processors parallelism is primary method of performance improvement
Less than linear scaling for a multiprocessor is failure
Even sub-linear speedups are beneficial as long as you beat the sequential on a watt-to-watt basis
Yesterday’s school of thought
Yesterday’s school of thought
Today’s take
Today’s take

## Slide 98: Conventional Wisdom in Computer Architecture
Old: Transistors expensive; Power is free
New: Transistors free; Power management very tricky (consequences, “lots of power”: heat to be dissipated & battery management)
Old: Math is slow; Memory access is fast
New: Math is fast; Memory slow (120 cycles for DRAM memory access, 1 cycle for pipelined FMA)
Old: Increasing Instruction Level Parallelism hardware and compilers (Out-of-order, speculation, VLIW, …)
New: ILP sees diminishing returns; non-ILP parallelism pursued
Power Wall
Memory Wall
ILP Wall
Notes: Power wall + Memory wall + ILP wall  BRICK wall

## Slide 99
Just a bunch of bad news…
OK, now what?

## Slide 100: Another quote of the day
“The report of my death was an exaggeration.”
-- Mark Twain, American writer, humorist, entrepreneur, publisher, and lecturer [1835-1910]

## Slide 101: The bright spot
We can produce small[er] transistors and we are increasingly good at packaging them in ICs

## Slide 102: Good news: number of transistors going up

## Slide 103: Moore’s Law (1965)
“The complexity for minimum component costs has increased at a rate of roughly a factor of two per year [see graph on next page]. Certainly over the short term this rate can be expected to continue, if not to increase. Over the longer term, the rate of increase is a bit more uncertain, although there is no reason to believe it will not remain nearly constant for at least 10 years. That means by 1975, the number of components per integrated circuit for minimum cost will be 65,000. I believe that such a large circuit can be built on a single wafer.”
“Cramming more components onto integrated circuits” by Gordon E. Moore, Electronics, Volume 38, Number 8, April 19, 1965

## Slide 104: Moore’s Law
1965 paper: Doubling of the number of transistors on integrated circuits every two years
  Moore himself wrote only about the density of components (or transistors) at minimum cost
http://news.cnet.com/Images-Moores-Law-turns-40/2009-1041_3-5649019.html

## Slide 106: Moving to the processor: transistor counts per microprocessor

## Slide 107: Intel Roadmap [or other folks’ roadmap]
2013 – 22 nm Tick: Ivy Bridge – Tock: Haswell
2015 – 14 nm Tick: Broadwell – Tock: Skylake
2016 – 14nm “Refresh” Kaby Lake
2017 – 10 nm Cannon Lake (delayed to 2019)
2019 – 7 nm [AMD: Radeon Instinct MI60/Zen2]
2021 – 5 nm (Samsung & TSMC, in testing)
2023 – 3 nm (Samsung?)
Notes: Hammad: Even intel is having problems going down in process technologies. 10nm was delayed until the second half of 2017. Broadwell didn’t have good yields, they never released a desktop version (only laptop) and went straight to skylake for desktop CPUs

## Slide 108
[OurWorldInData.org]