## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 08
02/10/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Cartoon of the day
[Joe Dator]

## Slide 3
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 4: Before we get started…
Last time
  Wrap up Virtual memory discussion
  Discuss why folks started to look into parallel computing
    The three walls: memory, power, ILP
    Moore’s law, and implications
Today
  Flynn’s Taxonomy
  Amdahl's Law
  Start GPU computing: discussion of hardware aspects
Other tidbits:
  Assignment due on Th, 02/11, at 9 pm
  Do not run your code on the Euler headnode (use Slurm)
  Please read the ME459 “elements of C” material if malloc/new & pointers are not your friends

## Slide 5: Transistors bonanza: bringing happiness in lots of corners
Ability to cram more transistors per unit area and still make a profit good in many respects
  Microprocessors
  Memory capacity & speed
  Storage controllers

## Slide 6: Parallel computing: The Ox vs. Chickens Analogy
Ox: one powerful CPU core, running at high frequency, lots of cache to hide memory latency
Chicken: many meagre processors, running at lower frequency, not much cache or brain (like in CU)
  Requires other ways to hide memory latency
Few were eating chicken a decade ago but popular now
“If you were plowing a field, which would you rather use: Two strong oxen or 1024 chickens?” [Seymour Cray]

## Slide 7: Two examples of Parallel HW: Putting to good use billions of transistors
Intel Haswell
  Multicore architecture
  Four oxen, that is
NVIDIA Fermi
  Large number of scalar processors (“shaders”)
  512 chicken, that is

## Slide 8: Intel Haswell
June 2013
22 nm technology
1.4 billion transistors
4 cores, HTT
Integrated GPU
System-on-a-chip (SoC) design
Notes: Direct Media Interface (DMI) is the link between the northbridge and southbridge on a computer motherboard

## Slide 9: Haswell example: multi-core architecture (four oxen)
Shared-Memory Multiprocessor Architecture
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
SRAM
DRAM
SRAM
Notes: Hammad – Updated Figure from fifth edition

## Slide 10: The Fermi Architecture [ Schematic of a NVIDIA Stream Multiprocessor (SM)]
Late 2009, early 2010
40 nm technology
Three billion transistors
512 Scalar Processors (SPs), or “shaders”
  This is the chicken
L1 cache
L2 cache
6 GB of global memory
Operates at low clock rate
High bandwidth (for 2010, 200 GB/s)

## Slide 11: A Fermi SM (Streaming Multiprocessor; one of 16)
Not a whole lot of brain here, compared to CPU.

## Slide 12: Fermi: 30,000 feet perspective, the entire chip
Lots of ALU (green), not much of CU (orange)
Explains why GPUs are fast for high arithmetic intensity applications
Arithmetic intensity: high when many operations performed per byte of data

## Slide 13: The CPU and GPU: showing their true colors
The GPU is specialized for compute-intensive, highly data parallel computation (owing to its graphics rendering origin)
  More transistors devoted to data processing rather than data caching and control flow
  Where are GPUs good: high arithmetic intensity (the ratio between arithmetic operations and memory operations)
The video game industry exerts strong economic pressure that pushes things forward in GPU computing
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 14: Beefy CPU vs. beefy GPU comparison, 2021
 | GPU – NVIDIA Tesla A100 40 GB $9895 | CPU – Intel® Xeon® Platinum 9282 (about $20K? – can’t find a price)
Processing Cores | 6912 CUDA Scalar Processors 432 Tensor Cores | 56 cores (112 threads, SMT)
Memory (apples vs. oranges) | 40GB HBM2 | - 32+32 KB L1 (I+D) cache / core (8-way assoc.) - 1 MB L2 cache / core (16-way assoc.) - 77 MB L3 cache (1.375 MB / core, average)
Clock speed | 1.41 GHz (max) | 2.6 GHz (3.80 GHz Turbo)
Memory bandwidth | 1555 GB/s | 262 GB/s
Floating Point Throughput | 9.7 Double Precision TFLOP/s 19.5 Single Precision TFLOP/s | 3.2 Double Precision TFLOP/s
TDP | 250 Watts | 400 Watts
https://en.wikipedia.org/wiki/Nvidia_Tesla
https://en.wikichip.org/wiki/intel/xeon_platinum/9282

## Slide 15: Beefy CPU vs. beefy GPU comparison, 2019
 | GPU – NVIDIA Tesla V100 32GB $8,995 | CPU – Intel® Xeon® Platinum 8180 $10,009
Processing Cores | 5120 CUDA Cores 640 Tensor Cores | 28 cores (56 threads, SMT)
Memory | 32GB HBM2 | - 64 KB L1 (I+D) cache / core - 1 MB L2 cache / core - 38.5 MB L3 cache (1.375 MB / core), average
Clock speed | 1.29 GHz | 2.5 GHz (3.80 GHz Turbo; Throttles to 2.3 GHz when all FP units are active)
Memory bandwidth | 900 GB/s | 119.21 GB/s (19.87 GB / channel / s)
Floating Point Throughput | 7.8 Double Precision TFLOP/s 15.6 Single Precision TFLOP/s | 2.0608 Double Precision TFLOP/s
TDP | 300 Watts | 205 Watts
https://en.wikipedia.org/wiki/Nvidia_Tesla
https://www.techpowerup.com/gpu-specs/tesla-v100-sxm2-32-gb.c3185
https://en.wikichip.org/wiki/intel/xeon_platinum/8180
https://ark.intel.com/products/120496/Intel-Xeon-Platinum-8180-Processor-38-5M-Cache-2-50-GHz-

## Slide 16: Other good news: 3D Stacked Memory [looking at other things than just raw increase in transistor count]
Major step forward in performance.
Traditional GPU chip GDDR5 memory layout
New GPU (Pascal/Volta/Ampre) chip HBM2 memory layout

## Slide 17: 3D Stacked Memory
1st Generation (HBM1) introduced in AMD Fiji GPUs
  1GB & 128GB/s per stack
  AMD Radeon R9 Fury X: had four stacks  4GB & 512GB/s
2nd Generation (HBM2) used in NVIDIA Pascal/Volta and AMD Arctic Island GPUs
  2 GB & 256GB/s bandwidth per stack
  NVIDIA Volta approximately 900 GB/s memory bandwidth
  Apparently AMD has 1024 GB/s HBM available
SK Hynix’s High Bandwidth Memory (HBM)
  Developed by AMD and SK Hynix
NOTE: There is consistent color code used in both these figures
Notes: PHY: die-to-die [physical?] interconnect (see https://www.synopsys.com/dw/ipdir.php?ds=dwc_die-to-die_phy)

## Slide 18: 3D Stacked Memory

## Slide 19: 3D Stacked Memory
Shorter distances
  Smaller latency nice!
  Less power required to move data
Smaller memory footprint
  16X smaller footprint
One HBM stack, made up of four DRAM dies (4-Hi)
Logic die

## Slide 20: [side trip, 1/2] on-chip vs. on-package vs. off-package
Where a resource is dictates to a large extent its communication latency and/or bandwidth
Example, on-chip: Intel Haswell has the GPU on the same chip with the rest of the CPU
Example, on-package: the 128 MB of eDRAM available on Intel Core i7 4950HQ
The GPU is on-chip
The eDRAM is on-package

## Slide 21: [side trip, 2/2] on-chip vs. on-package vs. off-package
Example, off-package vs. on-package: traditional memory vs. HBM
Off-package Example chip GDDR6 memory
On-package Example chip HBM2 memory

## Slide 22: [New Topic] Flynn’s Taxonomy of Architectures [Moving away from hardware; moving into software aspects]
SISD - Single Instruction/Single Data
SIMD - Single Instruction/Multiple Data
MISD - Multiple Instruction/Single Data
MIMD - Multiple Instruction/Multiple Data
There are several ways to classify architectures
Below, classification based on how instructions are executed in relation to data

## Slide 23: Single Instruction/Single Data (SISD) Architectures
Your desktop, before the spread of dual core CPUs
[Wikipedia, Flynn’s Taxonomy]
PU – Processing Unit
Notes: PU – Processing Unit

## Slide 24: Increasing Throughput of SISD
Instructions:
Multiple Issue
Pipelining
Time
Time
[Wikipedia, Flynn’s Taxonomy]

## Slide 25: Single Instruction/Multiple Data (SIMD) Architectures
Processors that execute same instruction on multiple pieces of data: GPUs
[Wikipedia, Flynn’s Taxonomy]
Notes: Mention also AVX

## Slide 26: Single Instruction/Multiple Data (SIMD)
Each core runs the same set of instructions on different data
Examples:
  Graphics Processing Unit (GPU): processes pixels of an image in parallel
  CRAY’s vector processor
[Klimovitski & Macri, Intel]
Notes: Big data is a major motivator for this type of processing.
Whenever you see lots of data, first consider SIMD

## Slide 27: SISD versus SIMD
[Jon Stokes]

## Slide 28: SISD, SIMD, and Vector Length
SIMD: the concept of vector length
  Assume numbers shown above are integers
  8 ints 4 Bytes each 8 Bits/Byte = 256 Bit Vector Length (AVX2)
  Intel AVX512: 512-bit vector length
A stream of 8 “SISD” instructions
One SIMD instruction
Accomplishing the same thing

## Slide 29: Multiple Instruction/Single Data
Not useful, not aware of any commercial implementation…
[Wikipedia, Flynn’s Taxonomy]

## Slide 30: Multiple Instruction/Multiple Data
Almost all our desktop/laptop chips are MIMD systems. Think Intel’s HTT
[Wikipedia, Flynn’s Taxonomy]
Notes: Most (all?) Top500 supercomputers based on MIMD

## Slide 31: Multiple Instruction/Multiple Data
The sky is the limit: each PU is free to do as it pleases
Can be of either shared memory or distributed memory categories
Instructions:
Notes: Before we move on, a couple of words on difference between HPC and HTC

## Slide 32: [New Topic] Amdahl's Law
“A fairly obvious conclusion which can be drawn at this point is that the effort expended on achieving high parallel processing rates is wasted unless it is accompanied by achievements in sequential processing rates of very nearly the same magnitude”
“Validity of the single processor approach to achieving large scale computing capabilities,” by Gene M. Amdahl, in Proceedings of the “AFIPS Spring Joint Computer Conference,” pp. 483, 1967
Notes: How do you know if it makes sense or not to parallelize a piece of code?
What should you expect (in terms of speedup)?

## Slide 33: Amdahl’s Law
Sometimes called the law of diminishing returns
In the context of parallel computing used to illustrate how going parallel with a part of your code is going to lead to overall speedups
The art is to find for the same problem an algorithm that has a large
  Sometimes requires a completely different angle of approach for a solution
Nomenclature
  Algorithms for which are called “embarrassingly parallel”

## Slide 34: Example: Amdahl's Law
Suppose that a program spends 60% of its time in I/O operations, pre and post-processing
The rest of 40% is spent on computation, most of which can be parallelized
Assume that you buy a multicore chip and can throw 6 parallel threads at this problem.
What is the maximum amount of speedup that you can expect given this investment?
Asymptotically, what is the maximum speedup that you can ever hope for?
Notes: Answer: 1.5X
(60 + 40)/(60 + 40/6)
Asymptotically: 100/60 = 5/3=1.666 X

## Slide 35: Trivia
Gene Amdahl (1922-2015)
Graduated from UW-Madison
  1952 PhD, Mathematics and Physics
Amdahl’s law (1967)

## Slide 36: GPU Computing with CUDA

## Slide 37: The long view
Goal: Understand how GPUs can be used in Scientific Computing
Topics
  Hardware considerations
  “Hello World” with GPU computing
  Execution configuration issues
  The memory model in CUDA
  Scheduling issues in CUDA
  Occupancy and optimization issues
Notes: It’s fast for a variety of jobs Really good for data parallelism (another way of saying SIMD)
It’s cheap to get one ($120 to $480) High end GPUs for Scientific Computing are more like $7000
GPUs are everywhere Chances are you have one or at least have easy access to one

## Slide 38: Typical Hardware Architecture
CPU
(the “host”)
GPU w/ local DRAM
(the “device”)
[http://www.anandtech.com]
Notes: The bridge now absorbed in CPU (the chipset).
GPUs also called accelerators or co-processors (complement the CPU).
The GPU connected through the PCIe bus
In PCIe 1.1 (currently the most common version) each lane sends information at a rate of 250 MB/s (250 million bytes per second) in each direction. PCIe 2.0 doubles this data rate, introduced in late 2007, PCIe 2.0 is found on newer systems such as those based around the Intel X38 or AMD 780G chipsets. The latest proposed PCIe 3.0 standard will increase the speed of the links further (tentatively scheduled for release around 2010).[1]
Each PCIe slot carries either one, two, four, eight, sixteen or thirty-two lanes of data between the motherboard and the addin card. Lane counts are written with an "x" prefix e.g. x1 for a single-lane card and x16 for a sixteen-lane card. Thirty-two lanes of 250 MB/s (PCIe 1.1) gives a maximum transfer rate of 8 GB/s (250 MB/s x 32, i.e., 8 billion bytes per second) in each direction. However the largest size in common use for PCIe 1.1 is x16, giving a transfer rate of 4 GB/s (250 MB/s x 16) in each direction. Putting this into perspective, a single lane for PCIe 1.1 has nearly twice the data rate of normal PCI, a four-lane slot has a transfer rate comparable to the fastest version of the old parallel PCI-X 1.0, and an eight-lane slot has a transfer rate comparable to the fastest version of AGP. However the data rates cited must be derated because 8b/10b coding is used in the physical layer. The link transfer speeds cited are to be considered maximum theoretical data rates.
PCIe slots come in a variety of physically different sizes referred to by the maximum lane count they support, ie. x1, x2, x4, x8, x16 and x32. A PCIe card will fit into a slot of its size or bigger, but not into a smaller PCIe slot.

## Slide 39: Euler Node, 2015 Vintage

## Slide 40: NVIDIA GPU Evolution [relative to dense matrix-matrix multiplication performance per Watt]
Slightly dated plot, doesn’t show Ampere architecture
Notes: Next (2018): Volta

## Slide 41: GPU computing: eager to accommodate Machine Learning needs

## Slide 42: Fermi: High-level Perspective
Lots of ALU (green), not much of CU (orange)
Explains why GPUs are fast for high arithmetic intensity applications
Arithmetic intensity: high when many operations performed per word of memory access
Notes: How else could you organize 3 billion (today 7 billion) transistors?
Specialize the hardware. Organize it into a bunch of Streaming Multiprocessors and dedicate most transistors to number crunching (ALUs)

## Slide 43: The Fermi Architecture: The Stream Multiprocessor (SM)
Late 2009, early 2010
40 nm technology
Three billion transistors
512 Scalar Processors (SP), or “shaders”
L1 cache (64 KB)
L2 cache (768 KB uniform, shared)
6 GB of global memory
Operates at low clock rate
Memory bandwidth 200GB/s
The “Stream Multiprocessor”
Notes: An SM is the quantum of scalability on a GPU. More $  more SMs
Think of an SM as a single core on a CPU (do not buy into NVIDIA’s marketing)
Why is this important? Think of launching a job with 1 million threads. The more SMs you have, the more SPs…
512= 16 x 32
Components:
16+16 = 32 SPs
16 load/store units
4 SFU (for special functions)
2 warp schedulers
Several clock rates:
Shaders (SPs)
Scheduler: ½ the frequency of the SPs
Memory: own rate

## Slide 44: NVIDIA Volta GV100: microarchitecture schematic and nomenclature
21.1 billion transistors
GPC – 6 of them
  GPU Processing Cluster
TPC – 42 of them
  Texture Processing Cluster
SM – 84 of them
  Stream multiprocessor
A full GV100 has
  Six GPCs, each of which has
    Seven TCP, each with
      Two SMs
Notes: A full GV100 GPU has a total of:
5376 FP32 cores
5376 INT32 cores
2688 FP64 cores
672 Tensor Cores
336 texture units

## Slide 45: NVIDIA Volta GV100: microarchitecture schematic and nomenclature
Each SM has
  64 FP32 scalar processors (SPs)
  64 INT32 scalar processors (SPs)
  32 FP64 scalar processors (SPs)
  8 Tensor scalar processors (SPs)
  Four texture units
  It’s own L0 Instruction Cache
  A wrap scheduler
  A Dispatch unit
  16,384 registers
[NVIDIA]

## Slide 46: Ampere A100
[https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/]

## Slide 47: NVIDIA Ampere GA100: microarchitecture schematic & nomenclature [1/2]
Each SM partitioned into four processing blocks, called SM sub-partitions
Each sub-partition contains the following:
  Warp scheduler
  Register file
  Functional units
    Integer Execution units
    Floating Point Execution units
    Memory Load/Store units
    Special Function unit
    Tensor Cores
[NVIDIA]

## Slide 48: NVIDIA Ampere GA100: microarchitecture schematic & nomenclature [2/2]
There are several things shared amongst the four sub-partitions
  Unified L1 Data Cache / Shared Memory
  Texture units
  RT Cores, if available (RT: ray tracing)
[NVIDIA]

## Slide 49: Performance overview, last four NVIDIA GPU generations
This is what more transistors buys you
[NVIDIA]

## Slide 50
[https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/]

## Slide 51: Theoretical GFLOP/s
[NVIDIA]
Notes: Xeon E7-8800 v4: 0.844 TFLOPS

## Slide 52: High Speed Requires High Bandwidth
Assume that you want to add two arrays and reach 1 Tflops: 1E12 ops/second
You need to fetch/feed 2E12 operands per second…
Assume each number is stored using 4 bytes (float or integer)
You need to fetch 2E12*4 bytes in a second. This is 8E12 B/s, which is 8 TB/s…
You haven’t taken into account that you probably want to send back the outcome of the operation that you carry out
Today’s global memory bandwidth on the GPU: 1.555 TB/s
Notes: The solution is to keep data in registers (more about this later)
The bandwidth of accessing data from registers is exactly around 8 TB/s.
Here’s a set of rules that you need to keep in mind before going further…
Get the data on the GPU and keep it there
Give the GPU enough work to do (High arithmetic intensity)
Focus on data reuse within the GPU to avoid memory bandwidth limitations

## Slide 53: Bandwidth in a CPU-GPU System
53
System Memory
(256 GB)
GPU SMs
120
GB/s
16-32 GB/s
1555
GB/s
CPU Core
Cache L1: 32 KB
L2: 256 KB
L3: 45 MB (shared)
6GB/s
Infiniband to Next Node
BW:???
Latency:
High
[4-6 us]
Latency:
Medium
Latency:
Medium Low
Latency:
Very Low
Latency:
Rel.Low
NOTE: The width of the black lines is proportional to the bandwidth.
GPU Memory
(40 GB)
Notes: 53
Hammad – GPU numbers are for a Pascal P100, PCI numbers are for PCIe3
Infiniband is assuming mellanox results from here: http://www.mellanox.com/page/performance_infiniband
CPU memory numbers are for a E7 8890v3 http://ark.intel.com/products/84685/Intel-Xeon-Processor-E7-8890-v3-45M-Cache-2_50-GHz
CPU cache numbers are an average between expected L1 and L3 cache performance (not exact but approximate)

## Slide 54: Info on Previous Slide
GPU numbers are for an NVIDIA Ampere A100
PCI numbers are for PCIe3 (16 GB/s) or PCIe4 (32 GB/s)
Infiniband is assuming Mellanox results from here
CPU memory numbers are for a E7 8890v3, 2.5GHz, 45MB L3
CPU cache numbers: depends highly on cache level
  In theory, can be 1000 GB/s (again, depending on cache level)
  Question, for “good answer” badge: why is the BW in the memory mountain experiment so low, if caches are warm?

## Slide 55: Bandwidths, GPU computing w/ NVIDIA
[NVIDIA]
Notes: If you look at flop rates GPU/CPU, also about 5 (roughly like the bandwidth ratio)
Take away message: you can expect a speedup of 2-10 if moving to GPU. Do not expect 100x
Tesla P100 (Pascal): 720 GB/s (stacked memory)  short detour

## Slide 56: Speed-ups, GPU Computing: What’s reasonable to expect?
Since you have higher bandwidth on a GPU, it is likely that your code will run faster on the right problem
How much faster?
  Compare the bandwidth/latency of mem accesses on GPU and CPU
  Ball park: 4-5X speedup
  Depends *heavily* on the nature of the problem solved: ML jobs sped up by a lot more
Other things might come into play
  Caches and cache size, for instance
  The very nature of the problem you’re trying to solve
    Good for data parallelism, fine grain parallelism