## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 10
02/15/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Quote of the day
“Would I rather be feared or loved? Easy. Both. I want people to be afraid of how much they love me.”
-- Michael Scott, Regional Manager (Scranton, PA branch), Dunder Mifflin Inc.

## Slide 3
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 4: Before we get started…
Last time
  GPU computing: generalities
  GPU computing: execution configuration
Today
  GPU computing: scheduling execution
Other tidbits:
  Assignment due on Th, 02/18, at 9 pm
  Do not run your code on the Euler headnode (use Slurm)
  1/3 of the semester feedback

## Slide 5: 1/3 of lectures behind us. Your feedback makes a difference
A link to an anonymous google form emailed to you. Also, it’s here.
Please take 60 second to provide input:
  What works ok?
  How can Lijing, Ruochun, Colin and Dan tweak things for a better ME759 experience?
  Other comments
Why bother?
  Perhaps there are things that can be tweaked to improve the 759 experience

## Slide 6: Array Indexing Issues
Next three slides: revisit how multiple blocks are used together
  Fundamental question that a thread asks in GPU computing:
  What work, or which task, do I have to do?
First, recall this: there is a hard limit on the number of threads you can squeeze in a CUDA block – you can have up to 1024 threads
Note: In the vast majority of applications, you need to use many blocks (each of which contains the same number of threads, say ) to get a job done. Next example puts things in perspective

## Slide 7: Array Indexing Demo: The multi-block case
When working w/ multiple blocks – you will likely be using more than just threadIdx.x
  Consider indexing into an 1D array, one thread accessing one element
  Assume you have M=8 threads per block and the array is 32 entries long
With M threads per 1D CUDA block, the array index that a thread works on is:
int index = threadIdx.x + blockIdx.x * M;
0
1
7
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
threadIdx.x
threadIdx.x
threadIdx.x
threadIdx.x
blockIdx.x = 0
blockIdx.x = 1
blockIdx.x = 2
blockIdx.x = 3
[NVIDIA]→
[Important to grasp: shows thread-to-task mapping]
Notes: Made up example, where a block can only have 8 threads, but we want to process an array with 32 entries.
0 <= threadIdx.x <= 7
What thread works on entry 21?
Identical to finding offset in 1-dimensional storage of a 2-dimensional matrix:
int index = x + width * y;

## Slide 8: Example: Array Indexing
What is the array index that thread of index 5 in block of index 2 will work on?
int index = threadIdx.x + blockIdx.x * M;
= 5 + 2 * 8;
= 21;
0
1
7
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
threadIdx.x = 5
blockIdx.x = 2
M = 8
0
1
31
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
0
1
31
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
[NVIDIA]→
blockIdx.x = 1
blockIdx.x = 0
Notes: In general, the work of a thread is what you would have inside a for loop (but no need for the loop itself)!

## Slide 9: Recurring Theme in CUDA Programming [summarizing previous discussion, started after CUDA Example]
Imagine you are one of many threads; you have your thread index & block index
Two things need to be addressed
  You need to figure out the work, or the job, you need to take care of
    Just like we did on previous slide, where thread 5 in block 2 realized it needed to work on entry 21
  You have to make sure you actually need to do that work
    In many problems there are threads that need not do any work
    Example: you launch 2 blocks with 512 threads; your array is only 1000 elements long; 24 threads at the end might do nothing
      “24 threads at the end might do nothing” – depending on the implementation

## Slide 10: [short topic, two slides]: Timing Your Application
Timing support – part of the CUDA API
  You pick it up as soon as you include <cuda.h>
  Provides cross-platform compatibility
  Deals with the asynchronous nature of the device calls by relying on events and forced synchronization
Reports time in milliseconds, accurate within 0.5 microseconds
From NVIDIA CUDA Library Documentation:
  Computes the elapsed time between two events (in milliseconds with a resolution of around 0.5 microseconds). If either event has not been recorded yet, this function returns cudaErrorInvalidValue. If either event has been recorded with a non-zero stream, the result is undefined.

## Slide 11: Timing Example: timing a GPU call
#include<iostream>
#include<cuda.h>
int main() {
cudaEvent_t startEvent, stopEvent;
cudaEventCreate(&startEvent);
cudaEventCreate(&stopEvent);
cudaEventRecord(startEvent, 0);
yourKernelCallComesHere<<<NumBlk,NumThrds>>>(args);
cudaEventRecord(stopEvent, 0);
cudaEventSynchronize(stopEvent);
float elapsedTime;
cudaEventElapsedTime(&elapsedTime, startEvent, stopEvent);
std::cout << "Time to get device properties: " << elapsedTime << " ms\n";
cudaEventDestroy(startEvent);
cudaEventDestroy(stopEvent);
return 0;
}
Notes: RECALL: asynchronous execution on the GPU
You cannot use timing on the host! That would give you garbage.
Need cudaEventSynchronize to wait for that event to complete.
But we only need this for the stopEvent
Indeed, the CUDA operations on the GPU execute in order, so no need to “synchronize” the startEvent

## Slide 12: Cartoon of the day
[P. C. Vey]

## Slide 13
Execution Scheduling Issues
Notes: Understanding execution scheduling is important for performance (effectively using the hardware).
Knowing the underlying hardware is also important on the CPU (e.g. being aware of caching – as we will see in the OpenMP section). However, the compiler and tool development on the GPU is much more recent and more is left to the developer.

## Slide 14: [short/important topic]: Thread Index vs. Thread ID [critical in () understanding how SIMD is supported in CUDA, and () understanding the concept of “warp”]
Notes: Thread indices are a convenience to the programmer.
The actual threads are organized in a single, linear array of IDs.
This concept also very important in how threads are organized into warps.
Warps are important because the threads in a warp proceed in lock-step fashion (implications to thread divergence, etc.). Warps are the quantum unit of scheduling on an SM.
The index that runs faster is x, next y, slowest z.
For thread with thread index (4,2,3), the next one (for scheduling purposes) is thread with index (5,2,3)! Not (4,2,4)

## Slide 15: Thread Execution Scheduling
Starting point observation:
  You launch on the device many blocks, each containing many threads
Questions in this segment:
  In which order are these blocks executed?
  How is this execution process managed?
  When/How are the threads in a block executed?
  Etc…
Notes: Two relevant questions...
For larger problems you must launch multiple blocks (because of the 1024 thread/block limit). So how is a kernel split over multiple blocks executed?
For this discussion, recall the mapping between thread index and thread ID. At the end of the day, the SM’s scheduler sees the threads in a block based on their ID (i.e. a one-dimensional array: 0,1,2,…)

## Slide 16: High-level Perspective
There are two schedulers at work in GPU computing
  A device-level scheduler: assigns blocks to SM that signal that they have “excess capacity”
    This scheduler called by NVIDIA the “GigaThread engine”
  An SM-level scheduler: schedules the execution of the threads in a block onto the SM functional units
    This is the more interesting scheduler
Notes: We’ll talk more about the SM-level scheduler as it is more interesting and important

## Slide 17: Device-Level Scheduler
This is the first levels of scheduling:
  For running [desirably] a large number of blocks (thousands) on a relatively small number of SMs
  There are perhaps tens of thousands of blocks that will eventually get executed in 108 SMs (on an A100)
Thread Blocks are distributed to the SMs
  Potentially more than one block per SM
As Thread Blocks complete kernel execution, resources are freed
  Device level scheduler can launch next block(s) in line
Limits, for resident blocks/SM:
  32 blocks on the Pascal SM, Volta SM, and Ampere SM
Another hard limit: no more than 2048 threads can be hosted on an SM (no matter how many blocks the threads are associated with/coming from)
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Notes: Device-level schedules blocks for execution.
You cannot rely on order of block execution or assignment of blocks over SMs.
You can have 8 (Fermi) or 16 (Kepler) or 32 (recent) blocks resident on an SM

## Slide 18: The nitty-gritty: hardware resources dictate what a capability can do
[NVIDIA]

## Slide 19: Device-Level Scheduler, Comments
Once a block is picked up for execution by one SM, the block does not leave that SM before all threads in that block finish executing the kernel
Once a block is finished & retired, only then can another block land for execution on that SM
  The Device-Level Scheduler dispatches a block of threads to an SM that indicates that it has excess capacity
This explains why it’s good to have many SM in your GPU
  More SMs more expensive card

## Slide 20: More Recent SM Generations
Maxwell SMX
Pascal SM
Volta SM
Motivated by AI & Machine Learning
Notes: Pascal architecture indicates a move to a simpler datapath that requires less die area and lower power requirements.
But performance was not affected: smarter schedulers!
For example, Pascal can issue 32-bit operations (double precision) in a cycle.

## Slide 21: SM-Level Schedulers
Each block of threads divided in 32-thread warps
  “32”: selected by NVIDIA, programmer has no say
  Warp: A group of 32 threads of consecutive IDs
Warps are the basic scheduling unit on the SM
Limits, number of resident warps on an SM:
  64: on Kepler, Maxwell, Pascal, Volta, Ampere (i.e., 2048 resident threads)
  48: on Fermi (i.e., 1536 resident threads)
  32: on Tesla (i.e., 1024 resident threads)
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps
SP
SP
SP
21
Notes: Assume 2 blocks with 256 threads each.
So you have 512 threads that must be executed on a small number of SPs (32 on Fermi, 64 on Pascal).
How do they get a chance to execution?
The SM has 2 warp schedulers. What gets scheduled for execution on an SM are warps. So we must deal with 16 warps from 2 blocks.
Scheduling is done based on scoreboarding: each warp gets a score based on whether or not they have everything needed to execute (e.g. all operands, required SFU). The schedulers work at ½ the frequency of the SPs.

## Slide 22: Quiz
If it turns out that 3 blocks are processed by an SM and each Block has 256 threads, how many warps are managed by the SM?
  Each block of threads is divided into 256/32 = 8 warps
  There are 8 * 3 = 24 warps
  At any point in time, there are 24 warps that can be selected for execution
NOTE: the SM can handle 2048 threads, yet you have it handle only 768. Occupancy is low

## Slide 23: SM Warp Scheduling, more details
SM hardware implements almost zero-overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute same instruction
warp 8 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 35
warp 8 instruction 12
. . .
time
warp 3 instruction 36
Notes: Low overhead for changing context (unlike CPU)
This is because the context for each thread (e.g. registers) is already available (no need to pack/unpack this with the threads as done on the CPU).
Important to have many warps on an SM: better chance to find one that’s ready to be executed.
Note: on old cards (Tesla) there were only 8 SPs and one scheduler: 4 cycles needed for one instruction (for one warp). Fermi has 2 schedulers and 2x16 SPs that work at twice the frequency of the schedulers  1 instruction / cycle
This information is important because it can tell you how many warps are needed (for a particular code) to hide memory access latencies with useful computations. In this example: 34 warps minimum.
High arithmetic intensity  fewer warps needed to hide latencies.

## Slide 24: Fermi Specifics
There are two schedulers that issue warps of “ready-to-go” threads
One warp issued at each clock cycle by each scheduler
During no cycle can more than 2 warps be dispatched for execution on the SM’s functional units
Scoreboarding used to figure out which warp is ready
Fermi SM
Notes: 4 function units:
16 ALU/FPU (integer/single precision)
16 ALU/FPU (integer/single precision)
4 SFU (for special mathematical functions)
16 LDST (load/store)
For double precision: both 1 and 2 are used
Scoreboarding looks at:
instructions being fetched/decoded
necessary resources (operands ready? SFU required?)
what instruction modifies what register
Two warps with same score are selected oldest-first

## Slide 25: Quick Remarks
GPU architecture is pipelined
  At each clock cycle one instruction can be retired
However, ILP support is relatively limited
To the best of my knowledge:
  Fermi has no out-of-order execution smarts
  There is no prefetching
  There is no speculative execution
Note:
  The odd warp index and handled by a scheduler, the even ones are handled by the other scheduler
    No trading warps at run time between schedulers
    Pic makes this point too

## Slide 26: Example, establishing Flop/s performance level: Fermi
Scheduler works at 607 MHz
Functional units work at 1215MHz
Question:
  What is the peak flop rate of GTX480?
  15 SMs * 32 SPs * 1215 * 2 (Fused Multiplied Add) = 1166400 Mflops
  That is, 1.166 Tflops, single precision

## Slide 27: Fermi Specifics
As shown in picture, at no time can we see more than 2 warps being dispatched for execution during a cycle
Note that at any given time we might have more than two functional units working though (which is actually very good, device kept busy)
T i m e
Past
Present
Functional units
Notes: Because there are 2 schedulers: at most 2 instructions are dispatched for execution in a cycle.
But you can have more of them being executed at any given time! Indeed, an SFU for example needs 4 cycles to complete. Other warps that do not require them can be executing on other FUs (ALU, FPU, LDST)

## Slide 28: FP32 & INT32 instructions can be carried out at the same time
The A100 SM includes separate FP32 and INT32 scalar processors
  Similar to Tesla V100 and Turing GPUs
Allows simultaneous execution of FP32 and INT32 operations at full throughput
Also increases instruction issue throughput
Good how:
  Many applications have inner loops that perform pointer arithmetic (integer memory address calculations) combined with floating-point computations that will benefit from simultaneous execution of FP32 and INT32 instructions
  Each iteration of a pipelined loop can update addresses (INT32 pointer arithmetic) and load data for the next iteration while simultaneously processing the current iteration in FP32
  You don’t have “structural hazards” (recall ILP discussion)
[NVIDIA]

## Slide 29: SM Architecture Specifications (data below refers to ONE SM)
[Wikipedia]→
Fermi
Pascal
Volta
Kepler
Maxwell
Turing
Ampere
Notes: Note: Volta will move back to 4 schedulers per SM
Pascal: compute capability 6.0

## Slide 30: Technical Specifications and Features
[Wikipedia]→
Notes: Recall: compute capability is an expression of the hardware generation.

## Slide 31: Organizing Threads into Warps
Thread IDs within a warp are consecutive and increasing
  Related to the 1D projection from thread index to thread ID
  Recall: in multidimensional blocks, the x thread index runs fastest, then y, then z
  Threads with IDs (0...31) combine into warp 0, threads (32…63) into warp 1, etc.
Partitioning of threads into warps is always the same
  You can use this in control flow
  Warp size has always been 32 and is unlikely to change soon
While you can rely on ordering among threads, DO NOT rely on any ordering among warps
  Warp scheduling is not under user control in CUDA
Notes: In other words, thread with ID 67 will always be in warp 2. You can use that!
(What you probably will use is that thread IDs 66 and 67 are in the same warp)
But you cannot count on, say, warp 1 to be always scheduled before warp 2!

## Slide 32: Threads are Organized & Executed as Warps
Each thread block split into one or more warps
If thread block size is not multiple of warp size, unused lanes go wasted
  Example: block w/ 50 threads – 64 lanes, of which last 14 lanes go wasted
The hardware schedules each warp independently
Warps within a thread block execute independently
Warp of 32 threads
Warp of 32 threads
Block of 128 threads
Warp of 32 threads
Warp of 32 threads
NVIDIA [J. Balfour]→
Notes: A block of 128 threads, color-coded in 4 colors (4 warps).
The warps are scheduled as a unit.
It is not required to have the block size a multiple of 32, but it’s a good idea!

## Slide 33: Why many warps in flight is a good thing
An SM can switch between warps with almost no overhead
Warps with instruction whose inputs are ready are eligible to execute, and will be considered when scheduling
When a warp is selected for execution, all [active] threads execute the same instruction in lockstep fashion
Wn
Executing Wn
Waiting for data
Ready to execute
W1
W2
W3
W4
[NVIDIA, J. Balfour]→
(pre-Volta only; this limitation lifted w/ Volta)
Notes: Why is it good to have many warps?
If you need a memory transaction, these take hundreds of cycles.
You need eligible warps to be executed while others wait for data (white areas)
Hiding memory latency with useful computation
Note: more warps not always better!

## Slide 34: The interplay between warps & warp-scheduler
Warps in one of three states
  Active Warps (deployed on an SM)
  Eligible Warps (a subset of the Active Warps)
  Issued Warps (a subset of the Eligible Warps)
On cycles with no eligible warps, the issue slot is skipped and no instruction is issued
  Having many skipped issue slots indicates poor latency hiding
What makes a warp “eligible”?
  Next instruction is decoded
  All input dependencies resolved
    That is, the operands it needs are available
  The function unit is needs is available

## Slide 35: What causes a warp to stall? [1/2]
“stalling”: no new instruction issued at a clock cycle
  Bubble in the pipeline
Preamble: a warp always runs on one of the four sub-partitions. It does not change sub-partitions during execution
Each sub-partition holds up to 16 warps
  Per SM: max 64 warps max 2048 threads
[NVIDIA]

## Slide 36: What causes a warp to stall? [2/2]
What stalls a warp?
  An instruction fetch
    Next instruction not available (super sad!!!)
  A memory dependency
    Result of memory instruction, e.g., load
  An execution dependency
    Result of previous instruction (recall data hazard in pipelining)
  A synchronization barrier (more later)
    E.g., __syncthreads()
[NVIDIA]

## Slide 37: The “wave”
The collection of all blocks in flight on the GPU at one time is called a “wave”
Note that not all blocks are in flight
sum of all threads in flight at a given time is called

## Slide 38: Execution Configuration, revisiting the concept
Prefer thread block sizes that result in mostly full warps
Bad: kernel<<<N, 1>>> ( ... )
Okay: kernel<<<(N+31) / 32, 32>>>( ... )
Better: kernel<<<(N+127) / 128, 128>>>( ... )
Many threads per block provide SM with many warps to switch between
  This is how the GPU hides memory access latency
Resource like amount of ShMem & size of RegFile may constrain number of threads per block
NVIDIA [J. Balfour]→
Notes: Do not launch N blocks each with 1 thread!
OK, but not great, to have 32 threads in 1 block (that’s only 1 warp)
Best: Use 128, 256 threads/block
But maximum number of threads in a block is limited by shared memory (for example – see later). That would limit the number of blocks resident on an SM. This may reduce occupancy.
The moral of the story: algorithms may need to be changed for parallel computing, maybe to something that would be ridiculous to do on a sequential architecture!
We will see this on matrix multiplication with shared memory

## Slide 39: Scheduling: Summing It Up…
When host invokes a kernel grid, the blocks of the grid are enumerated and distributed to SMs with available execution capacity
Number of resident blocks on one SM
  Up to 8 blocks (on Fermi)
  Up to 16 on Kepler & Turing
  Up to 32 on Maxwell, Pascal, Volta , Ampere
When a block of threads is executed on an SM, its threads are grouped in warps. The SM manages several warps at the same time
  Up to 48 warps can be managed by an SM on Fermi
  Up to 64 warps can be managed on Kepler, Maxwell, Pascal, Volta, Ampere
  Up to 32 warps can be managed on Turing
When a thread block finishes, a new block is launched on the vacated SM

## Slide 40
Thread Divergence
[pre-Volta]
Notes: New topic related to execution scheduling

## Slide 41: Thread divergence issues
Consider the following code:
__global__ void odd_even(int n, int* x)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
if( (i & 0x01) == 0 )
{
x[i] = x[i] + 1;
}
else
{
x[i] = x[i] + 2;
}
}
Half the threads (even i) in the warp execute the if clause, the other half (odd i) the else clause
NVIDIA [J. Balfour]→
Notes: 0x01: all bits are 0 except the very least significant one.
When i is even, the “if” gets hit; when i is odd, the “else” side gets hit
Neighboring threads do different things  the threads inside a warp diverge
This requires two cycles: it’s as if the number of instructions was doubled

## Slide 42: Thread Divergence in “if-then-else”
Handling of an if-then-else construct in CUDA
  First, a subset of threads of the warp execute one branch
    Execution moves forward for these threads in lockstep fashion
  Next, the rest of the threads in the warp execute the other branch
    Execution moves forward for these threads in lockstep fashion
After the if-then-else statement all threads of the warp move on in lockstep fashion

## Slide 43: Thread divergence issues
The system automatically handles control flow divergence, conditions in which threads within a warp execute different paths through a kernel
Often, this requires that the hardware execute multiple paths through a kernel for a warp
  For example, both the if clause and the corresponding else clause
NVIDIA [J. Balfour]→
Notes: A switch statement may have similar effects.
This results in longer times required to advance the warp

## Slide 44: Thread divergence issues
__global__ void kv(int* x, int* y)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
int t;
bool b = f(x[i]);
if( b )
{ // g(x)
t = g(x[i]);
}
else
{ // h(x)
t = h(x[i]));
}
y[i] = t;
}
NVIDIA [J. Balfour]→
Notes: Some threads in the warp follow the if branch. The rest are idle.
Some threads in the warp follow the else branch. The rest are idle.

## Slide 45: Thread divergence issues
Nested branches are handled similarly
  Deeper nesting results in more threads being temporarily disabled
In general, one does not need to consider divergence when reasoning about the correctness of a program*
  Certain code constructs, such as those involving schemes in which threads within a warp spin-wait on a lock, can cause deadlock
In general, one does need to consider divergence when reasoning about the performance of a program
NVIDIA calls execution model SIMT (Single Instruction Multiple Threads) to differentiate from actual SIMD where threads really are in lockstep
NVIDIA [J. Balfour]→
Notes: You do not need to understand this to write code that runs correctly. The system handles this.
You need to worry about this for code that is performant.
Thread divergence is why NVIDIA calls their execution model SIMT. Subtle difference from SIMD: SIMT is SIMD for as long as the threads in a warp execute in lockstep mode; slightly different when threads diverge.

## Slide 46: Performance of Divergent Code (1/2)
Performance decreases with degree of divergence in warps
Here’s an extreme example…
__global__ void dv(int* x)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
switch (i % 32)
{
case 0 : x[i] = a(x[i]);
break;
case 1 : x[i] = b(x[i]);
break;
...
case 31: x[i] = v(x[i]);
break;
}
}
NVIDIA [J. Balfour]→
Notes: There are different levels of thread divergence.
This extreme example requires a minimum of 32 cycles.

## Slide 47: Performance of Divergent Code (2/2)
Compiler and hardware can detect when all threads in a warp branch in the same direction
  Example: all take the if clause, or all take the else clause
  The hardware is optimized to handle these cases without loss of performance
    if (threadIdx.x / WARP_SIZE >= 2) { }
  Creates two different control paths for threads in a block
  Branch granularity is a whole multiple of warp size; all threads in any warp follow the same path. No warp divergence…
The compiler can also compile short conditional clauses to use predicates (bits that conditionally convert instructions into null ops)
  Avoids some branch divergence overheads and is more efficient
  Often acceptable performance with short conditional clauses
NVIDIA [J. Balfour]→
Notes: Note:
the presence of an if/else statement in a kernel function is not a problem by itself.
thread divergence concerns only divergence of threads within a warp!
Even for threads diverging inside a warp, in special situations (short sequences), the compiler can modify the code to remove thread divergence: all threads in a warp execute the same instructions, but some of those are replaced by the compiler with no-ops which do not write memory or registers.  acceptable penalty hit

## Slide 48
See forum post here:
https://devtalk.nvidia.com/default/topic/1031723/cuda-programming-and-performance/warp-divergence-triggered-by-for-loop/post/5249002/?offset=3#5249003

## Slide 49: Thread divergence, VOLTA and more recent
Volta GV100 is the first GPU to support independent thread scheduling, which enables finer-grain synchronization and cooperation between parallel threads in a program
Consequence
  Greater flexibility in thread cooperation, leading to higher efficiency for fine-grained parallel algorithms

## Slide 50: Handling thread divergence, pre-Volta (Pascal and before)
Pascal and earlier NVIDIA GPUs execute groups of 32 threads (warps) in SIMT
The Pascal warp uses a single program counter shared amongst all 32 threads, combined with an active mask that specifies which threads of the warp are active at any given time
Loss of concurrency means that threads from the same warp in divergent regions or different states of execution cannot signal each other or exchange data
  This is because some threads are not active; as such, they cannot signal each other
[NVIDIA]

## Slide 51: Warp Execution Model of Volta and later GPUs
Volta was first GPU architecture to enable equal concurrency between all threads, regardless of warp
Volta maintains execution state (PC and S) per thread, see pic at the right
  Can do so, since there’re “only” 2048 threads
Up to Pascal: one PC and one S per warp
  PC: program counter
  S: call stack
[NVIDIA]

## Slide 52: The “schedule optimizer” hardware asset
To maximize parallel efficiency, Volta includes a “schedule optimizer” which determines how to group active threads from the same warp together into SIMT units
Threads can now diverge and re-converge at sub-warp granularity
While the scheduler supports independent execution of threads, it optimizes non-synchronizing code to maintain as much convergence as possible
  “convergence optimizer” still groups together threads that execute the same code to run them in parallel

## Slide 53: Handling thread divergence, Volta/Turing/Ampere
Instructions from the if and else branches can now be interleaved in time, as shown in the pic.
  NOTE: what’s shown in the pic is one possibility. How the scheduling takes place depends on the code being executed and be different than what shown in the pic
IMPORTANT: execution is still SIMT – at any given clock cycle, the same instruction is executed for all active threads in a warp just as before Volta
  NOTE: this is why the “schedule optimizer” tries to converge all threads
    If all converged, the 32 threads get to execute an instruction. Otherwise, only a subset of threads get to execute an instruction
Why bother with understanding this?
  Ability to independently schedule threads within a warp makes it possible to implement complex, fine-grained algorithms and data structures in a more natural way
[NVIDIA]

## Slide 54: Handling thread divergence, Volta/Turing/Ampere
Note that instruction Z is not executed by the same warp threads at the same time
Call CUDA 9 warp synchronization function syncwarp() to force reconvergence (lower pic)
  The divergent portions of the warp might not execute Z together, but all execution pathways from threads within a warp will complete before any thread reaches the statement after the syncwarp()
Placing the call to syncwarp() before the execution of Z would force reconvergence before executing Z, potentially enabling greater SIMT efficiency if the developer knows that this is safe for their application
[NVIDIA]

## Slide 55: Don’t panic yet…
[Robert Mankoff]

## Slide 56
The NVIDIA GPU Memory Ecosystem

## Slide 57: Fermi: Global Memory
Up to 6 GB of “global memory” on Fermi, see pic below
  Kepler goes up to 12 GB, Pascal up to 16 GB, Volta up to 32 GB, Ampere up to 40 GB
“Global” in the sense that it doesn’t belong to an SM but rather all SMs can access it
Notes: DDR5 memory blocks, external to the SMs.
SMs must “reach out” to global memory
L2 cache is also shared among all SMs. The rest of the memory hierarchy is inside each SM

## Slide 58: CUDA Memory Ecosystem, high vantage point [Note: picture assumes two blocks, each with two threads]
Image shows the memory hierarchy that a block sees while running on an SM
Each thread can:
  R/W per-thread registers
  R/W per-thread local memory
  R/W per-block shared memory
  R/W per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
  Read only per-grid surface memory
Host can R/W global, constant, and texture* memory
  *: texture can be written only as “surface” mem
IMPORTANT NOTE: Global, constant, and texture memory spaces are persistent between kernels called by the same host application.
[UIUC]
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
One SM
Another SM
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.
“surface” memory is like “texture”, except that the former can be written (“texture” can only be read)

## Slide 59: What “register” means in CUDA
Any variable that you are using in a kernel eats up a register
  The variable that you use, it needs to “live” somewhere
Then every single variable you use in a kernel will burn (at some point in the execution flow) a register
  NOTE: even a variable stored in ShMem, for it to be operated on, it’ll eat up a register* at some point in the execution
As execution advances through a kernel, the number of registers occupied keeps changing
  What’s relevant: max number of registers required during the execution of the kernel
*: except on Ampere, where one can actually control this…

## Slide 60: Live registers

## Slide 61: Programmer View of Register File
Number of 32 bit registers in one SM:
  8K registers in each SM in G80
  16K on Tesla
  32K on Fermi
  64K on Kepler and Maxwell, Pascal, Volta, and Ampere
Registers are dynamically partitioned across all Blocks assigned to the SM
Once assigned to a Block, these registers are NOT accessible by threads in other Blocks
A thread in a Block can only access registers assigned to itself
  IMPORTANT: A thread can have assigned by the compiler up to 255 registers
4 blocks
3 blocks
Possible per-block partitioning scenarios of the RF available on the SM

## Slide 62: Register related: a “level of parsimony” issue
Size of a register: 4 bytes
Is it that if you use a char in a kernel, then you don’t use a full register but rather ¼ of it?
Not really, unfortunately; i.e., there is no parsimony in usage of a register
  Any data type that requires less then or equal to 4 bytes eats up a register
    One char thus eats up an entire register
  If you use a double, it eats up two registers
Notes: See also https://devtalk.nvidia.com/default/topic/491309/int-vs-short-vs-char-in-kernels/

## Slide 63: From the left field…
Q: Who do you think controls/decides the register allocation when executing a kernel?
A: The compiler

## Slide 64: The Concept of Local Memory [“local”: misnomer]
Physically, local memory does not exist
  In reality, data stored in “local memory” is placed in cache or the global memory at run time or by the compiler
What gets stored in local memory?
  Register spill, if too many registers are needed for computation (“high register pressure”)
  The stack of the thread
Quick observations:
  “Local” means that it’s got local scope; i.e., it’s specific to one thread and not visible to any other thread
  Local memory has the same latency as global memory, unless cached
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 65: Caches & the Shared Memory
Fermi
  Each SM: 64 KB L1 cache & shared memory
  All SMs tap into a common 768 KB L2 cache memory
Pascal:
  Each SM: Unified 24 KB L1 cache
  Each SM: 64 KB shared memory
  All SMs tap into 4096 KB of L2 cache memory
Volta:
  L1 cache + Shared Mem = 128 KB per SM
  One can carve out of 128KB shared memory as follows:
    0 KB, 8 KB, 16 KB, 32 KB, 64 KB, or 96 KB
  What is not taken by the ShMem becomes L1 cache:
    128 KB, 120 KB, 112 KB, 96 KB, 64 KB, 32 KB
  All SMs tap into 6144 KB of L2 cache memory
IMPORTANT: Numbers reported are per SM
Fermi SM
Notes: The previous plot is bandwidth for moving data from/to global memory.
Each SM has local L1 cache (shared with shared memory, ratio under user control).
Fermi default: 48 KB shared / 16 KB L1 cache (can also do16/48)
Kepler: 48/16, 32/32, 16/48
Difference: shared memory is controlled by the user. L1 cache use is automatic. If you do not use shared memory, increase the chunk for L1 cache to allow the hardware to leverage it.

## Slide 66: Ampere A100 specific, Cache and Shared Memory aspects
Data cache/Share mem combo: 192 KB/SM in A100 (versus 128 KB/SM in V100)
SECDED ECC protection for L2 cache, as well as the L1 caches and register files inside all SMs
New asynchronous copy instruction loads data directly from global memory into shared memory, optionally bypassing L1 cache, and eliminating the need for intermediate register file (RF) usage
[NVIDIA Ampere whitepaper]

## Slide 67: Global, Constant, and Texture Memories
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Global memory
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
Texture and Constant Memories
  Constants initialized by host
  Contents visible to all threads
Global, texture and constant memories are accessible by host
  Done at high latency, low bandwidth
[NVIDIA]
NOTE: We will not emphasize texture in ME759.

## Slide 68: Memory Access Times
Register – dedicated HW on chip - single cycle NOTE: you don’t have control over this
Shared Memory – dedicated HW on chip – a few cycles NOTE: physically, like L1 cache
Local Memory – DRAM, (if not in cache - *slow*; if cached – relatively fast)
Global Memory – DRAM, no cache - *slow*; cached, is fast…
Constant Memory – DRAM, cached, 10s…100s of cycles, depending on cache locality
Texture Memory – DRAM, cached, 10s…100s of cycles, depending on cache locality
Instruction Memory (invisible) – DRAM, cached
Notes: Take away message: organize your code to use as much as possible the faster memory:
keep in mind the relative access times (some of these change with new hardware)
be careful how you organize data and what data you bring over (do not duplicate information)
Recall:
GPUs have much larger register files than a CPU
64K registers (each one word, i.e. 32 bits) per SM on Pascal
But you can also have up to 2048 threads resident per SM
So you end up with just 32 registers per thread!
In fact, NVIDIA sets an upper limit of 255 registers/thread

## Slide 69: Storage Locations
Memory | Location | Cached | Access | Who
Register | On-chip | N/A | Read/write | One thread only
Shared | On-chip | N/A | Read/write | All threads in a block
Global | Off-chip | Yes | Read/write | All threads + host
Constant | Off-chip | Yes | Read | All threads + host
Texture | Off-chip | Yes | Read | All threads + host
Off-chip means on the GPU but not on the SM, which translates into high latency.
Notes: Back in the day (Tesla C1060): global memory was not cached

## Slide 70: Putting things in perspective: The 3 most important GPU memory spaces
Register: per-thread basis
  Private per thread
  Can spill into local memory (potential performance hit unless cached)
Shared Memory: per-block basis
  Shared by threads of the same block
  Used for: intra-block inter-thread communication
Global Memory: per-application basis
  Available for use by all threads
  Used for: global access, all threads
  Also used for inter-grid communication
Thread
Register
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 71: Example: Matrix Multiplication, Revisited
Purpose
  See an example where the use of multiple blocks of threads plays a central role
  Highlight the use/role of the shared memory
  Point out the __syncthreads() function call
NOTE: A one dimensional array stores the entries in the matrix
Notes: Here we will use a bus instead of a bunch of cars to bring over data from memory.
Savings come from the fact that bandwidth to accessing shared memory is ~10 better than global memory.
Thread synchronization becomes crucial to avoid race conditions

## Slide 72: A Critique of the Old Matrix Multiplication Example
One row of M is loaded N.width times
This happens for each row of M
Moral of the story: the matrix M is loaded N.width times
One column of N is loaded M.height times
This happens for each column of N
Moral of the story: the matrix N is loaded M.height times
Loading M and N over and over → not a good idea, memory transactions are expensive
Grid 1
Block 1
48
Thread
(2, 2)
width
M
P
N

## Slide 73: Why Revisit the Old Example?
In the naïve first implementation the ratio of arithmetic computation to memory transaction (“arithmetic intensity”) very low
  Each arithmetic computation required one fetch from global memory
  The entries in M are copied from global memory to the device N.width times
  The entries in N are copied from global memory to the device M.height times
No brownie points for moving data around
  Hundreds of cycles required for bringing data from global memory
  When solving a problem, the goal is to go through the machine instructions in your executable, not to wait for data to come your way
Notes: Data reuse is the goal

## Slide 74: Answering the question: “Could/Should I use Shared Memory?”
Figuring out whether you should use share mem
  Imagine you are a thread executing the code in the kernel
  If the data that you, as a thread, use can also be used by another thread in your block, then you should consider using shared memory
Note: regardless of the above test, you can use shared memory as scratch pad memory
  Don’t let it go wasted, use for storing often-used variables even if they’re not used by multiple threads

## Slide 75: A Common CUDA Programming Pattern: Tiling w/ Shared Memory
Global memory access - much slower when compared to shared memory access
No brainer: Use shared memory, if possible
  Partition data into data subsets (tiles) that each fits into shared memory
  Handle each data subset (tile) with one thread block by:
    Loading the tile from global memory into shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the tile from shared memory; each thread can efficiently multi-pass over any data element of the tile
Notes: Recall: global memory: DRAM Shared memory: SRAM (split with L1 - Fermi or dedicated - Pascal)
Focus on data reuse
Introduce the concept of tiling (common programming pattern)

## Slide 76: Tiling used for Matrix-Matrix multiplication
One block computes one square sub-matrix Csub of size Block_Size
tx
A
B
C
Csub
Block_Size
wB
wA
Block_Size
Block_Size
ty
Block_Size
Block_Size
Block_Size
hA
wA
NOTE: A similar technique is used on CPUs to improve cache hits. See slide “Blocking Example” at
http://cseweb.ucsd.edu/classes/fa10/cse240a/pdf/08/CSE240A-MBT-L15-Cache.ppt.pdf
One thread computes one entry of Csub
Assumption: A and B are square matrices and their dimensions of are multiples of Block_Size
  Doesn’t have to be like this, but keeps example simpler and focused on the concepts of interest
  In this example work with Block_Size=16x16
Notes: We will have a first loop over tiles (moving left in A, moving down in B)
Then, inside a tile (i.e. a block), each thread will loop over a row in the A tile and a column in the B tile to calculate a piece of its final value (the red square in C)

## Slide 77: A Block of 16 X 16 Threads
Notes: We will have 256 (16x16) threads that will work in concert on a tile
They will bring together (in shared memory) one tile from A and one tile from B
Then, they each work separately on calculating an increment for their assigned C[i,j]
But they do so by sharing data!

## Slide 78
// Thread block size
#define BLOCK_SIZE 16
// Forward declaration of the device multiplication func.
__global__ void Muld(float*, float*, int, int, float*);
// Host multiplication function
// Compute C = A * B
// hA is the height of A
// wA is the width of A
// wB is the width of B
void Mul(const float* A,const float* B,int hA,int wA,int wB, float* C)
{
// Load A and B to the device
float* Ad;
int size = hA * wA * sizeof(float);
cudaMalloc((void**)&Ad, size);
cudaMemcpy(Ad, A, size, cudaMemcpyHostToDevice);
float* Bd;
size = wA * wB * sizeof(float);
cudaMalloc((void**)&Bd, size);
cudaMemcpy(Bd, B, size, cudaMemcpyHostToDevice);
// Allocate C on the device
float* Cd;
size = hA * wB * sizeof(float);
cudaMalloc((void**)&Cd, size);
// Compute the execution configuration *assuming*
// the matrix dimensions are multiples of BLOCK_SIZE
dim3 dimBlock(BLOCK_SIZE, BLOCK_SIZE);
dim3 dimGrid( wB/dimBlock.x , hA/dimBlock.y );
// Launch the device computation
Muld<<<dimGrid, dimBlock>>>(Ad,Bd,wA,wB,Cd);
// Read C from the device
cudaMemcpy(C, Cd, size, cudaMemcpyDeviceToHost);
// Free global memory
cudaFree(Ad);
cudaFree(Bd);
cudaFree(Cd);
}
Notes: Execution configuration:
blocks must all have 16x16 = 256 threads (take advantage of 2D layout)
how many blocks do we need? simple under our assumption that the matrix dimensions are multiples of the tile size
if not, more complicated (some tiles will “fall off” the matrix extent) this is messy and main part of frustration in CUDA computing

## Slide 79
Notes: bx = blockIdx.x the B (and C) matrix sub-block column index
by = blockIdx.y the A (and C) matrix sub-block row index
aBegin = wA * (by*BLOCK_SIZE) index of the first sub-matrix of A processed by the block
aEnd = aBegin + wA – 1
aStep = BLOCK_SIZE
bBegin = BLOCK_SIZE * bx;
bStep = BLOCK_SIZE * wB

## Slide 80
// Shared memory for the sub-matrices (tiles) of A and B
__shared__ float As[BLOCK_SIZE][BLOCK_SIZE];
__shared__ float Bs[BLOCK_SIZE][BLOCK_SIZE];
// Loop over all the sub-matrices (tiles) of A and B required to
// compute the block sub-matrix; moving in A left to right in
// a row, and in B from top to bottom in a column
for (int a = aBegin, b = bBegin;
a <= aEnd;
a += aStep, b += bStep) {
// Load tiles from global memory into shared memory; each
// thread loads one element of the two tiles from A & B
As[ty][tx] = A[a + wA * ty + tx];
Bs[ty][tx] = B[b + wB * ty + tx];
// Synchronize to make sure the matrices are loaded
__syncthreads();
// Each thread in this block computes one element
// of the block sub-matrix (tile). Thread with indexes
// ty and tx computes in this tile the entry [ty][tx].
for (int k = 0; k < BLOCK_SIZE; ++k)
Csub += As[ty][k] * Bs[k][tx];
// Synchronize to make sure that the preceding
// computation is done before loading two new
// sub-matrices of A and B in the next iteration
__syncthreads();
}
// Write the block sub-matrix to global memory;
// each thread writes one element
int c = wB * BLOCK_SIZE * by + BLOCK_SIZE * bx;
C[c + wB * ty + tx] = Csub;
}
// Device multiplication function called by Mul()
// Compute C = A * B
// wA is the width of A
// wB is the width of B
__global__ void Muld(float* A, float* B, int wA, int wB, float* C)
{
// Block index
int bx = blockIdx.x; //the B (and C) matrix sub-block column index
int by = blockIdx.y; //the A (and C) matrix sub-block row index
// Thread index
int tx = threadIdx.x; //the column index in the sub-block
int ty = threadIdx.y; //the row index in the sub-block
// Index of the first sub-matrix of A processed by the block
int aBegin = wA * BLOCK_SIZE * by;
// Index of the last sub-matrix of A processed by the block
int aEnd = aBegin + wA - 1;
// Step size used to iterate through the sub-matrices of A
int aStep = BLOCK_SIZE;
// Index of the first sub-matrix of B processed by the block
int bBegin = BLOCK_SIZE * bx;
// Step size used to iterate through the sub-matrices of B
int bStep = BLOCK_SIZE * wB;
// The element of the block sub-matrix that is computed
// by the thread
float Csub = 0;
Notes: if __shared__ does not appear: each thread sets aside 16x16 memory locations for As and 16x16 for Bs
that’s already double what could ever be in registers  spills to local memory
with __shared__ this memory is specific to the block and shared between all threads in the block!
attention: all threads bring over disjoint pieces of data
Why do we need the __syncthreads here? Only threads in the same warp proceed in lock-step fashion. But threads in different warps do not.
Who gets synchronized? Threads in the same block
Would it make sense to have a Cs in shared memory? No – recall the “test for using shared memory”; no other thread needs this information

## Slide 81: Synchronization Function
Synchronization accomplished through a device lightweight function
  void __syncthreads();
Synchronizes all threads in a block (acts as barrier for all block threads)
  Does not synchronize threads from two blocks
One more condition for execution to commence once all threads in a block reached the sync point:
  All global & shared mem. transactions made by these threads prior to __syncthreads() are visible to all block threads
  Used to avoid RAW/WAR/WAW hazards when accessing shared or global memory (more later)
Notes: Attention: do not put a __syncthreads in an if statement unless you can guarantee all threads in the block go through there!

## Slide 82: [warning] __syncthreads() & thread divergence
Be very cautious when using a __syncthreads() in a conditional
The actual behavior is not clear
  Some difference between the Programming Guide and what happens in reality
See here for discussion of how/when code deadlocks:
  https://stackoverflow.com/questions/6666382/can-i-use-syncthreads-after-having-dropped-threads
  https://stackoverflow.com/questions/15146886/conditional-syncthreads-deadlock-or-not
#include<cuda.h>
#include<iostream>
__global__ void badIdeaSynchronization(int* data)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
if ((i & 0x01) == 0)
{
data[i] = data[i] + i; // if not odd, come here
}
else
{
data[i] = data[i] + 2 * i; // come here if you're odd
__syncthreads();
}
}
int main()
{
const int numElems = 4;
int hostArray[numElems], *devArray;
//allocate memory on the device (GPU); zero out all entries in this device array
cudaMalloc((void**)&devArray, sizeof(int) * numElems);
cudaMemset(devArray, 0, numElems * sizeof(int));
//invoke GPU kernel, with one block that has four threads
hangs<<<1, numElems >>>(devArray);
//bring the result back from the GPU into the hostArray
cudaMemcpy(&hostArray, devArray, sizeof(int) * numElems, cudaMemcpyDeviceToHost);
//print out the result to confirm that things are looking good
std::cout << "Values stored in hostArray: " << std::endl;
for (int i = 0; i < numElems; i++)
std::cout << hostArray[i] << std::endl;
//release the memory allocated on the GPU
cudaFree(devArray);
return 0;
}

## Slide 83: 3 Ways to Set Aside Shared Memory
First way: Statically, declared inside a kernel
  See matrix multiplication example w/ shared memory use
Second way: Through the execution configuration
  Ns below indicates size (in bytes) to be allocated in shared memory
__global__ void MyFunc(float*) // __device__ or __global__ function
{
extern __shared__ float shMemArray[];
// Size of shMemArray determined through the execution configuration
// You can use shMemArray as you wish here…
}
// invoke like this
MyFunc<<< Dg, Db, Ns >>>(parameter);
Third way: Dynamically, via CUDA Driver API
  Advanced feature, uses API function cuFuncSetSharedSize(), not discussed here