## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 25
03/22/2021
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2: Quote of the day
“The happiness of your life depends upon the quality of your thoughts. Therefore, guard accordingly, and take care that you entertain no notions unsuitable to virtue and reasonable nature.”
-- Marcus Aurelius, Roman Emperor 161 to 180 CE

## Slide 3: Quote of the day, same dude
“Never let the future disturb you. You will meet it, if you have to, with the same weapons of reason which today arm you against the present.”
-- Marcus Aurelius, Roman Emperor 161 to 180 CE

## Slide 4: Some Roman Emperors
Trajan (98–117 CE)
Hadrian (117–138 CE)
Antoninus Pius (138–161 CE)
Marcus Aurelius (161–180 CE)
Nice piece of Engineering, bridge across Danube
Nice thinking, this one
Nice novel about this one

## Slide 5
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.

## Slide 6: Before we get started…
Last time
  Critical thinking, and similar tricks for speeding up your code
    Know your hardware; help the compiler help you; optimization blockers: function calls and use of pointers
Today
  Wrapping up, “Critical thinking” segment
    Case study
Other tidbits:
  Assignment due on Th, 03/25, at 9 pm
  Final Project *Proposal*, due tonight at 9 pm. Post related questions on Piazza
    Details about the proposal are here
    The template for the two-page proposal is here
  Big ME759 PDF is here
  Do not run your code on the Euler head-node (use Slurm)

## Slide 7: New Example, with three actors: one struct + two functions
/* data structure for vectors */
typedef struct {
size_t len;
data_t *data;
} vec;
Our struct will use various Data Types
  Use different declarations for data_t:
    int
    long
    float
    double
[15-213 @ CMU]
len-1
len
data
0
1
/* retrieve vector element and store in val */
void get_vec_element(vec* v, size_t idx, data_t *val) {
if (idx < 0 || idx >= v->len)
*val = 0;
else
*val = v->data[idx];
}
The first function that comes into play
This is “the” struct that comes into play

## Slide 8: Wrapping up the setup, for the new example
Data Types
  Use different declarations for data_t
    int
    long
    float
    double
Operations (OP)
  Use different definitions of OP and IDENT
    “+” : 0
    “*” : 1
Compute sum or product of vector elements (based on OP)
[15-213 @ CMU]
void combine1(vec_ptr v, data_t *dest) {
*dest = IDENT; // the identity value for OP
for (int i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
The second function that comes into play

## Slide 9: Cycles Per Element (CPE)
Assume a program operates on vectors or lists
  Vector Length = n
Assume we’re interested in sweep over the vector
  Number of OPs is n (n-1, to be correct)
Thus, cycles per OP cycles per element (CPE)
Sweep, total # of cycles: C = CPE*n + Overhead
  CPE is slope of line
    Depends on the type of data handled
  See figure
[15-213 @ CMU]
Chart: n Elements
| 0 | 193 | 120 | 91 | 95 | 196 | 97 | 181 | 91 | 83 | 43 | 183 | 140 | 146 | 94 | 134 | 163 | 131 | 110 | 182 | 189 | 112 | 141 | 185 | 188 | 47 | 130 | 102 | 59 | 174
psum1 | 2112.6 | 1451.1 | 1188.6 | 1218 | 2131.5 | 1247.4 | 2003.4 | 1190.7 | 1117.2 | 758.1 | 2020.2 | 1629.6 | 1686.3 | 1211.7 | 1568.7 | 1841.7 | 1543.5 | 1358.7 | 2011.8 | 2066.4 | 1373.4 | 1635.9 | 2032.8 | 2058 | 787.5 | 1539.3 | 1285.2 | 905.1 | 1938.3
psum1i | 367.79 | 2107.43 | 1449.43 | 1188.03 | 1224.09 | 2134.47 | 1242.12 | 1999.27 | 1188.03 | 1115.92 | 755.38 | 2017.29 | 1629.7 | 1683.79 | 1215.07 | 1575.62 | 1837.02 | 1548.58 | 1359.29 | 2008.28 | 2071.37 | 1377.32 | 1638.72 | 2035.32 | 2062.36 | 791.43 | 1539.57 | 1287.18 | 899.6 | 1936.17
psum2 | 1535.1 | 1100.4 | 921.9 | 940.8 | 1545.6 | 949.2 | 1455.3 | 917.7 | 865.2 | 623.7 | 1467.9 | 1209.6 | 1253.7 | 936.6 | 1173.9 | 1352.4 | 1150.8 | 1029 | 1461.6 | 1509.9 | 1039.5 | 1215.9 | 1478.4 | 1505.7 | 642.6 | 1152.9 | 987 | 732.9 | 1419.6
psum2i | 367.66 | 1531.11 | 1091.05 | 916.23 | 940.34 | 1549.2 | 952.4 | 1458.77 | 916.23 | 868.01 | 626.87 | 1470.83 | 1211.62 | 1247.79 | 934.32 | 1175.45 | 1350.27 | 1157.36 | 1030.77 | 1464.8 | 1507 | 1042.82 | 1217.64 | 1482.89 | 1500.97 | 650.99 | 1151.33 | 982.54 | 723.33 | 1416.58
psum1
Slope = 9.0
(double prec.)
psum2
Slope = 6.0
(int)
Notes: CPE – amount of average effort, per element, to see the sweep through

## Slide 10: Benchmark Performance
Sweep to compute sum or product of vector elements
Method | data_t: Integer |  | data_t:Double FP | 
Operation (OP) | add | mult | add | mult
combine1 unoptimized | 22.68 | 20.02 | 19.98 | 20.18
combine1 with –O1 | 10.12 | 10.12 | 10.17 | 11.14
combine1 with –O3 | 4.5 | 4.5 | 6 | 7.8
Results in CPE (cycles per element) – Smaller is BETTER!
[15-213 @ CMU]
void combine1(vec_ptr v, data_t *dest) {
*dest = IDENT; // the identity value for OP
for (int i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
!

## Slide 11: Basic Optimizations
Modification #1: vec_length moved out of loop
  One function call avoided at each iteration
Modification #2: bypassed get_vec_element call
Modification #3: Accumulate in temporary “temp”
[15-213 @ CMU]
void combine4(vec_ptr v, data_t *dest) {
int length = vec_length(v);
data_t *d = get_vec_start(v);
data_t temp = IDENT;
for (int i = 0; i < length; i++)
temp = temp OP d[i];
*dest = temp;
}
Shortcut: you get the raw pointer, and index into it… No need to call get_vec_element
No function call here anymore

## Slide 12: Effect of Basic Optimizations
Eliminates overhead in for loop & it can do prefetching
Method | Integer |  | Double FP | 
Operation | add | mult | add | mult
combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
combine4 | 1.27 | 3.01 | 3.01 | 5.01
[15-213 @ CMU]
void combine4(vec_ptr v, data_t *dest) {
int length = vec_length(v);
data_t *d = get_vec_start(v);
data_t temp = IDENT;
for (int i = 0; i < length; i++)
temp = temp OP d[i];
*dest = temp;
}

## Slide 13: Opportunities for Efficiency Gains
We have little to no control 
We have full control 
Superscalar
Non-sequence instructions sharing functional units
Pipelining
Sequence of instruction sharing functional units
Vectorization
Higher operation throughput via special/fat registers
Multi-Core Processor
Communication through shared caches and main mem.
Acceleration (GPU/Phi)
Compute devices accelerating parallel computation on one node
Multi-Socket Node
Group of CPUs on the same node, talk through main mem.
Cluster (distributed mem.)
Group of nodes communicate through fast interconnect
MPI, Charm++, Chapel
OpenMP, MPI
CUDA, OpenCL, OpenMP
OpenMP, TBB, pthreads
AVX, SSE
Assembly
Assembly
Little, but might pack a punch!

## Slide 14: [Next thing to consider:] Exploiting Instruction-Level Parallelism
Simple ILP-targeted transformations can yield good performance improvements
  Compilers often cannot make these transformations since they don’t know if it’s safe to do so or not
ILP
  Hardware can execute multiple instructions in parallel
  Performance limited by ILP hazards

## Slide 15: Curbing our enthusiasm, ILP hazards
Structural hazards
  The scheduler: “Unfortunately, there aren’t enough hammers in this plant”
Data dependency hazards
  The scheduler: “This next instruction depends on the outcome of the instruction right ahead of it”
Control hazards
  The scheduler: “I’m not sure what is supposed to happen next”

## Slide 16: Modern CPU Design [old slide]
[15-213 @ CMU]
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 17: Recall ILP discussion, 1.5 months ago: superscalar attribute
Superscalar processor: one that can issue more than one instruction in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically
Superscalar processor: one manifestation of the instruction level parallelism idea
Note: Most modern CPUs are superscalar
  Intel: since Pentium (1993)
[15-213 @ CMU]

## Slide 18: Old ILP discussion: the pipelining attribute
Stage 1
Stage 2
Stage 3
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage s can start on new computation once values passed to s+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
  Note when p1*p2 is issued – classical data dependency situation
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2
int mult_example(int a, int b, int c) {
int p1 = a * b;
int p2 = a * c;
int p3 = p1 * p2;
return p3;
}

## Slide 19: Example: The Intel Haswell CPU – aspects that are ILP relevant
  Haswell: 8 Total Functional Units
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer ops (doing address arithmetic too – explains why you have more)
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Its Latency (in cycles) Its Issue (in cycles)
  Load / Store 4 1
  Integer Add 1 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Add 3 1
  Single/Double FP Multiply 5 1
  Single/Double FP Divide 3-15 3-15
[15-213 @ CMU]
For this type of info: see Agner Fog's optimization manual (part of “ME759 assigned reading” list)

## Slide 20: x86-64 Compilation of combine4 function
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | add | mult | add | mult
combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
[15-213 @ CMU]

## Slide 21: combine4 = Serial Computation
Computation, assume length=8:
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
You have sequential dependence
  Performance: determined by latency of OP
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7
[15-213 @ CMU]
Assume OP multiplication ()

## Slide 22: First trick: Loop Unrolling (2x1)
Perform 2x more useful work per iteration
[15-213 @ CMU]
void unroll2a_combine(vec_ptr v, data_t *dest) {
int length = vec_length(v);
int limit = length - 1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
int i;
// Combine 2 elements at a time
for (i = 0; i < limit; i += 2) {
x = (x OP d[i]) OP d[i + 1];
}
// Finish any remaining elements
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}

## Slide 23: Effect of Loop Unrolling
Helps integer add
  Achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | add | mult | add | mult
combine4 | 1.27 | 3.01 | 3.01 | 5.01
unroll2a | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
[15-213 @ CMU]

## Slide 24: Loop Unrolling with Reassociation (2x1a)
void unroll2aa_combine(vec_ptr v, data_t *dest) {
int length = vec_length(v);
int limit = length - 1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
int i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i += 2) {
x = x OP(d[i] OP d[i + 1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
Can this change the result of the computation?
Yes, for FP. Why?
x = (x OP d[i]) OP d[i+1];
Compare to before
[15-213 @ CMU]

## Slide 25: Effect of Reassociation
Nearly 2x speedup for “INT ”, “FP +”, “FP ”
  Reason: Breaks sequential dependency
  Why is that? (next slide)
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | add + | mult. | add + | mult.
combine4 | 1.27 | 3.01 | 3.01 | 5.01
unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Method | Integer |  | Double FP | 
Operation | add + |  | add + | 
combine4 | 1.27 | 3.01 | 3.01 | 5.01
unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 func. units for “FP ”
2 func. units for load
4 func. units for “INT +”
2 func. units for load
[15-213 @ CMU]

## Slide 26: Reassociated Computation
What changed:
  Ops in the next iteration can be started early (no dependency)
  Prefetching kicks in
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);
[15-213 @ CMU]

## Slide 27: Loop Unrolling with Separate Accumulators (2x2)
Different form of reassociation
[15-213 @ CMU]
void unroll2a_combine(vec_ptr v, data_t *dest) {
long length = vec_length(v);
long limit = length - 1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
// Combine 2 elements at a time
for (i = 0; i < limit; i += 2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i + 1];
}
// Finish any remaining elements
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}

## Slide 28: Effect of Separate Accumulators
“INT +” makes use of two load units
2x speedup (over unroll2) for “INT *”, “FP +”, “FP *”
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Unroll 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
[15-213 @ CMU]

## Slide 29: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/op
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?
[15-213 @ CMU]

## Slide 30: Unrolling & Accumulating
Idea
  Can unroll to any degree L
  Can accumulate K results in parallel
  L must be multiple of K
Limitations
  Diminishing returns
    Cannot go beyond throughput limitations of execution units
  Large overhead for short lengths
    Finish off iterations sequentially
[15-213 @ CMU]

## Slide 31: Unrolling & Accumulating: Floating Point Multiplication
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators
[15-213 @ CMU]

## Slide 32: Unrolling & Accumulating: Integer Addition
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Accumulators
[15-213 @ CMU]

## Slide 33: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, un-optimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best | 0.54 | 1.01 | 1.01 | 0.52
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
[15-213 @ CMU]

## Slide 34: Vector instructions
Basic idea: Use fat registers to perform the same operation on all variables stored in register
X86 has, for instance, 512 bit-wide registers
  Technology called AVX512
Since chip in this example is Haswell, it only has 256-bit registers
  Technology called AVX2

## Slide 35: Programming with AVX2, YMM Registers related
16 such registers, each 32 bytes (i.e., 256 bits wide)
What can you do with them?
  Store 8 32-bit integers:
  Store 8 single-precision floats:
  Store 4 double-precision floats:
  Store 1 single-precision float but then waste bits:
  Store 1 double-precision float but then waste bits:

## Slide 36: SIMD Operations, with AVX2
  SIMD Operations: Single Precision
  SIMD Operations: Double Precision
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
%ymm0
%ymm1
vaddsd %ymm0, %ymm1, %ymm1
+
+
+
+
+
+
+
+
[15-213 @ CMU]

## Slide 37: Using Vector Instructions
This is where we are now
Additional speedup owing to use of AVX Instructions
  Parallel operations on multiple data elements
  The “mips” in OpenMP
CPE: From 22.68 to 0.06: 378X speed increase
Method | Integer |  | Double FP | 
Operation | add | mult | add | mult
Scalar Best | 0.54 | 1.01 | 1.01 | 0.52
Vector Best | 0.06 | 0.24 | 0.25 | 0.16
Latency Bound | 0.50 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Vec Throughput Bound | 0.06 | 0.12 | 0.25 | 0.12
[15-213 @ CMU]
This is where we started

## Slide 38: Supplemental Material: Branch Prediction (another ILP trick)
Challenge
  Instruction Control Unit must work ahead of Execution Unit to generate enough operations to keep EU busy
  When encounters conditional branch, cannot reliably determine where to continue fetching
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
Executing
How to continue?
[15-213 @ CMU]

## Slide 39: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates
[15-213 @ CMU]

## Slide 40: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
Branch Taken
Branch Not-Taken
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
[15-213 @ CMU]

## Slide 41: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data (draws on RAT & ROB, see later)
Predict Taken
Begin
Execution
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
[15-213 @ CMU]

## Slide 42: Branch Prediction Through Loop
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Read invalid location
Executed
Fetched
[15-213 @ CMU]

## Slide 43: Branch Misprediction Invalidation
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Invalidate
[15-213 @ CMU]

## Slide 44: Branch Misprediction Recovery
Performance Cost
  Multiple clock cycles on modern processor
  Can be a major performance limiter
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401036: jmp 401040
. . .
401040: vmovsd %xmm0,(%r12)
i = 99
Definitely not taken
Reload
Pipeline
[15-213 @ CMU]

## Slide 45: Branch Prediction Numbers
Default behavior:
  Backwards branches are often loops so predict taken
  Forwards branches are often if so predict not taken
Predictors average better than 95% accuracy
  Most branches are already predictable.
Bonus material:
  http://stackoverflow.com/questions/11227809/why-is-processing-a-sorted-array-faster-than-an-unsorted-array
[15-213 @ CMU]

## Slide 46: Short trip: actors, the “speculative execution” trick [it’s tricky]
“instruction issue phase” vs. “instruction retirement phase”: two different animals
ROB: reorder buffer
  At issue time, an instruction is assigned an entry at the tail of the ROB. It’s there while in flight, before being committed
RAT: register alias table
  RAT needed because of “register renaming”, which is a technique that abstracts logical registers from physical registers
    Every logical register has a set of physical registers associated with it
    The physical registers are opaque and cannot be referenced directly but only via the canonical names
The interplay between ROB and RAT allows an unwinding of the instructions without compromising the state of the program (since things were not committed yet)
Resources: see here and here, it takes 7 mins total.

## Slide 47: Looking back at examples, what we did to improve performance
  Used good compiler and the right flags
  Helped the compiler get optimization going (e.g., use “restrict” keyword on pointer arguments)
  Exploited instruction-level parallelism

## Slide 48: Parallel Computing with the Message Passing Interface (MPI)
Notes: DAN: NEXT TIME YOU DO MPI, GO READ https://computing.llnl.gov/tutorials/mpi/

## Slide 49: Acknowledgments
Parts of the MPI material covered draws on slides made available by Irish Centre for High-End Computing (ICHEC)
  The ICHEC material was based on the MPI course developed by Rolf Rabenseifner at the High-Performance Computing-Center Stuttgart (HLRS), University of Stuttgart in collaboration with the EPCC Training and Education Centre, Edinburgh Parallel Computing Centre, University of Edinburgh
Slides have been changed, which probably explains any inaccuracies in the material

## Slide 50: ME759: where we are right now
Behind us: OpenMP & CUDA
  Commodity parallel computing (eight cores, or one GPU, etc.)
Next segment: the non-commodity parallel computing
  Reliance on supercomputers
We will focus on the Message Passing Interface (MPI) standard
  MPI: The software environment that makes supercomputers tick
  MPI is for supercomputers what CUDA is for the GPU and OpenMP for the multi-core chip

## Slide 51: Opportunities for Efficiency Gains
We have little to no control 
We have full control 
Superscalar
Non-sequence instructions sharing functional units
Pipelining
Sequence of instruction sharing functional units
Vectorization
Higher operation throughput via special/fat registers
Multi-Core Processor
Communication through shared caches and main mem.
Acceleration (GPU/Phi)
Compute devices accelerating parallel computation on one node
Multi-Socket Node
Group of CPUs on the same node, talk through main mem.
Cluster (distributed mem.)
Group of nodes communicate through fast interconnect
MPI, Charm++, Chapel
OpenMP, MPI
CUDA, OpenCL, OpenMP
OpenMP, TBB, pthreads
AVX, SSE
Assembly
Assembly
Any ILP issues that we can address?
Hitting the cache?
Any opportunities for vectorization?
Do the threads work together harmoniously?
Any NUMA issues to be aware of?
Communication/synchronization reduced as much as possible?
What is left at this point 

## Slide 52: Supercomputers, example

## Slide 53: Frontier, exascale AMD supercomputer, to be released 2021
1.5 Exaflops of DP arithmetic; first exascale computer
$600 million contract from Department of Energy to AMD
Built off AMD’s EPYC CPUs, each connected to four Radeon Instinct GPUs
  Instinct GPU: BW – 1228 GB/s; Flops/s – 11.5 Tflops (DP); Technology - 7 nm; 300W; PCIe-4.0
Size of two basketball courts (7300 square feet)
90 miles of cables
Drawing 30 MWatts

## Slide 54: Overview of Large Multiprocessor Hardware Configurations (“supercomputers”)
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fourth edition
Euler
Notes: For the Microprocessor this is measured in MIPS (million instructions per second). Many reported IPS values have represented "peak" execution rates on artificial instruction sequences with few branches, whereas realistic workloads typically lead to significantly lower IPS values.

## Slide 55: Nomenclature Issues
Shared address space: when you invoke address “0x0043fc6f” on one machine and then invoke “0x0043fc6f” on a different machine they actually point to the same global memory space
  Issues: memory coherence
    Fix: software-based or hardware-based
Distributed address space: the opposite of the above
Symmetric Multiprocessing (SMP): you have one machine that shares amongst all its processing units a certain amount of memory (same address space)
  Mechanisms should be in place to prevent data hazards (RAW, WAR, WAW). Raises the issue of memory coherence
Distributed shared memory (DSM) – aka distributed global address space (DGAS)
  Although physically memory is distributed, it shows as one uniform memory
  Memory latency is highly unpredictable; depends on where in memory your data is stored

## Slide 56: Example
Distributed-memory multiprocessor (MP) architecture
  Euler, for instance
56
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Notes: Hammad – Updated Figure from fifth edition

## Slide 57: Comments, distributed-memory multiprocessor architecture
Basic architecture consists of nodes containing a processor, some memory, typically some I/O, and an interface to an interconnection network that connects all nodes
Individual nodes may contain a small number of processors, which may be interconnected by a small bus or a different interconnection technology, which is less scalable than the global interconnection network
  As of last five years or so, a node has a certain number of GPUs, typically 4 or 8
Popular interconnection network: Mellanox and Qlogic InfiniBand
  Bandwidth range: 1 through 200 Gb/sec (about 25 GB/s)
  Latency: in the microsecond range (1E-6 to 1E-7 second); i.e., relatively high
  Requires special network cards: HCA – “Host Channel Adaptor”

## Slide 58
Supercomputers: Where Are We Today? [Info lifted from Top500 website: http://www.top500.org/]
Notes: 58

## Slide 59: How is a supercomputer’s speed measured?
How is the speed measured to put together the Top500?
  Test based on how fast you can solve a dense linear system

## Slide 60
Supercomputers: What setup employed?
60
Abbreviations/Nomenclature
  MPP – Massively Parallel Processing
  Constellation – subclass of cluster architecture envisioned to capitalize on data locality
2018
1998
Notes: Hammad – Updated with newer plots
60

## Slide 61: Supercomputers: Where Are We Today? [Cntd.]
Abbreviations/Nomenclature
  MPP – Massively Parallel Processing
  Constellation – subclass of cluster architecture envisioned to capitalize on data locality
  MIPS – “Microprocessor without Interlocked Pipeline Stages”, a chip design of the MIPS Computer Systems of Sunnyvale, California
  SPARC – “Scalable Processor Architecture” is a RISC instruction set architecture developed by Sun Microsystems (now Oracle) and introduced in mid-1987
  Alpha - a 64-bit reduced instruction set computer (RISC) instruction set architecture developed by DEC (Digital Equipment Corporation was sold to Compaq, which was sold to HP) – adopted by Chinese chip manufacturer
Notes: Hammad – Updated with newer plots

## Slide 62: Nomenclature: What is an MPP? How’s it different from a cluster?
MPP: A very large-scale computing system with commodity processing nodes interconnected with a custom-made high-bandwidth low-latency interconnect
  A cluster is an MPP for which the manufacturer forgot to put a high-bandwidth low-latency interconnect
Memories are physically distributed
Nodes often run a microkernel
  Perhaps this is a second difference, a cluster might run some rather pedestrian Linux distro
Rather blurred line between MPPs and clusters
Example:
  Euler (our machine) is a cluster
  An IBM BG/Q machine is an MPP (because of the interconnect)

## Slide 63: Supercomputers: Any acceleration?
Top 500: What accelerators do they use?

## Slide 64: Shared Memory Hardware Systems
Memory is shared; i.e., visible to all processors and threads
  Typical scenario, on a budget: one node with four CPUs, each with 16 cores
  Typically one node systems; i.e., a workstation or a laptop
Example:
  Symmetric Multi-Processors (SMP) – like one node of Euler
    Each processor has equal access to RAM
    There are custom solutions that have a software layer that makes the physically distributed memory appear to the program as one unified pool of logical memory
      Popular at some point, not so much anymore

## Slide 65: SMS vs. Distributed Memory Systems (DMS)
CPU
CPU
CPU
CPU
Memory
Interconnect
Shared Memory System
CPU
Memory
CPU
Memory
CPU
Memory
CPU
Memory
Interconnect
Distributed Memory System

## Slide 66: Distributed Memory Hardware Systems: The Virtual Memory Angle
Typically, parallelism on supercomputers accomplished by interplay between different *processes* and not threads
Consequence: each process sees its own virtual memory, there’s no overlap
More tedious to write programs for distributed memory systems since the programmer must keep track of memory usage

## Slide 67: Bandwidths in a multi-node, CPU-GPU System
System Memory
GPU cores
50-100
GB/s
8-16 GB/s
900
GB/s
CPU Core
Cache
6GB/s
Infiniband to Next Node
80GB/s
Latency:
High
Latency:
Medium
Latency:
Medium Low
Latency:
Low
Latency:
Pretty Low
NOTE: The width of the black lines is proportional to the bandwidth.
GPU Memory
GPU accelerator
This is important over the next two lectures
The typical node, connected to other nodes in a supercomputer
Notes: 67
Hammad – GPU numbers are for a Volta V100, PCI numbers are for PCIe3
Infiniband is assuming mellanox results from here: http://www.mellanox.com/page/performance_infiniband
CPU memory numbers are for a E7 8890v3 http://ark.intel.com/products/84685/Intel-Xeon-Processor-E7-8890-v3-45M-Cache-2_50-GHz
CPU cache numbers are an average between expected L1 and L3 cache performance (not exact but approximate)

## Slide 68: A “High Performance Computing” Digression
High Performance Computing, to an expert, has a very precise meaning: supercomputing
  HPC entails the idea of a bunch of nodes linked through fast interconnect trying to solve together one big problem
This class “759: High Performance Computing for Applications in Engineering”
  High performance computing: you compute at the bounds (bandwidth bound or compute bound)
The terms in blue and red: same syntax, different semantics
  A way of computing vs. an attribute of a program

## Slide 69: High Performance Computing (HPC) vs. High Throughput Computing (HTC)
High Performance Computing
  The idea: run one executable as fast as you can
    Might spend one month running one DFT job or a week on a CFD job…
High Throughput Computing
  The idea: run many executables at the same time on different machines
  Example: bone analysis in ABAQUS
    You have uncertainty in the length of the bone (20 possible lengths) in the material of the bone (10 values for Young’s modulus) in the loading of the bone (50 force values with different magnitude/direction) . Grand total: 10,000 ABAQUS runs
    We have 1400 workstations hooked up together on-campus -> use Condor to schedule the 10,000 independent ABAQUS jobs and have them run on scattered machines overnight

## Slide 70: High Performance Computing (HPC) vs. High Throughput Computing (HTC)
High Performance Computing
  Usually one cluster (e.g. Euler) or one massively parallel machine (e.g. IBM Blue Gene or Cray) that is dedicated to running one large application that requires a lot of memory, a lot of compute power, and a lot of communication
    Example: each particle in a MD simulation requires (due to long range electrostatic interaction) to keep track of a large number of particles that it interacts with. Needs to query and figure out where these other particles are at any time step of the numerical integration
  What is crucial is the interconnect between the processing units
    Typically some fast dedicated interconnect (e.g. InfiniBand), which operates at 40 GB/s
      Euclid@UW-Madison: 1 GB/s Ethernet, Bluewaters@UIU/C: 100 GB/s, Tianhe-I claims double the speed of Infiniband
  Typically uniform hardware components: e.g. 100,000 Intel Xeon 5520, etc.
  Expensive
HPC: this interconnect expected to be fast…

## Slide 71: High Performance Computing (HPC) vs. High Throughput Computing (HTC)
High Throughput Computing
  Usually a collection of heterogeneous compute resources linked through a slow connection, most likely Ethernet
    Example: 120 Windows workstations in the CAE labs (all sorts of machines, some new, some old)
  When CAE machine 58 runs an ABAQUS bone simulation there is no communication needed with CAE machine 83 that runs a different ABAQUS scenario
  Don’t need to spend any money, you can piggyback on resources willing to make themselves available
  Very effective to run Design of Experiments type analyses
This interconnect
might be slow
Any two nodes might have very
different setups/assets

## Slide 72: High Performance Computing (HPC) vs. High Throughput Computing (HTC)
You can do HPC on a configuration that has slow interconnect
  It will run very, very slow…
Conversely, you can do HTC on an IBM Blue Gene
  You will use the processors but will waste the fast interconnect that made the machine expensive in the first place
  You need to have the right licensing system in place to “check out” 10,000 ABAQUS licenses
University of Wisconsin-Madison well known due to pioneering work in the area of HTC
  Professor Miron Livny in CS
  UW-Madison solution for HTC: Condor, used by a broad spectrum of organizations from academia and industry