## Slide 1
ME759 High Performance Computing for Applications in Engineering [Spring 2021]
Lecture 18
03/05/2021
1
Dan Negrut, 2021 ME759 UW-Madison

## Slide 2
Quote of the day
1
"There is a wonderful, almost mystical, law of nature that says three of the things we want most—happiness, freedom, and peace of mind—are always attained when we give them to others. Give it away to get it back.“
-- John Wooden (1910-2010), UCLA basketball coach, winner of ten NCAA national championships in a 12-year period

## Slide 3
Is BBC recording on?
If my internet connection goes down, I’ll email from my phone to provide more information – go/no-go, next step, etc.
3

## Slide 4
Before we get started…
Last time
  A three-stop journey noted in the evolution of the CUDA memory model
    Z-C accesses on the host; the UVA milestone; the unified memory model that allowed to use of managed memory
Today
  GPU computing, from a distance (via thrust & CUB)
Other tidbits:
  Assignment due on Th, 03/11, at 9 pm
  Assignment is tough; it’ll get better soon
  Do not run your code on the Euler head-node (use Slurm)
  Big PDF file contains all the slides thus far; easy to search into it to find topics covered thus far. Doc is here.
  Pushing Final Project discussion into Monday
4

## Slide 5
GPU Computing with thrust
4

## Slide 6
Three Ways to Accelerate on GPU
4
Libraries
Directives
Programming Languages
Some Application
[built on top of]
Easier to Use
Opportunities for Performance Gains
NVIDIA [C. Woolley]→
Notes: On the NVIDIA website, Thrust is listed under “Libraries” (https://developer.nvidia.com/gpu-accelerated-libraries).
69

## Slide 7
Acknowledgments
4
The thrust slides include material provided by Nathan Bell previously of NVIDIA (at Google now)
Modified here and there, responsible for inaccuracies

## Slide 8
Design Philosophy, thrust
thrust aims to balance two competing aspects in programming
  Increase programmer productivity
    Build applications quickly via generic programming
      Leverage a template-based approach
  Do not sacrifice (or sacrifice as little as possible of) execution speed
    Efficient leveraging of GPU hardware
NVIDIA [N. Bell]→

## Slide 9
What is thrust?
A template library for parallel computing on GPU and CPU*
  Mimics the C++ STL
Heavy use of C++ containers
  BTW, this is the one lecture where C++ comes into play heavily
Provides ready to use generic algorithms
  Sorting, reduction, scan, etc.
NVIDIA [N. Bell]→

## Slide 10
thrust: used how?
10
thrust is a header library
  All its functionality accessed by #include-ing the appropriate thrust header file
Program is compiled with nvcc as per usual, no special tools are required
Uses the GPU, but that is transparent to the user
  The concepts of execution configuration, shared memory, occupancy, blah, blah, blah: all but gone
  The lib is only callable on the host-side, using C++ flavored code
NVIDIA [N. Bell]→

## Slide 11
Work Plan, thrust
Namespaces, containers, iterators
Algorithms
General transformations. Zipping & fusing
Thrust example: Processing rainfall data
10

## Slide 12
Namespaces
10
Avoid name collisions: thrust vs. std namespaces
// allocate host memory
thrust::host_vector<int> h_vec(10);
// call STL sort
std::sort(h_vec.begin(), h_vec.end());
// call Thrust sort
thrust::sort(h_vec.begin(), h_vec.end());
// for brevity
using namespace thrust;
// without namespace
int sum = reduce(h_vec.begin(), h_vec.end());
NVIDIA [N. Bell]→
Notes: You’ll notice that we use things like thrust::host_vector or thrust::copy in our examples. The thrust:: part tells the C++ compiler that we want to look inside the thrust namespace for a specific function or class. Namespaces are a nice way to avoid name collisions. For instance,thrust::copy is different from std::copy provided in the STL. C++ namespaces allow us to distinguish between these two copy functions.
69

## Slide 13
thrust containers: host_vector & device_vector
thrust provides two vector containers: host_vector and device_vector
  host_vector is stored in host memory
  device_vector lives in GPU device memory
thrust’s vector containers are just like std::vector in the C++ STL
  Like std::vector, host_vector & device_vector are generic containers – they store whatever
10
[NVIDIA]

## Slide 14
thrust containers: host_vector & device_vector
Common operations become concise & readable through use of containers
// allocate host vector with two elements
thrust::host_vector<int> h_vec(2);
// copy host vector to device
thrust::device_vector<int> d_vec;
// manipulate device values from the host
d_vec[0] = 13;
d_vec[1] = 27;
std::cout << "sum: " << d_vec[0] + d_vec[1] << std::endl;
// copy host vector to device
h_vec = d_vec;
// vector memory automatically released w/ free() or cudaFree()
14
Notes: Thrust provides two vector containers, host_vector and device_vector.
the = operator can be used to copy a host_vector to a device_vector (or vice-versa). The = operator can also be used to copy host_vector to host_vector or device_vector to device_vector.
note that individual elements of a device_vector can be accessed using the standard bracket notation. However, because each of these accesses requires a call to cudaMemcpy, use sparingly. We’ll look at some more efficient techniques later.
14

## Slide 15
thrust containers
Compatible with STL containers (thrust & std containers play well together)
  Below, a std list plays well with a thrust device vector
// list container on host
std::list<int> h_list;
h_list.push_back(13);
h_list.push_back(27);
// copy list to device vector
thrust::device_vector<int> d_vec(h_list.size());
thrust::copy(h_list.begin(), h_list.end(), d_vec.begin());
// alternative method using vector constructor
thrust::device_vector<int> d_vec2(h_list.begin(), h_list.end());
NVIDIA [N. Bell]→
14
Notes: Another reason to distinguish between iterators and pointers is that iterators can be used to traverse many kinds of data structures. For example, the STL provides a linked list container (std::list) that provides bidirectional (but not random access) iterators. Although Thrust does not provide device implementations of such containers, it is compatible with them.
This eases integration
15

## Slide 16
Iterators: think of them as pointers
Sequences are defined by pairs of iterators
  See more about iterators in the context of vector containers here
For vector containers, iterators act like pointers
  They can be used like pointers (e.g. incremented)
  Can be converted to raw pointers
16
// allocate device vector
thrust::device_vector<int> d_vec(4);
d_vec.begin(); // returns iterator at first element of d_vec
d_vec.end(); // returns iterator one past the last element of d_vec
d_vec.end()
d_vec.begin()
Notes: In the case of vector containers, which are really just arrays, iterators can be thought of as pointers to array elements. Therefore, H.begin() is an iterator that points to the first element of the array stored inside the H vector. Similarly, H.end() points to the element one past the last element of the H vector.
15

## Slide 17
Interoperability: iterators to pointers
16
Convert iterators to raw pointers
// allocate device vector
thrust::device_vector<int> d_vec(4);
// obtain raw pointer to device vector’s memory
int * ptr = thrust::raw_pointer_cast(&d_vec[0]);
// use ptr in a CUDA C kernel
my_kernel<<< (N+255) / 256, 256 >>>(N, ptr);
// use ptr in a CUDA API function
cudaMemcpy(ptr, ... );
NVIDIA [N. Bell]→
Notes: To extract a raw pointer from a device_ptr the raw_pointer_cast should be applied
15

## Slide 18
Interoperability: pointers to iterators
17
Wrap raw pointers with device_ptr
// raw pointer to device memory
int * raw_ptr;
cudaMalloc((void **) &raw_ptr, N * sizeof(int));
// wrap raw pointer with a device_ptr
thrust::device_ptr<int> dev_ptr(raw_ptr);
// use device_ptr in thrust algorithms
thrust::fill(dev_ptr, dev_ptr + N, (int) 0);
// access device memory through device_ptr
dev_ptr[0] = 1;
// free memory
cudaFree(raw_ptr);
NVIDIA [N. Bell]→
Notes: Like the STL, Thrust permits using a “raw” pointer as an argument to a Thrust function and it will dispatch the host path of the algorithm.
If the pointer in question is in fact a pointer to device memory then you’ll need to wrap it with thrust::device_ptr before calling the function.
15

## Slide 19
Example: UM and thrust
18
#include <ostream>
#include <cmath>
#include <thrust/reduce.h>
#include <thrust/system/cuda/execution_policy.h>
#include <thrust/system/omp/execution_policy.h>
const int ARRAY_SIZE = 1000;
int main(int argc, char **argv) {
double* mA;
cudaMallocManaged(&mA, ARRAY_SIZE * sizeof(double));
thrust::sequence(mA, mA + ARRAY_SIZE, 1); // sequence of increasing numbers, from 1 to ARRAY_SIZE
double maximumGPU = thrust::reduce(thrust::cuda::par, mA, mA + ARRAY_SIZE, 0.0, thrust::maximum<double>());
cudaDeviceSynchronize();
double maximumCPU = thrust::reduce(thrust::omp::par , mA, mA + ARRAY_SIZE, 0.0, thrust::maximum<double>());
std::cout << "GPU reduce: " << (std::fabs(maximumGPU - ARRAY_SIZE) < 1e-10 ? "Passed" : "Failed") << std::endl;
std::cout << "CPU reduce: " << (std::fabs(maximumCPU - ARRAY_SIZE) < 1e-10 ? "Passed" : "Failed") << std::endl;
cudaFree(mA);
return 0;
}

## Slide 20
Namespaces, containers, iterators: closing remarks
Namespaces
  Used to avoids collisions and increase functionality
Containers
  Manage both host & device memory
  Automatic allocation and deallocation
  Simplify data transfers
Iterators in thrust
  Behave like pointers pointing in an array
  Can move back-and-forth between iterators and raw pointers
20

## Slide 21
Work Plan, thrust
Namespaces, containers, iterators
Algorithms
General transformations. Zipping & fusing
Thrust example: Processing rainfall data
20

## Slide 22
Algorithms
Element-wise operations
  for_each, transform, gather, scatter …
Reductions
  reduce, inner_product, reduce_by_key …
Prefix Sums [scans]
  inclusive_scan, inclusive_scan_by_key …
Sorting
  sort, stable_sort, sort_by_key …
20
NVIDIA [N. Bell]→
Notes: Thrust provides a large number of common parallel algorithms. Many of these algorithms have direct analogs in the STL, and when an equivalent STL function exists, we choose the name (e.g. thrust::sort and std::sort).
All algorithms in Thrust have implementations for both host and device. Specifically, when a Thrust algorithm is invoked with a host iterator, then the host path is dispatched. Similarly, a device implementation is called when a device iterator is used to define a range.
With the exception of thrust::copy, which can copy data between host and device, all iterator arguments to a Thrust algorithm should live in the same place: either all on the host or all on the device. When this requirement is violated the compiler will produce an error message.
15

## Slide 23
Thrust Example: Sort
20
#include <thrust/host_vector.h>
#include <thrust/device_vector.h>
#include <thrust/sort.h>
int main(void) {
// generate 16M random numbers on the host
thrust::host_vector<int> h_vec(1 << 24);
thrust::generate(h_vec.begin(), h_vec.end(), rand);
// transfer data to the device
thrust::device_vector<int> d_vec = h_vec;
// sort data on the device
thrust::sort(d_vec.begin(), d_vec.end());
// transfer data back to host
thrust::copy(d_vec.begin(), d_vec.end(), h_vec.begin());
return 0;
}
NVIDIA [N. Bell]→

## Slide 24
Leveraging Parallel Primitives, benchmark test
20
Test: sort 32M keys on each platform
  Performance measured in millions of keys per second [higher is better]
Conclusion: sort is highly optimized
data type | std::sort [per second] | tbb::parallel_sort [per second] | thrust::sort [per second]
char | 25.1 | 68.3 | 3532.2
short | 15.1 | 46.8 | 1741.6
int | 10.6 | 35.1 | 804.8
long | 10.3 | 34.5 | 291.4
float | 8.7 | 28.4 | 819.8
double | 8.5 | 28.2 | 358.9
Intel Core i7 950 @3.07 GHz
NVIDIA GeForce 480
NVIDIA [N. Bell]→
Notes: Sorting 32M keys on each platform - performance measured in millions of keys per second
CPU – Intel Core i7 950 @ 3.07 GHz
GPU – NVIDIA GeForce GTX 480
Lesson – use sorting instead of ad hoc binning b/c thrust::sort() is highly optimized
24

## Slide 25
Input-Sensitive Optimizations
24
Chart: Key Bits
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Series 1 | 2241.4 | 2241.5 | 2241.6 | 2241.1 | 2092.5 | 2087.5 | 2087.3 | 2091.7 | 1560.2 | 1559.7 | 1560.9 | 1560.6 | 1491.9 | 1490.5 | 1488.9 | 1486.8 | 1199.6 | 1194.3 | 1185.3 | 1168.5 | 1103.6 | 1087.2 | 1072.5 | 1068 | 897.36 | 881.66 | 879.43 | 874.66 | 857.41 | 852.99 | 847.62 | 844.18
NVIDIA [N. Bell]→
Notes: Sorting 32M unsigned integers (uniformly distributed) with different numbers of occupied key bits
For example, Key Bits = 20 means all keys are in the range [0, 2^20)
Reason: dispatched internally as a RADIX sort
25

## Slide 26
Example: Vector Addition
24
X
Y
Z
NVIDIA [N. Bell]→
for (int i = 0; i < N; i++)
Z[i] = X[i] + Y[i];
Notes: Transformations are algorithms that apply an operation to each element in a set of (zero or more) input ranges and then stores the result in a destination range.
The Thrust implementations rely on functors, which are function objects used to pass state and function objects, to perform transformation.
Let’s see how they come into play on a simple vector addition example
25

## Slide 27
#include <thrust/device_vector.h>
#include <thrust/transform.h>
#include <thrust/functional.h>
#include <iostream>
int main(void) {
thrust::device_vector<float> X(3);
thrust::device_vector<float> Y(3);
thrust::device_vector<float> Z(3);
X[0] = 10; X[1] = 20; X[2] = 30;
Y[0] = 15; Y[1] = 35; Y[2] = 10;
thrust::transform(X.begin(), X.end(),
Y.begin(),
Z.begin(),
thrust::plus<float>());
for (size_t i = 0; i < Z.size(); i++)
std::cout << "Z[" << i << "] = " << Z[i] << "\n";
return 0;
}
Example, Vector Addition
24
NVIDIA [N. Bell]→
Notes: Here, plus is a binary function defined in thrust/functional.h
25

## Slide 28
#include <thrust/device_vector.h>
#include <thrust/reduce.h>
#include <thrust/functional.h>
#include <iostream>
int main(void) {
thrust::device_vector<float> X(3);
X[0] = 10.f; X[1] = 30.f; X[2] = 20.f;
float init = X[0];
float result = thrust::reduce(X.begin(), X.end(),
init,
thrust::maximum<float>());
std::cout << "maximum is " << result << "\n";
return 0;
}
Maximum Value – after all, it’s just a reduce operation
24
NVIDIA [N. Bell]→
Notes: Functors can also be used with other types of algorithms, reduce in this case.
Here, maximum is a binary function defined in thrust/functional.h
25

## Slide 29
Algorithms
24
Standard operators
// allocate memory
device_vector<int> A(10);
device_vector<int> B(10);
device_vector<int> C(10);
// transform A + B -> C
transform(A.begin(), A.end(), B.begin(), C.begin(), plus<int>());
// transform A - B -> C
transform(A.begin(), A.end(), B.begin(), C.begin(), minus<int>());
// multiply reduction
int product = reduce(A.begin(), A.end(), 1, multiplies<int>());
NVIDIA [N. Bell]→
Notes: In previous examples, we have seen the use of various built-in functors (plus, maximum, etc).
Functors in thrust/functional.h cover most of the built-in arithmetic and comparison operations.
25

## Slide 30
Example: SAXPY (of sorts)
29
X
Y
Z
a
NVIDIA [N. Bell]→
for (int i = 0; i < N; i++)
Z[i] = a * X[i] + Y[i];
Notes: As an example of a custom functor for a “non-standard” operation, consider SAXPY
25

## Slide 31
SAXPY
29
struct saxpy
{
float m_a;
saxpy(float a) : m_a(a) {}
__host__ __device__
float operator()(float x, float y)
{
return m_a * x + y;
}
};
functor
call operator, callable from both host & device
constructor
state
NVIDIA [N. Bell]→
void main(void){
thrust::device_vector<float> X(3), Y(3), Z(3);
X[0] = 10; X[1] = 20; X[2] = 30;
Y[0] = 15; Y[1] = 35; Y[2] = 10;
float aVal = 2.0f;
thrust::transform(X.begin(), X.end(),
Y.begin(),
Z.begin(),
saxpy(aVal));
for (size_t i = 0; i < Z.size(); i++)
std::cout << "Z[" << i << "] = " << Z[i] << "\n";
}
This is the big deal on this slide…
Notes: If we want to implement SAXPY with Thrust we have a few options:
The first is to use two transformations (one addition and one multiplication) and a temporary vector filled with the value a.
A better choice is to use a single transformation with a user-defined functor that does exactly what we want.
31

## Slide 32
Functor, another example (negating all values in a vector)
29
struct negate_float2
{
__host__ __device__
float2 operator()(float2 a)
{
return make_float2(-a.x, -a.y);
}
};
// declare storage
device_vector<float2> input = ...
device_vector<float2> output = ...
// create function object or ‘functor’
negate_float2 fnctr;
// negate vectors
transform(input.begin(), input.end(), output.begin(), fnctr);
NVIDIA [N. Bell]→
Notes: When the built-in functors are not enough, you can define your own.
Here, note also that we are using a CUDA type (float2)
31

## Slide 33
Functor, another example yet: used for sorting
29
// compare x component of two float2 structures
struct compare_float2
{
__host__ __device__
bool operator()(float2 a, float2 b)
{
return a.x < b.x;
}
};
// declare storage
device_vector<float2> vec = ...
// create comparison functor
compare_float2 comp;
// sort elements by x component
sort(vec.begin(), vec.end(), comp);
NVIDIA [N. Bell]→
Notes: Custom functor objects are useful if:
Performing a “non-standard” operation (see SAXPY example later)
Working on “non-standard” data (e.g. float2)
This example uses a custom functor to define one possible definition of “less than” for a float2.
31

## Slide 34
Functor, another example: counting elements larger than threshold
34
// return true if x is greater than threshold
struct is_greater_than
{
int threshold;
is_greater_than(int t) { threshold = t; }
__host__ __device__
bool operator()(int x) { return x > threshold; }
};
device_vector<int> vec = ...
// create predicate functor (returns true for x > 10)
is_greater_than pred(10);
// count number of values > 10
int result = count_if(vec.begin(), vec.end(), pred);
NVIDIA [N. Bell]→
Notes: As mentioned before, functors can have state.
Note that this could be implemented more concisely as:
int result = thrust::count_if(vec.begin(), vec.end(), _1 > 10);
31

## Slide 35
Algorithms, More Examples…
34
Algorithm | Description
reduce | Sum of a sequence
find | First position of a value in a sequence
mismatch | First position where two sequences differ
inner_product | Dot product of two sequences
equal | Whether two sequences are equal
min_element | Position of the smallest value
count | Number of instances of a value
is_sorted | Whether sequence is in sorted order
transform_reduce | Reduction op following a transform op
NVIDIA [N. Bell]→
Notes: Searching, Copying, Reductions, Reorderings, Scans, Sorting, Transformations, Set Operations,…
31

## Slide 36
Work Plan, thrust
Namespaces, containers, iterators
Algorithms
General transformations. Zipping & fusing
Thrust example: Processing rainfall data
34

## Slide 37
General Transformations
34
for (int i = 0; i < N; i++)
X[i] = f(A[i]);
Unary Transformation
for (int i = 0; i < N; i++)
X[i] = f(A[i],B[i]);
Binary Transformation
for (int i = 0; i < N; i++)
X[i] = f(A[i],B[i],C[i]);
Ternary Transformation
for (int i = 0; i < N; i++)
X[i] = f(A[i],B[i],C[i],...);
General Transformation
NVIDIA [N. Bell]→
Like C++ STL, thrust provides built-in support for unary and binary transformations
Transformations involving 3 or more input ranges must use a different approach
Notes: 37

## Slide 38
The Zip Operation (“zipping”)
34
A0
A1
A2
X0
X1
X2
zip_iterator
Multiple
Distinct
Sequences
Unique
Sequence
of Tuples
NVIDIA [N. Bell]→
A0
A1
A2
X0
X1
X2
…
…
…

## Slide 39
void main(void) {
thrust::device_vector<float> X(3), Y(3), Z(3);
thrust::device_vector<float> U(3); // U = 2X + 3Y + 4Z
X[0] = 10; X[1] = 20; X[2] = 30;
Y[0] = 15; Y[1] = 35; Y[2] = 10;
Z[0] = 20; Z[1] = 30; Z[2] = 25;
thrust::transform
(thrust::make_zip_iterator(thrust::make_tuple(X.begin(), Y.begin(), Z.begin())),
thrust::make_zip_iterator(thrust::make_tuple(X.end(), Y.end(), Z.end())),
U.begin(),
linear_combo());
for (size_t i = 0; i < Z.size(); i++)
std::cout << "U[" << i << "] = " << U[i] << "\n";
}
#include <thrust/device_vector.h>
#include <thrust/transform.h>
#include <thrust/iterator/zip_iterator.h>
#include<iostream>
struct linear_combo {
__host__ __device__
float operator()(thrust::tuple<float,float,float> t) {
float x, y, z;
thrust::tie(x,y,z) = t;
return 2.0f * x + 3.0f * y + 4.0f * z;
}
};
Example: General Transformations
34
NVIDIA [N. Bell]→
Functor
Definition
These are the important parts: three different entities are zipped together into a big one

## Slide 40
Example: thrust::transform_reduce
40
#include <thrust/transform_reduce.h>
#include <thrust/device_vector.h>
#include <thrust/iterator/zip_iterator.h>
#include<iostream>
struct linear_combo {
__host__ __device__
float operator()(thrust::tuple<float,float,float> t) {
float x, y, z;
thrust::tie(x,y,z) = t;
return 2.0f * x + 3.0f * y + 4.0f * z;
}
};
void main(void) {
thrust::device_vector<float> X(3), Y(3), Z(3), U(3);
X[0] = 10; X[1] = 20; X[2] = 30;
Y[0] = 15; Y[1] = 35; Y[2] = 10;
Z[0] = 20; Z[1] = 30; Z[2] = 25;
thrust::plus<float> binary_op;
float init = 0.f;
float myResult = thrust::transform_reduce
(thrust::make_zip_iterator(thrust::make_tuple(X.begin(), Y.begin(), Z.begin())),
thrust::make_zip_iterator(thrust::make_tuple(X.end(), Y.end(), Z.end())),
linear_combo(),
init,
binary_op);
std::cout << myResult << std::endl;
}
The main point here:
Previous slide transform
This slide transform_reduce
Punch line: “fusing” operations together whenever possible is a good idea
Notes: Note: a tuple can have a max. number of 10 elements. Can use hierarchical tuples. Also, work on variadic template support (not sure if merged in main trunk).
37

## Slide 41
Performance Considerations [discussion tided to “fusing”]
41
SMs
DRAM
144 GB/s
1030 GFLOP/s
[Single Precision]
Tesla C2050 data
NVIDIA [N. Bell]→
Picture below shows the two key parameters in any computation
  Peak flop rate
  Max bandwidth
Punch line (for Tesla C2050):
  In one second I do 1030 GFLOPs. In one second, I can bring over 144 GB of data
  Therefore, on average, I need to do 1030/144 operations per byte of data; i.e., an average of 7.1 ops per byte
Notes: Zip operators: take care of reorganizing data for thrust use.
We will talk next about fusing operations: take care of reorganizing computations for thrust use.
Your problem at hand can hit one of two bounds: the FLOP bound or the BANDWIDTH bound (compute-bound, memory-bound)
41

## Slide 42
Arithmetic Intensity [discussion tided to “fusing”]
42
Kernel | FLOP/Byte*
Vector Addition | 1 : 12
SAXPY | 2 : 12
Max Index | 1 : 12
Reduce | 1 : 4
Ternary Transformation | 5 : 16
* excludes indexing overhead
Hardware** | FLOP/Byte
GeForce GTX 280 | ~7.0 : 1
GeForce GTX 480 | ~7.6 : 1
Tesla C870 | ~6.7 : 1
Tesla C1060 | ~9.1 : 1
Tesla C2050 | ~7.1 : 1
NVIDIA [N. Bell]→
“Byte” refers to a Global Memory byte
** lists the number of flop per byte of data to reach peak Flop/s rate
Ternary Transformation:
Notes: Max index: compare two, and possibly store an index – therefore, you handle three entities.
More precisely: you bring an index, the associated value. If the new index “wins”, then you store it in memory.
Compare how far the arithmetic intensities are from the values that would leverage the hardware. On a GTX480 you should be able to perform 8 operations for each byte you bring over.
Ternary: w[i] = \alpha x[i] + \beta y[i] + \gamma z[i]
41

## Slide 43
Arithmetic Intensity [discussion tided to “fusing”]
43
FLOP/Byte
Memory bound
Compute bound
SAXPY
FFT
SGEMM
NVIDIA [N. Bell]→

## Slide 44
Fusing, as a strategy to increase the arithmetic intensity
43
for (int i = 0; i < N; i++)
U[i] = F(X[i],Y[i],Z[i]);
for (int i = 0; i < N; i++)
V[i] = G(X[i],Y[i],Z[i]);
for (int i = 0; i < N; i++)
{
U[i] = F(X[i],Y[i],Z[i]);
V[i] = G(X[i],Y[i],Z[i]);
}
Loop Fusion
NVIDIA [N. Bell]→
One way to look at things…
  Zipping: reorganizes data for thrust processing
  Fusing: reorganizes computation for efficient thrust processing
Notes: So what can we do to maximize the work we do for the same amount of data transferred?
Simple idea… But powerful
41

## Slide 45
typedef thrust::tuple<float,float> Tuple2;
typedef thrust::tuple<float,float,float> Tuple3;
struct linear_combo {
__host__ __device__
Tuple2 operator()(Tuple3 t) {
float x, y, z; thrust::tie(x,y,z) = t;
float u = 2.0f * x + 3.0f * y + 4.0f * z;
float v = 1.0f * x + 2.0f * y + 3.0f * z;
return Tuple2(u,v);
}
};
void main(void) {
thrust::device_vector<float> X(3), Y(3), Z(3);
thrust::device_vector<float> U(3), V(3);
X[0] = 10; X[1] = 20; X[2] = 30;
Y[0] = 15; Y[1] = 35; Y[2] = 10;
Z[0] = 20; Z[1] = 30; Z[2] = 25;
thrust::transform
(thrust::make_zip_iterator(thrust::make_tuple(X.begin(), Y.begin(), Z.begin())),
thrust::make_zip_iterator(thrust::make_tuple(X.end(), Y.end(), Z.end())),
thrust::make_zip_iterator(thrust::make_tuple(U.begin(), V.begin())),
linear_combo());
}
Fusing Transformations
43
NVIDIA [N. Bell]→
Functor
Definition
Notes: Zip iterator: bring data together
Fusing operations: bring operations together
41

## Slide 46
Fusing Transformations in Previous Example
43
Original Implementation
Optimized Implementation
GPU
DRAM
12 Bytes
8 Bytes
GPU
DRAM
12 Bytes
4 Bytes
12 Bytes
4 Bytes
NVIDIA [N. Bell]→
Since the operation is completely memory bound the expected speedup is ~1.6x (=32/20)
Notes: What does this fusing get us?
Since the operation is completely memory bound the expected speedup is ~1.6x (=32/20)
46

## Slide 47
Fusing Transformations
43
for (int i = 0; i < N; i++)
Y[i] = F(X[i]);
for (int i = 0; i < N; i++)
sum += Y[i];
for (int i = 0; i < N; i++)
sum += F(X[i]);
Loop Fusion
NVIDIA [N. Bell]→
Notes: Another example of loop fusion
46

## Slide 48
#include <thrust/device_vector.h>
#include <thrust/transform_reduce.h>
#include <thrust/functional.h>
#include <iostream>
using namespace thrust::placeholders;
int main(void) {
thrust::device_vector<float> X(3);
X[0] = 10; X[1] = 30; X[2] = 20;
float result = thrust::transform_reduce
(X.begin(), X.end(),
_1 * _1,
0.0f,
thrust::plus<float>());
std::cout << "sum of squares is " << result << "\n";
return 0;
}
Fusing Transformations
48
NVIDIA [N. Bell]→
Notes: Calculate sum of squares.
Note a different way of specifying the binary operation
46

## Slide 49
Fusing Transformations in Previous Example
49
Original Implementation
Optimized Implementation
GPU
DRAM
4 Bytes
4 Bytes
GPU
DRAM
4 Bytes
4 Bytes
NVIDIA [N. Bell]→
Try to answer this: how many times will we be able to run faster if we fuse?
Notes: Since the operation is completely memory bound the expected speedup is ~3x (=12/4)
The numbers of bytes are showing what happens for each i, from i=1 to 3 (or lengths of array)
49

## Slide 50
thrust Wrap-Up
49
Good productivity and execution boost at the price of having to deal with C++ syntax
  No need to be aware of execution configuration, shared memory, etc.
Key concepts
  Functor
  Zipping data
  Fusing operations
Why not always use thrust?
  There is no “perform finite element analysis” support in thrust
  Thrust provides support for primitives – up to us to use them as needed

## Slide 51
thrust on GitHub
49
Quick Start Guide
Examples
News
Documentation
Mailing List (thrust-users)
NVIDIA [N. Bell]→
http://thrust.github.io/
Notes: 51

## Slide 52
thrust in “GPU Computing Gems”
49
PDF available at http://goo.gl/adj9S
NVIDIA [N. Bell]→

## Slide 53
Work Plan, thrust
Namespaces, containers, iterators
Algorithms
General transformations. Zipping & fusing
Thrust example: Processing rainfall data
49

## Slide 54
Example, thrust: Processing Rainfall Data
49
0
1
2
3
4
day [0 0 1 2 5 5 6 6 7 8 ... ]
site [2 3 0 1 1 2 0 1 2 1 ... ]
measurement [9 5 6 3 3 8 2 6 5 9 ... ]
Remarks:
Time series sorted by day
Measurements of zero are excluded from the time series
2
3
NVIDIA [N. Bell]→
Rain situation, end of first day, for a set of five observation stations. Results, summarized over a period of time, reported in the table below.

## Slide 55
Example: Processing Rainfall Data
49
Given the data above, here’re some questions you might ask:
  Total rainfall at a given site
  Total rainfall between given days
  Total rainfall on each day
  Number of days with any rainfall
NVIDIA [N. Bell]→
day [0 0 1 2 5 5 6 6 7 8 ... ]
site [2 3 0 1 1 2 0 1 2 1 ... ]
measurement [9 5 6 3 3 8 2 6 5 9 ... ]

## Slide 56
Total Rainfall at a Given Site
49
NVIDIA [N. Bell]→
struct one_site_measurement
{
int siteOfInterest;
one_site_measurement(int site) : siteOfInterest(site) {}
__host__ __device__
int operator()(thrust::tuple<int,int> t)
{
if (thrust::get<0>(t) == siteOfInterest)
return thrust::get<1>(t);
else
return 0;
}
};
template <typename Vector>
int compute_total_rainfall_at_one_site(int siteID, const Vector& site, const Vector& measurement)
{
return thrust::transform_reduce
(thrust::make_zip_iterator(thrust::make_tuple(site.begin(), measurement.begin())),
thrust::make_zip_iterator(thrust::make_tuple(site.end(), measurement.end())),
one_site_measurement(siteID),
0,
thrust::plus<int>());
}
Functor
Definition
Notes: transform_reduce fuses the transform and reduce operations. transform_reduce is equivalent to performing a transformation defined by unary_op into a temporary sequence and then performing reduce on the transformed sequence. In most cases, fusing these two operations together is more efficient, since fewer memory reads and writes are required.
transform_reduce performs a reduction on the transformation of the sequence [first, last) according to unary_op. Specifically, unary_op is applied to each element of the sequence and then the result is reduced to a single value with binary_op using the initial value init. Note that the transformation unary_op is not applied to the initial value init. The order of reduction is not specified, so binary_op must be both commutative and associative.
<number>

## Slide 57
Total Rainfall Between Given Days
49
day [0 0 1 2 5 5 6 6 7 8 ... ]
measurement [9 5 6 3 3 8 2 6 5 9 ... ]
lower_bound( ... , 2)
upper_bound( ... , 6)
NVIDIA [N. Bell]→
template <typename Vector>
int compute_total_rainfall_between_days(int first_day, int last_day,
const Vector& day, const Vector& measurement)
{
int first = thrust::lower_bound(day.begin(), day.end(), first_day) - day.begin();
int last = thrust::upper_bound(day.begin(), day.end(), last_day) - day.begin();
return thrust::reduce(measurement.begin() + first, measurement.begin() + last);
}
#include <thrust/device_vector.h>
#include <thrust/binary_search.h>
#include <thrust/transform.h>
#include <thrust/iterator/zip_iterator.h>
#include <iostream>
You will need to include several header files (not all for the code snippet above)
Notes: reduce is a generalization of summation: it computes the sum (or some other binary operation) of all the elements in the range [first, last). This version of reduce uses 0 as the initial value of the reduction. reduce is similar to the C++ Standard Template Library's std::accumulate. The primary difference between the two functions is that std::accumulate guarantees the order of summation, while reduce requires associativity of the binary operation to parallelize the reduction.
Note that reduce also assumes that the binary reduction operator (in this case operator+) is commutative. If the reduction operator is not commutative then thrust::reduce should not be used. Instead, one could use inclusive_scan (which does not require commutativity) and select the last element of the output array.
<number>

## Slide 58
Number of Days with Any Rainfall
49
day [0 0 1 2 5 5 6 6 7 8 ... ]
1 [0 1 1 1 0 1 0 1 1 ... ]
NVIDIA [N. Bell]→
template <typename Vector>
int compute_number_of_days_with_rainfall(const Vector& day)
{
return thrust::inner_product(day.begin(), day.end() - 1,
day.begin() + 1,
0,
thrust::plus<int>(),
thrust::not_equal_to<int>()) + 1;
}
Notes: inner_product calculates an inner product of the ranges [first1, last1) and [first2, first2 + (last1 - first1)).
This version of inner_product is identical to the first, except that is uses two user-supplied function objects instead of operator+ and operator*.
Specifically, this version of inner_product computes the sum binary_op1( init, binary_op2(*first1, *first2) ), ...
Unlike the C++ Standard Template Library function std::inner_product, this version offers no guarantee on order of execution.
<number>

## Slide 59
Total Rainfall on Each Day
49
day [0 0 1 2 5 5 6 6 7 8 ... ]
measurement [9 5 6 3 3 8 2 6 5 9 ... ]
day_output [0 1 2 5 6 7 8 ... ]
measurement_output [14 6 3 11 8 5 10 ... ]
NVIDIA [N. Bell]→
template <typename Vector>
void compute_total_rainfall_per_day(const Vector& day, const Vector& measurement,
Vector& day_output, Vector& measurement_output)
{
size_t N = compute_number_of_days_with_rainfall(day); //see previous slide
day_output.resize(N);
measurement_output.resize(N);
thrust::reduce_by_key(day.begin(), day.end(),
measurement.begin(),
day_output.begin(),
measurement_output.begin());
}
Notes: reduce_by_key is a generalization of reduce to key-value pairs. For each group of consecutive keys in the range [keys_first, keys_last) that are equal, reduce_by_keycopies the first element of the group to the keys_output. The corresponding values in the range are reduced using the plus and the result copied to values_output.
This version of reduce_by_key uses the function object equal_to to test for equality and plus to reduce values with equal keys.
<number>

## Slide 60
GPU Computing with CUB
49

## Slide 61
Hi, my name is CUB!
People know me as CUB, but my real name is “CUDA UnBound”
Currently, I’m at version V1.8.0 (DOB: 02/16/2018)
I’m developed as open-source project by good folks at NVIDIA Research
  Primary contributor: Duane Merrill
You can fork/clone me if you want (on GitHub: https://github.com/nvidia/cub)
Something about me: I can run really, really fast… Usain Bolt fast. Perhaps even better.
49

## Slide 62
CUB, factoids
CUB provides software components at each layer of the CUDA programming model
Like thrust, it’s a headers library, not one library that you link against
Implications, given that it’s a header-file library:
  When you need to call a function, you need to include the header file that includes the *source* code of the CUB function you want to call
  Rationale, header-file library: if the compiler sees the code, it can engage in all sort of optimizations
    Inlining, compiles for the exact architecture you have, etc.
  Fallout: it takes a little bit longer to compile
49
[NVIDIA]

## Slide 63
Straight from CUB webpage
Device-wide primitives
  Sort, prefix scan, reduction, histogram, etc.
Block-wide “collective” primitives
  I/O, sort, prefix scan, reduction, histogram, etc.
Warp-wide “collective” primitives
  Warp-wide prefix scan, reduction, etc.
Thread and resource utilities
  PTX intrinsics, device reflection, texture-caching iterators, caching memory allocators, etc.
63
[NVIDIA]

## Slide 64
CUB ruminations
The device-wide support is not a novelty, thrust does it too…
  thrust built on top of CUB, by the way
The novelty:
  You can call CUB from a kernel function that uses the threads in one block to accomplish something
  You can call CUB from a kernel function that uses the threads in a warp to accomplish something
    The threads in a warp start behaving like the 32 threads of a chip with 32 cores running 32 threads
64

## Slide 65
Reiterating what CUB does [slide hyperlinks should work…]
Parallel primitives
  Warp-wide "collective" primitives
    Cooperative warp-wide prefix scan, reduction, etc.
    Safely specialized for each underlying CUDA architecture
  Block-wide "collective" primitives
    Cooperative I/O, sort, scan, reduction, histogram, etc.
    Compatible with arbitrary thread block sizes and types
  Device-wide primitives
    Parallel sort, prefix scan, reduction, histogram, etc.
    Compatible with CUDA dynamic parallelism
Utilities
  Fancy iterators
  Thread and thread block I/O
  PTX intrinsics
  Device, kernel, and storage management
65
[NVIDIA]

## Slide 66
CUB, device-wide operations
You can call these from you C host code:
  Histogram
  Partition
Reduce
Run length encode
Scan
Select
65
[NVIDIA]

## Slide 67
CUB, block-wide operations [callable from a kernel function]
BlockDiscontinuity class provides collective methods for flagging discontinuities within an ordered set of items partitioned across a CUDA thread block
BlockExchange class provides collective methods for rearranging data partitioned across a CUDA thread block
BlockHistogram
BlockLoad
BlockRadixSort class provides collective methods for sorting items partitioned across a CUDA thread block using a radix sorting method
BlockReduce
BlockScan
BlockStore class provides collective data movement methods for writing a blocked arrangement of items partitioned across a CUDA thread block to a linear segment of memory
67
[NVIDIA]

## Slide 68
Example, back of the envelope, for BlockDiscontinuity
67
[https://nvlabs.github.io/cub/classcub_1_1_block_discontinuity.html]
#include <cub/cub.cuh>
__global__ void ExampleKernel(...)
{
// Specialize BlockDiscontinuity for a 1D block of 128 threads on type int
typedef cub::BlockDiscontinuity<int, 128> BlockDiscontinuity;
// Allocate shared memory for BlockDiscontinuity
__shared__ typename BlockDiscontinuity::TempStorage temp_storage;
// Obtain a segment of consecutive items that are blocked across threads
int thread_data[4];
...
// Collectively compute head flags for discontinuities in the segment
int head_flags[4];
BlockDiscontinuity(temp_storage).FlagHeads(head_flags, thread_data, cub::Inequality());
First important actor
Second important actor

## Slide 69
CUB, warp-level primitives
Idea: each warp of threads will work on a chunk of an array and do a scan or reduce on that chunk of the array
WarpScan class provides collective methods for computing a parallel prefix scan of items partitioned across a CUDA thread warp.
WarpReduce class provides collective methods for computing a parallel reduction of items partitioned across a CUDA thread warp.
69
[NVIDIA]

## Slide 70
Example, CUB: sort by key, device-level operation
69
#define CUB_STDERR // print CUDA runtime errors to console
#include <cub/util_allocator.cuh>
#include <cub/device/device_radix_sort.cuh>
#include "test/test_util.h"
using namespace cub;
// Caching allocator for device memory
CachingDeviceAllocator g_allocator(true);
struct pairsOfBodies {
unsigned int body_I;
unsigned int body_J;
};
int main() {
const unsigned int num_items = 8;
// host side setup
pairsOfBodies h_vals[num_items];
unsigned int h_keys[num_items] = { 2 , 0, 7, 3, 5, 4, 1, 6 };
pairsOfBodies h_vals_out[num_items];
unsigned int h_keys_out[num_items];
h_vals[0].body_I = 3; h_vals[0].body_J = 0;
h_vals[1].body_I = 9; h_vals[1].body_J = 2;
h_vals[2].body_I = 0; h_vals[2].body_J = 9;
h_vals[3].body_I = 2; h_vals[3].body_J = 4;
h_vals[4].body_I = 1; h_vals[4].body_J = 5;
h_vals[5].body_I = 1; h_vals[5].body_J = 7;
h_vals[6].body_I = 2; h_vals[6].body_J = 9;
h_vals[7].body_I = 6; h_vals[7].body_J = 8;
// device side setup
unsigned int* d_keysIN = NULL;
unsigned int* d_keysOUT = NULL;
pairsOfBodies* d_valsIN = NULL;
pairsOfBodies* d_valsOUT = NULL;
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_keysIN, sizeof(unsigned int) * num_items));
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_keysOUT, sizeof(unsigned int) * num_items));
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_valsIN, sizeof(pairsOfBodies) * num_items));
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_valsOUT, sizeof(pairsOfBodies) * num_items));
// get memory set aside on the device
size_t temp_storage_bytes = 0;
void* d_temp_storage = NULL;
CubDebugExit(DeviceRadixSort::SortPairs(d_temp_storage, temp_storage_bytes, d_keysIN, d_keysOUT, d_valsIN, d_valsOUT, num_items)); // Caching allocator for device memory
CubDebugExit(g_allocator.DeviceAllocate(&d_temp_storage, temp_storage_bytes));
// initialize data on the device
CubDebugExit(cudaMemcpy(d_keysIN, h_keys, sizeof(unsigned int) * num_items, cudaMemcpyHostToDevice));
CubDebugExit(cudaMemcpy(d_valsIN, h_vals, sizeof(pairsOfBodies) * num_items, cudaMemcpyHostToDevice));
// do the actual sort
CubDebugExit(DeviceRadixSort::SortPairs(d_temp_storage, temp_storage_bytes, d_keysIN, d_keysOUT, d_valsIN, d_valsOUT, num_items));
// get data back
CubDebugExit(cudaMemcpy(h_keys_out, d_keysOUT, sizeof(unsigned int) * num_items, cudaMemcpyDeviceToHost));
CubDebugExit(cudaMemcpy(h_vals_out, d_valsOUT, sizeof(pairsOfBodies) * num_items, cudaMemcpyDeviceToHost));
// clean up
if (d_keysIN) CubDebugExit(g_allocator.DeviceFree(d_keysIN));
if (d_keysOUT) CubDebugExit(g_allocator.DeviceFree(d_keysOUT));
if (d_valsIN) CubDebugExit(g_allocator.DeviceFree(d_valsIN));
if (d_valsOUT) CubDebugExit(g_allocator.DeviceFree(d_valsOUT));
if (d_temp_storage) CubDebugExit(g_allocator.DeviceFree(d_temp_storage));
return 0;
}

## Slide 71
Example, CUB: reduce, device-level operation
69
#define CUB_STDERR // print CUDA runtime errors to console
#include <stdio.h>
#include <cub/util_allocator.cuh>
#include <cub/device/device_reduce.cuh>
#include "test/test_util.h"
using namespace cub;
CachingDeviceAllocator g_allocator(true); // Caching allocator for device memory
int main() {
const size_t num_items = 10;
// Set up host arrays
int h_in[num_items] = { 2, 3, -1, 0, 3, 6, 7, 2, -2, 0 };
int sum = 0;
for (unsigned int i = 0; i < num_items; i++)
sum += h_in[i];
// Set up device arrays
int* d_in = NULL;
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_in, sizeof(int) * num_items));
// Initialize device input
CubDebugExit(cudaMemcpy(d_in, h_in, sizeof(int) * num_items, cudaMemcpyHostToDevice));
// Setup device output array
int* d_sum = NULL;
CubDebugExit(g_allocator.DeviceAllocate((void**)& d_sum, sizeof(int) * 1));
// Request and allocate temporary storage
void* d_temp_storage = NULL;
size_t temp_storage_bytes = 0;
CubDebugExit(DeviceReduce::Sum(d_temp_storage, temp_storage_bytes, d_in, d_sum, num_items));
CubDebugExit(g_allocator.DeviceAllocate(&d_temp_storage, temp_storage_bytes));
// Do the actual reduce operation
CubDebugExit(DeviceReduce::Sum(d_temp_storage, temp_storage_bytes, d_in, d_sum, num_items));
int gpu_sum;
CubDebugExit(cudaMemcpy(&gpu_sum, d_sum, sizeof(int) * 1, cudaMemcpyDeviceToHost));
// Check for correctness
printf("\t%s\n", (gpu_sum == sum ? "Test passed." : "Test falied."));
printf("\tSum is: %d\n", gpu_sum);
// Cleanup
if (d_in) CubDebugExit(g_allocator.DeviceFree(d_in));
if (d_sum) CubDebugExit(g_allocator.DeviceFree(d_sum));
if (d_temp_storage) CubDebugExit(g_allocator.DeviceFree(d_temp_storage));
return 0;
}

## Slide 72
CUB, departing thoughts
CUB is not the friendliest library to use, and the documentation is both dense and limited
CUB provides amazing performance
thrust is implemented in terms of CUB
Use it when you start processing big data
69